## Slide 1: EE 152 – Real-time embedded systems
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lab 2 prep

## Slide 2: Lab 2 prep
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details
  FreeRTOS debug instrumentation

## Slide 3: Operating systems
Our first in-your-face issue with embedded systems: no keyboard or monitor
Our second one: “what about the O/S?”
Who can roughly define the term “operating system?” Name a few desktop or phone O/S?
Which do you think run on most embedded systems?
  Often none!
  Huh? But an O/S is kind of useful, isn’t it?
Notes: A few popular O/Ss: Linux, Unix, Windows, IOS, Android, …

## Slide 4: What does an O/S really do?
Who remembers what kinds of things an O/S does?
  manage multiple users/threads. Tricks them into each thinking they own the machine
  files; paging/VM
  attach your keyboard/screen to a window(s)

## Slide 5
What an O/S does
  manage multiple users/threads Tricks them into each thinking they own the machine
  files; paging/VM
  attach your keyboard/screen to a window(s)
Which of those functions do we need on the Nucleo?
Do we really need an O/S?

## Slide 6: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 7: Bare metal
Cross-compile on the host  ARM binary
Download binary  Nucleo flash
Disconnect the board
Ship to customer. Turn it on  runs from flash
Host
USB
Bare metal is ≈ 26% market share
  it means no O/S at all!

## Slide 8: Bare metal
Bare metal = board boots to your program
What do you think are pros and cons?
  An O/S takes up flash space, so no O/S is cheap
  Files are useful (but our program can write/read flash)
  Multiple threads may be useful (more on that later)
  We have no “boot to a shell, where you can run any program you want” – but our embedded system only runs one program, anyway

## Slide 9: Linux?
What about Linux (or Windows)?
  Mainstream Linux needs 10GB hard drive and virtual memory
  STM32L432 has 256KB on-die flash
  Microcontrollers rarely support virtual memory
  So no mainstream Linux (or Windows!)
  “Tiny” versions can be down to 500KB
Notes: So even a tiny Linux won’t fit our flash. And we’ll do a comparison to FreeRTOS soon – which takes only about 7KB.

## Slide 10: Virtual memory
Virtual memory lets two users use the same hardware
Compile your C program
    extern a = 5
    a = a + 1
Compiler gives you, e.g.,
    mem[1000] = mem[1000] + 1
What if two users run this program at the same time?
  Do they each see a wind up as 7?
  How about three users?
It actually works fine – because of virtual memory
Notes: OK, most assembly languages won’t let you add 1 directory to memory. But I’m just keeping it simple

## Slide 11: Virtual memory
Virtual memory maps
address in your program
your user ID
actual address
Memory manager
virtual address | user # | physical address
1000 | 0 | 10000
1000 | 1 | 20000
1000 | 2 | 30000
Can’t really do a multi-user system without VM
Most microcontrollers don’t support VM
Notes: In fact, some might say that the definition of a microcontroller (as opposed to a microprocessor) is that it doesn’t support VM

## Slide 12: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 13: RTOS
RTOS = Real-time O/S
The most popular one is called FreeRTOS
Any guesses why it’s the most popular? 
  Open source
  “Owned” by Amazon Web Services
  Can pay for support, and for FDA-friendly version

## Slide 14: RTOS
Pared-down bare-bones O/S
  No file system, VM  about 7KB!
  FreeRTOS gives you threads + inter-thread comms
  gives you alloc(), free() (but see later…)
  gives you real-time “guarantees”
Why do we care about threads?
  About ¼ of projects are bare metal and ¾ are RTOS
  Multiple threads are good (labs will show us why)
  Lets you put different functionality in different threads, making your code more modular

## Slide 15: RTOS superpower
RTOS can work in real time
Why does this matter? What embedded systems might need real-time response?
  Pacemaker, neural prosthetic, anti-lock brakes, …
A few definitions
  soft RTOS  almost always meet a deadline
  hard RTOS  meet a deadline deterministically
Notes: What does “deterministic” mean in this context? You yourself can write bad code that results in deadlines not being met. But at least the RTOS is deterministic, and good code on your part can work. The main thing that would cause an RTOS to not be deterministic is garbage collection.

## Slide 16
Slightly interesting opinions
https://www.embedded.com/are-all-rtoses-equivalent
https://www.embedded.com/why-a-bare-metal-developer-moved-to-operating-systems
https://www.embedded.com/how-to-select-your-embedded-systems-operating-system-selection-guidelines

## Slide 17: So many infrastructures…
How many embedded-programming environments can you think of?
  Arduino, Raspberry Pi, MicroPython, CircuitPython
  STM CMSIS, LL, HAL
  Infineon PDL, HAL
  C vs. C++ vs. assembly
Remember this?
Which of these counts as an O/S?
Notes: Hopefully this is an easy question to answer

## Slide 18: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 19: Tour of FreeRTOS
Next up: enough FreeRTOS details to get you through labs #2, #3

## Slide 20: FreeRTOS tasks
Concept #1: tasks
A task is (roughly)
  the basic thing that runs in FreeRTOS
  what the scheduler schedules
  others call it a thread (or, wrongly, a process)
Three tasks in lab #2
  green LED blinker
  red LED blinker
  UART
Any guess what the green-LED-blinker task does?

## Slide 21: UART
UART = Universal Asynchronous Receiver and Transmitter
Host
USB
serial to USB
UART in 432
1B parallel
1b series
UART
Notes: UART takes 1B all at once and ships out 1b at a time (or vice versa).
USB changes from the simple UART format to the very complex USB format.
There’s a host-side USB chip too.

## Slide 22: UART for output
We write 1B to the UART
  it sends out 1b at a time to Nucleo USB
  Nucleo USB sends out 1b at a time to host USB
  serial term (Moba or other) on host prints
Nucleo
serial to USB
432
UART
Look at serial_write() and UART_write_byte() in lib_UART.c
  they takes multiple bytes and do spin-waits

## Slide 23: UART for input
Host terminal waits for keyboard input (one char)
Sends one char over USB to Nucleo
Nucleo USB chip receives 1B, serializes it
UART on 432 reassembles it as 1B
Look at USART_read()
  mostly just a big spin-wait loop
  can wait a long time for a keystroke!

## Slide 24: FreeRTOS and UARTs
Why are we talking about UARTs in the FreeRTOS slides?
Sending text to a screen helps us debug
  the sooner we learn that the better!
More tasks equals more fun on lab 2 
  UART will be a third task
Lots of spin waits in UART drivers
  FreeRTOS can help us multitask while we wait

## Slide 25: Create a FreeRTOS task
TaskHandle_t task_handle_red = NULL;
BaseType_t red_status = xTaskCreate (
      task_blink_red, // name of the task function
      "Blink Red LED", // for debugging
      100, // stack size in words
      NULL, // parameter passed into task
      tskIDLE_PRIORITY, // priority
      &task_handle_red);
if (red_status != pdPASS) …
Notes: The task handle is typically unused, but could be used to edit the task properties.

## Slide 26: More “what is a task?”
We haven’t really said exactly what a task is yet!
  We said “tasks are the things FreeRTOS schedules”
FreeRTOS makes it look like all these tasks are happening at the same time
  Of course they’re not
  We only have one core; only one thing can run at a time
  But we switch back-and-forth really fast

## Slide 27: Multitasking & the scheduler
Any examples of multi-tasking in your daily life?
  Daydreaming while listening to a boring lecture?
  Listening to music while studying?
Every multi-user OS does that
  A real time OS gives us more control on the switching
  Let’s talk about how that works
Notes: I can’t really listen to music and concentrate any more… not even when driving

## Slide 28: Scheduler in a nutshell
The heart of an RTOS is a scheduler
The scheduler…
  has a list of all tasks that want to run
  picks the highest priority one
What if there are several tasks ready to run at the same priority?
  Take turns (round robin)
xTaskCreate (task_blink_red, …,
      tskIDLE_PRIORITY,
      …);

## Slide 29: Can FreeRTOS hang?
Problem: who runs the scheduler?
  Is it that a task runs the scheduler when it wants to play nice & share the MCU?
If one task wants to run and run and run, and never calls the scheduler, will it succeed?
Will other tasks never execute?

## Slide 30: Who runs the scheduler
That scenario cannot happen
Two ways the scheduler gets control
  FreeRTOS has a tick (1ms for us). Hardware timer ticks every 1ms; interrupts whoever is running and runs the scheduler instead. The scheduler then does its thing to pick who goes next
  A task says I’m stuck until (say) 10ms from now. E.g., vTaskDelay(10)  pause me for 10 ticks
  Note it’s in ticks (and for us, 1 tick = 1ms)

## Slide 31: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Blinky starts running (it’s the high-priority task)
  Flips the GPIO pin
  Calls vTaskDelay(2) long before tick #1 occurs
  Will sleep 2 ticks (so, until tick #2)
0 1 2 3 4
Notes: Because we switch to the scheduler with an interrupt, we can return to the interrupted task. It takes a bit of doing (since usually we unroll the stack in LIFO order and the scheduler can instead do what it wants).
Also be sure to show the difference between preemption and cooperation.

## Slide 32: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

vTaskDelay(2) calls the scheduler
Control passes to , which computes happily along
0 1 2 3 4

## Slide 33: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Next tick interrupt happens (tick #1)
Blinky is blocked until tick #2, so  can keep running
0 1 2 3 4

## Slide 34: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Next tick interrupt happens (tick #2)
Blinky is now unblocked
 is pre-empted, Blinky runs again
0 1 2 3 4

## Slide 35: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Blinky flips the GPIO pins
Blinky calls VTaskDelay(2), sleeps until tick #4
VTaskDelay(2) calls scheduler, returns control to 
0 1 2 3 4

## Slide 36: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

And the beat goes on…
0 1 2 3 4

## Slide 37: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Every tick, the scheduler picks the highest-priority unblocked task
Calls to vTaskDelay() and other FreeRTOS kernel functions can re-schedule mid-tick
0 1 2 3 4

## Slide 38: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Thought questions: how would this diagram have changed if Blinky and  had equal priority?
0 1 2 3 4

## Slide 39: RTOS vs Linux
The whole point of an RTOS
  you pick the timer tick
  you assign priorities
  (you pick the heap algorithm)
Result: you can guarantee mission-critical tasks happen on time
Do ps on a Linux system; so many weird tasks!

## Slide 40: Ready for lab #2!

## Slide 41: Instrumentation
I think I got the last few slides right 
But how do you debug this stuff? Processes are switching at 1000 times/second
FreeRTOS allows you to instrument the scheduler
  FreeRTOS manual section 11.6, Trace Hook Macros
  https://www.freertos.org/rtos-trace-macros.html

## Slide 42: How to use instrumentation
Trace-hook macros get called at, e.g.,
  every tick interrupt
  every task switch
  lots of other point if you want
You have to get that information from the code to your eyes
  Macros can toggle GPIO or change DAC voltages
  Macros can build data structures you look at later

## Slide 43: Blinky- demo
Class exercise: look at the code & the output: does it make sense, and are the last few slides correct?
FreeRTOSconfig.h (at the end of the file)
  declares array g_debug_notes[] to save real-time debug info for printing later
  defines trace hook macros so task switch & tick interrupt save info into g_debug_notes
  configUSE_APPLICATION_TASK_TAG lets us put a small integer into each task as its “note”
demo_blinky_pi_main.c
  allocates g_debug_notes[]
  after  is computed, prints them out

## Slide 44: Problem of the day
How do two units talk to each other reliably without needing a ton of wires?

## Slide 45: Keep it simple
Simplest method: one wire, on/off
Transmitter
LED
one wire
Assume you receive 1s on, 1s ff, 1s on. Is that binary 101?
  Hard to say without a clock
  It could also be 110011 or 111000111
Having a clock is really useful!

## Slide 46: Add a clock
Transmitter
data clk
Lecture done?
  UART gets away with one wire, not two!
  Transmits 8-bit data, not one bit
  We’ll learn a bit about I2C, SPI too
Receiver
clk
data
1
1
0
0
1
1

## Slide 47: 8-bit wide data
This would be one way to implement 8 bits of data
  but it’s not what UART does
Transmitter
clk
data0
data1
data2
…
data7
Receiver

## Slide 48: Shift register
Parallel-in, serial-out shift register
  Lives inside the transmitter
  And the receiver has a serial-in, parallel-out version
D Q
CK
P3
P2
P1
ser_out
clk
D Q
CK
D Q
CK
D Q
CK
P0

## Slide 49: The problems
We want 8-bit data but only use one data wire
  Parallel-to-serial shift register in the transmitter, serial-to-parallel in the receiver
  What did we trade away to get this?
Transmitter
data clk
Receiver
clk
data
1
1
0
0
1
1
USRT

## Slide 50: Getting rid of the clock wire
Can we remove the clock wire?
  Yes, UART does it. But how?
Tx and Rx must agree on the data speed
  e.g., 9600 baud = 9600 bits/second
  Is that good enough?
Transmitter
data clk
Receiver
USRT
Notes: That’s not good enough. The two frequencies will always drift apart.

## Slide 51: Clock drift
Works fine if Tx and Rx clocks are identical
  But they’re never quite the same frequency
  Or quite perfectly aligned, even at the same freq
How do we build a practical UART?
1
1
0
0
1
1
Tx clk
data
Rx clk

## Slide 52: Start and stop bits
Every packet has
  start bit = 0
  5-8 data bits
  optional parity bit
  stop bit = 1
Stop + start = guaranteed rising data transitions at known locations
  Rx clock continually adjusts itself!
  any downside to this scheme?
Notes: The downside is we need two extra bits for each packet, and extra complexity in the Rx clock generation.

## Slide 53: UARTs in the Nucleo board
USART1 Tx=PA9, PB6; Rx=PA10, PB7
  Choose via CSR programming
432
USART2
USART1
ST-LINK
Tx
Rx
Tx Rx Clk
USB to host

## Slide 54: Ready for lab #3!

## Slide 55: SPI
Similar to synchronous UART
  Clk wire is required, driven by the “master”
  Full-duplex transmission via MISO and MOSI
Bonus
  Supports multiple slaves (but just one master)
  Master drives a select line to each slave
  Fully-synchronous operation can reach 20 MB/s

## Slide 56: I2C
Only two wires – SCL (clock) and SDA (data)
  Single duplex
Any unit can be master or slave!
Complex protocol
  Each unit has a 7-16 bit address
  SDA can contain commands and/or unit address
  The current master always drives SCL
Up to 3.4Mb/sec
  Why do you think it’s slower than SPI?
Notes: Clock switching is ugly, and data bandwidth is stolen for control. Both these slow it down.

## Slide 57: What we didn’t cover
USB
  Much more complex, multi-layer protocol
  Many versions
  But lots faster, and the newer versions are parallel

## Slide 58: Exceptions
Anyone know a cheap-ish hobbyist Linux-ish board?
  Raspberry Pi
But how do they do it?

## Slide 59: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 60: Raspberry Pi use model
Remember our use model
Host
USB
Raspberry Pi is very different

## Slide 61: Raspberry Pi hardware
This is a single-board computer
Uses SD card instead of flash (the “hard drive”)
Power
SD card (holds O/S)
HDMI monitor
4x USB
LAN

## Slide 62: Raspberry Pi O/S
Raspberry Pi O/S is Linux
  Variant of Debian Linux
  All of the bells and whistles of Linux
  Class exercise: what are the consequences of that?

## Slide 63: How can a Pi run “Linux?”
 | Bits | Cores | MHz | On-chip flash | VM | Peripherals
STM32L476 | 32 | 1 | 80 | 1MB | No | tons
Broadcom BCM2837 | 64 | 4 | 1200 | ??? | Yes | few
Way more powerful CPU
But to avoid going over budget, few peripherals
  No analog GPIO pins; timers are few and simple
  Fine for hobbyists; they buy shields
  Hobbyist volumes can afford a few extra bucks, space
Requires ≥16GB SD card
Notes: The Pi specs are for a Raspberry Pi 3b (the 3b+ is1.4GHz rather than 1.2GHz)

## Slide 64: Raspberry Pi pros/cons
Pros
  fast, “cheap” ($35 for Pi 3b) computer
  can program it in your favorite language with your favorite editor
  fast enough to run Python easily
Cons
  STM32 = $1 to $10 or so
  standalone use without monitor or keyboard is hard (but can SSH in via ethernet or wireless)
  not a lot of peripherals (you need shields)
  bigger form factor than you may need (esp. w/shields)
  Needs ≥16GB SD card
  It’s not an RTOS (what???)

## Slide 65
Serial vs. parallel. We can always send 8 bits as one bit/cycle x 8 cycles or 8 bits/cycle * 1 cycles (or anything else). We could have done that with our 1-bit LED datum (sending 8 datum/cycle).
The obvious tradeoff? More wires vs. higher speed. Any examples of different busses that are narrow vs. wide? (USB-C is 24 pins wide).

## Slide 66: Mutexes and queues
Do an example of multiple tasks filling an array
Show the problem, and how a mutex helps
Next, avoid the problem by using a queue
Show them lab 3: two different ways to use a queue for two UART writers. But don’t tell them the solution.