EE26 Digital Logic Systems

Spring Semester 2011

Notes 5  (2/14/2011)

Project #2  Design, implementation and testing of 16-bit adders using FPGA

(Implementation due on Friday, Feb. 25

Report due on Fiday, March 4.)

SUMMARY

The goals of this lab are to become familiar with the

demo-board from Altera and to explore the design

complexity, hardware complexity, time complexity and testing

complexity of 16-bit parallel adders.

INTRODUCTION

We introduced several parallel adder design techniques

in class, namely 2-level design, FA implementation, and

Carry-Look-Ahead-Adder (CLAA) implementation. The trade-offs

are design complexity, hardware complexity and time

complexity. In this lab, you are going to design 2 versions

of 16-bit parallel adders using 2-bit and 4-bit CLAAs,

to simulate and to test your design.

ASSIGNMENT

1. Design a 2-bit CLAA and a 4-bit CLAA. Enter your design

using VHDL.

2. Design two 16-bit parallel adders using the CLAA components

designed in (1). Simulate your design. Discuss how you set

up the testing vectors.

3. Write a report individually which should include all

schematics and one example (timing diagram) of an input to

output transition.