EE26 Digital Logic Systems

Spring Semester 2013

Notes 5  (2/6/2013)

Project #2  Design, implementation and testing of 16-bit adders using FPGA

(Implementation due the week of Feb. ???

Report due in the week of February ???.)

SUMMARY

The goals of this lab are to become familiar with the

demo-board from Altera and to explore the design

complexity, hardware complexity, time complexity and testing

complexity of 16-bit parallel adders.

INTRODUCTION

We introduced several parallel adder design techniques

in class, namely 2-level design, FA implementation, and

Carry-Look-Ahead-Adder (CLAA) implementation. The trade-offs

are design complexity, hardware complexity and time

complexity. In this lab, you are going to design 2 versions

of 16-bit parallel adders using 2-bit and 4-bit CLAAs,

to simulate and to test your design.

ASSIGNMENT

1. Design a 2-bit CLAA and a 4-bit CLAA. Enter your design

using VHDL.

2. Design two 16-bit parallel adders using the CLAA components

designed in (1). Simulate your design. Discuss how you set

up the testing vectors.

3. Write a report individually which should include all

schematics and one example (timing diagram) of an input to

output transition.