## Slide 1: MIMD Multiple instruction, multiple data
BY Michael Nuzzolo

## Slide 2: Introduction
Multiple instruction streams
Multiple data streams
At any time, different processors may be executing different instructions on different pieces of data.
Not limited to executing a single instruction (SIMD)

## Slide 3: Parallelism Architectures
 | Single Instruction | Multiple Instruction | Single Program | Multiple Program
Single Data | SISD | MISD | - | -
Multiple Data | SIMD | MIMD | SPMD | MPMD
Notes: Flynn’s Taxonomy

## Slide 4: Multiple Instruction, Multiple Data
Became popular in the 80s, when multiple processors became relatively inexpensive and easily accessible
^Made possible by progress in integrated circuit technology and the transputer
By the 90s, MIMD computers with hundreds of processors became available
(Sima, D., Fountain, T. J., Kacsuk, P.)
Notes: Transputer was the first general purpose microprocessor designed specifically to be used in parallel computing systems

## Slide 5: Example Program Execution
(Wojcik, 2014)
Notes: Speed is dependent on the longest execution time of one processor in MMD

## Slide 6: MIMD
Good at independent branching (if & else)
Poor at synchronization and communication
(SIMD has opposite problem)
MSIMD/MIMD systems solve this problem, but are expensive
(Baig, El-Ghazawi, and Alexandridis, p.460)
Notes: Configured at run-time Multiple SIMD/ MIMD

## Slide 7: MIMD
Allows for more efficient execution of conditional statements because each processor can independently follow either decision path
Generally more expensive and complex than SIMD
Multiple decoders (one for each processor)
(Kaur & Kaur, 2013)

## Slide 8: Memory Architectures
Shared Memory
Distributed Memory

## Slide 9: Shared Memory
Interconnection Network
Memory 1
Memory 2
Memory 3
Processor 1
Processor 2
Processor 3
(Choi, 2014)

## Slide 10: Shared Memory
Advantages:
    Can use single processor programming style
    Efficient communication between processors
Disadvantages:
    Need to synchronize access to the shared data
    Memory contention limits scalability
(Choi, 2014)

## Slide 11: Shared Memory Classes
NUMA
COMA
CC-NUMA
(Kaur & Kaur, 2013)
Notes: COMA and CC-NUMA are used in newer generation of parallel computers

## Slide 12: NUMA
(Non-uniform memory access)
Shared memory is divided into blocks, each block is attached with processor
(Kaur & Kaur, 2013)

## Slide 13: NUMA
(Choi, 2014)
Notes: (PE - processing element)

## Slide 14: COMA
(Cache only memory access)
Every memory block works as a cache memory
(Kaur & Kaur, 2013)

## Slide 15: COMA
(Choi, 2014)

## Slide 16: CC-NUMA
(Cache-coherent non-uniform memory access)
Cache memory and memory blocks are attached with a processor
Solves cache coherence problem
(Kaur & Kaur, 2013)

## Slide 17: CC-NUMA
(Choi, 2014)

## Slide 18: Memory Architectures
Shared Memory
Distributed Memory

## Slide 19: Distributed Memory
Interconnection Network
Memory 1
Memory 2
Processor 3
Processor 1
Processor 2
Memory 3
(Choi, 2014)
PE 1
PE 2
PE 3

## Slide 20: Distributed Memory
Each processor contains its own memory
Accessing remote memory can cause stalls
Messages are sent between processing elements by switch units (router)
May be a communication processor - organizes communication, packetizing & depacketizing
(Kaur & Kaur, 2013)

## Slide 21: Distributed Memory
Advantages:
    Scalable design
    No synchronization problem
Disadvantages:
    Load balancing problem
    Message passing between processors causes deadlock
    Shared data must be copied between processors
(Choi, 2014)

## Slide 22: References
Kaur, Mandeep, Kaur, Rajdeep. (September, 2013) A Comparative Analysis of SIMD and MIMD Architectures. International Journal of Advanced Research in Computer Science and Software Engineering (1151-1156). http://www.ijarcsse.com/docs/papers/Volume_3/9_September2013/V3I9-0332.pdf
Choi, Ben. (2014) Introduction to MIMD Architectures http://www2.latech.edu/~choi/Bens/Teaching/Development/Hardware/
Wojcik, Vlad. (2013)Taxonomy of Supercomputers http://www.cosc.brocku.ca/Offerings/3P93/notes/2-Taxonomy.pdf
Sima, D., Fountain, T. J., Kacsuk, P.. Advanced Computer Architectures. Chaper 15 - Introduction to MIMD Architectures http://eclass.uoa.gr/modules/document/file.php/D36/%CE%A3%CE%B7%CE%BC%CE%B5%CE%B9%CF%8E%CF%83%CE%B5%CE%B9%CF%82%20%CE%93%CE%B9%CE%AC%CE%BD%CE%BD%CE%B7%20%CE%9A%CE%BF%CF%84%CF%81%CF%8E%CE%BD%CE%B7%29/chap15%20SIMA%20MIMD.pdf