## Slide 1: NVIDIA Tesla GPU
Zhuting Xue
EE126

## Slide 2: GPU
Graphics Processing Unit
The "brain" of graphics, which determines the quality of performance of the graphics

## Slide 3: NVIDIA Tesla
NVIDIA
  is a company, which designs graphics chip and chipset-based semiconductor , also achieving a lot of breakthroughs in parallel processing.
Tesla
  is a GPU produced by NVIDIA, which is designed for large-scale parallel computer;mostly work for science research in labs.

## Slide 4: GPU & CPU
In NVIDIA’s design, the GPU cooperates with CPU to accelerate scientific and other applications.
Application Code
GPU
CPU
Compute-Intensive Functions
5% of code
Rest of Sequential CPU Code
95% of code

## Slide 5: GPU Architecture
Dynamic Parallelism
  All child launches must complete in order for the parent kernel to be seen as completed
  Recursion, irregular loop structure or other structures that do not fit a flat, single-level parallelism can be more transparently expressed.
CPU
B
A
X
Y
Z
C

## Slide 6: GPU Architecture
Host interface and Compute Work Distribution
  Getting instructions and data from the host CPU and its main memory; also manage the threads of execution by assigning groups of threads to processor clusters and performing context switching;
TPC (texture/processor cluster)
  A basic building block of Tesla architecture GPUs (a single GPU can have from one to eight TPCs);
SM (Streaming Multiprocessor)
  A part of TPC, consisting of eight streaming processor cores, two special function units (for performing interpolation and approximate evaluation of trigonometric functions, logarithms, etc.), a multithreaded instruction fetch and issue unit, two caches and a pool of shared memory;
Texture unit
  Each unit is shared by two SMs, the unit plays its part in graphics calculations and is equipped with L1 cache memory accessible from SPs; Level 2 Cache memory units are connected through fast network to TPCs.
Host CPU
Bridge
System Memory
Host Interface
Input Assembler
Vertex Work
Distribution
Pixel Work
Distribution
Compute Work
Distribution
viewport/clip/setup/raster/zcull
GPU
Text Unit
TPC
SM
Shared
Memory
SP
SM
Shared
Memory
SP
Text Unit
TPC
SM
Shared
Memory
SP
SM
Shared
Memory
SP
Text Unit
TPC
SM
Shared
Memory
SP
SM
Shared
Memory
SP
Text Unit
TPC
SM
Shared
Memory
SP
SM
Shared
Memory
SP
Interconnection Network
ROP
L2
DRAM
ROP
L2
DRAM
ROP
L2
DRAM

## Slide 7: GPU Challenges
The GPU remains a specialized processor
Its performance in graphics computation belies a host of difficulties to perform true general-purpose computing.
The processors themselves require recompiling software they have rudimentary programming tools, as well as limits in programming languages and features.

## Slide 8: GPU VS CPU
CPU VS GPU

## Slide 9: Conclusion
GPU still cooperates with CPU , which is supposed to be broken through so that the GPU can complete all work without the help of CPU.
The competition between CPU and GPU is positive, which leads to the development of both GPU and CPU.

## Slide 10: Reference
[1]Maciol, Pawel, and Krzysztof Banas. "Testing tesla architecture for scientific computing: The performance of matrix-vector product." Computer Science and Information Technology, 2008. IMCSIT 2008. International Multiconference on. IEEE, 2008.
[2]Andreyev, A., A. Sitek, and A. Celler. "Acceleration of blob-based iterative reconstruction algorithm using Tesla GPU." Nuclear Science Symposium Conference Record (NSS/MIC), 2009 IEEE. IEEE, 2009.
[3]Lindholm, Erik, et al. "NVIDIA Tesla: A unified graphics and computing architecture." Ieee Micro 28.2 (2008): 39-55.
[4]Heinecke, Alexander. "Accelerators in scientific computing is it worth the effort?." High Performance Computing and Simulation (HPCS), 2013 International Conference on. IEEE, 2013.