## Slide 1: Memory testing methodologies
For embedded memory
Minghuan Zhao

## Slide 3: Fault Characteristics
Address-Decoder Fault (AF)
Stuck-At Fault (SAF)
Transition Fault (TF)
Coupling Fault (CF)
3

## Slide 4: Traditional solution
Walking Pattern-Complexity 2N2
Sliding Pattern-Complexity 4N1.5
Butterfly Pattern-Complexity 5NlogN
Means
Size | N | NlogN | N1.5 | N2
1G | 10.5sec | 5.3min | 4days | 366years
4

## Slide 5: Embedded memory Characteristics
embedded memory’s address, data, and control signals are usually not directly accessible through the I/O pins.

## Slide 6: Solution: March && Memory Built-In-Self Test
March Test typically has complexity: O(N)
  Linear access to memory by a specific order
Memory Built-In-Self Test(Architecture)
Normal data out
Normal address
Model select
Test clk
Address Generator
RAM
Self-test controller
Data generator
Data receiver
(Comparator)
Normal data in
reset
Reference

## Slide 7: March C-(evolved March C)
March C- is a classical algorithm which is the foundation of other algorithms
{(w0);(r0,w1);(r1,w0);(r0,w1); (r1,w0);  (r0)}
Complexity—5N=>O(N)
 ascending order
 descending order
r0:read 0
w1:write 1
March Element (w0): M0

## Slide 8: {(w0);(r0,w1);(r1,w0);(r0,w1); (r1,w0); (r0)} M0 M1 M2 M3 M4 M5
Address Fault, Transition Fault: M2 and M3
Stuck-At Fault: overwrite 0’s and 1’s
M1
0 1
0 1
0 1
M2
1 0
1 0
1 0
M2
1 0
1 0
1 0

## Slide 9: {(w0);(r0,w1);(r1,w0);(r0,w1); (r1,w0); (r0)} M0 M1 M2 M3 M4 M5
Coupling Fault (CF)
  j< i, Cj affected by Ci
  M1: Ci 1->0 falling behavior affect Cj
  M2: Ci 0->1 raising behavior affect Cj
  j> i, detected by M3 and M4
M1
1
0 1
0 1
M2
0
1 0
1 0
0(j)
1
2(i)

## Slide 10: Other March algorithm
 | SAF | AF | TF | CF
MATS | ALL | Some |  | 
MATS++ | ALL | ALL |  | 
March X | ALL | ALL | ALL | Some
March C- | ALL | ALL | ALL | ALL
March A | ALL | ALL | ALL | Some
March B | ALL | ALL | ALL | Some
March Y | ALL | ALL | ALL | Some

## Slide 11: Challenge
Silicon area overhead
Complexity can be less than O(N)
Faults coverage
Decrease test instructions and data
Normal data out
Normal address
Model select
Test clk
Address Generator
RAM
Self-test controller
Data generator
Data receiver
(Comparator)
Normal data in
reset
Reference