## Slide 1: Bioelectricity
Fall 2022
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Bioelectricity 2a – neurons

## Slide 2: Big picture of the course
Where does bioelectricity come from?
Neurons and working with the nervous system
Cardiac bioelectricity
Worms
How a single neuron works
Lots of neurons – the nervous system
EMG, prosthetics, NCS, SCS, PNS, electroceuticals

## Slide 3: Turning off cytokine storms
Can you explain the science here?
  www.setpointmedical.com (white paper at https://setpointmedical.com/sp-content/uploads/2018/09/Setpoint_Medical_White_Paper_digital.pdf )
  https://spectrum.ieee.org/the-human-os/biomedical/devices/handheld-vagus-nerve-stimulator-gets-emergency-approval-for-covid19-use
Notes: Cytokines are signaling chemicals used by the immune system. There are many different cytokines, with different effects. A cytokine storm is when the immune system produces way too many pro-inflammatory cytokines.

## Slide 4: Why neurons?
Why do humans have neurons?
  Bacteria don’t have neurons, and they do fine 
  Humans have brains and bacteria don’t
  Bacteria can “think” without brains!
  On Having No Head: Cognition throughout Biological Systems, 2016
Any other reasons humans have neurons and bacteria don’t?

## Slide 5: The problem with being big
Imagine you’re Fred Flintstone and a dinosaur is chasing you
  To run away, your brain must send a message to your feet – over 5’ away
  Bacteria don’t need long-distance signaling

## Slide 6: Long-distance diffusion is slow
Another diffusion equation
  average distance covered by diffusion is
Is diffusion more feasible for smaller or larger creatures?
  traveling twice as far takes 4x longer
  works fine for bacteria, not so well for humans
For long-distance communication, electrical is much faster than diffusion
  if you’re bigger than a bacteria, you need neurons
  fun fact: bacterial communities communicate electrically
  Venus flytraps don’t have brains, but they do use action potentials to act fast!
Notes: Diffusion doesn’t work well for giraffes, either!
I’m not sure if the electrical communication in bacterial communities is providing a big speed advantage (bacterial communities are still pretty small).

## Slide 7: Slick video
https://www.youtube.com/watch?v=UZthGjcuTDs
  Joe Hansen video
  5 minutes in class
  the rest on your own if you like

## Slide 8: This slide set
How a single neuron works
Lots of neurons – the nervous system

## Slide 9: What is a neuron?
Long skinny cell that conducts action potentials
  Communication (mostly) between your brain and the rest of your body
One neuron is not very useful
  Your brain has ≈86 billion neurons
Notes: People used to say 100 billion; now they say 86.

## Slide 10: How neurons spike
Nature has built a pretty amazing system
  By altering GNa and GK, we can quickly swing between -89mV and +77mV
  We can build any waveshape by suitably altering GNa and GK
77mV
-89mV
-71mV
ECF
ICF
GNa
GK
GCl
INa
IK

## Slide 11: In-class exercise
For each of the three regions
  what do you think is happening to GNa?
  to GK?
both “baseline”
Both return to baseline
VNNa=+54mV; VNK=-90mV; VNCl=-70mV
GNa rising
GK rising

## Slide 12: Detailed waveforms
If you were to guess, how do you think GNa and GK change over the course of a spike? Draw it
Na and K both have low G
Na has high G
K has high G
Both return to baseline
GNa is the green curve
GK is the blue curve
VNNa=+54mV; VNK=-90mV; VNCl=-70mV

## Slide 13: How do we get those shapes?
Now we know what shapes we want for GNa and GK; how do we get them?
The Hodgkins-Huxley model
  Differential equations for the blue and green curves
  Basic idea is voltage-sensitive ion-channel turnon
  GNa contains an increasing function of Vmem; fast positive feedback → rising spike with a turnon threshold
  Slow negative-feedback mechanism shuts the spike off
Exercise – can you explain the refractory period?
GNa is the green curve
GK is the blue curve
Notes: The Na gate is m^3*h; m is a monotonically increasing function of Vmem (with a fast tau), and h is a monotonically decreasing function of Vmem (with a slow tau). So overall they work to make GNa actually shut itself off even without needing GK. The K gate is n^4, where n is monotonically increasing and medium slow.
In fact, to really explain the refractory period you need to know about “h”; the refractory period is when h is low, and thus the Na ion channels cannot turn on until h (slowly) goes back to 1. But we can roughly explain the refractory period by saying that it’s when the slow negative-feedback mechanism is forcing the spike off, and since it’s slow G_K stays high for a while.

## Slide 14: It’s nice that APs are short & sweet
Neurons are fast
  Change GNa and/or GK → near instant change in Vmem
But…
  the march to a new steady state starts instantly too
  if the changes in GNa and/or GK lasted long enough, the internal [Na], [K] and [Cl] would change
Any consequences of that?
  the neuron would function differently at the next spike
  But it doesn’t happen; we saw that neurons return to baseline quite quickly
  There’s a good reason why action-potential spikes are short and sweet!
Notes: This one is a semi-backup. Mention that!
Now we know all about APs. What missing? The fact that they travel!

## Slide 15: APs travel
Time(ms)
0
1
2
3
4
5
Vmem(mV)
-55
-70
0
+40
Speed=0.5 – 150 m/s
Notes: This is our first exposure to a neuron – we’ll look at it in more detail later. For now, it just has an input on the left, output on the right
AP starts on the left
It looks like a traveling wave.
There’s a wide range of neuron speeds – more on that later

## Slide 16: Mechanism of travel
Start with an action potential (AP) at one end of a neuron
  it started when Vmem was pushed high enough
Vmem is changing via drift, diffusion through ion channels
But – diffusion is 3D
  goes axially as well as radially
ion channels
Notes: The AP was caused by a bit of extra + charge at one point.
Diffusion happens left/right as well as through ion channels!

## Slide 17: Mechanism of travel
Next plot: Vmem vs. x
t=0: blue
t=1: green
Now there’s enough Vmem here to fire an AP
0 1 2 3
Vmem
distance from the neuron’s starting (dendrite) end
Notes: The AP was caused by a bit of extra + charge at one point.

## Slide 18: Mechanism of travel
Start with an action potential (AP) at one end of a neuron
  it started when Vmem was pushed high enough
Diffusion:
  it damps
  but this pushes Vmem higher nearby
Vmem nearby
x axis is time; each graph is a different location

## Slide 19: Traveling APs
Why don’t they reverse direction?
  Why doesn’t the green AP at x=2 diffuse to x=1 as well as to x=3?
  It does diffuse. But x=1 is in refractory mode
  Rising above threshold won’t kick off an AP
Time(ms)
0
1
2
3
4
5
Vmem(mV)
-55
-70
0
+40
x=1
x=2

## Slide 20: Myelin
Some neurons are coated with myelin
  A fatty, non-conductive layer
How does myelin affect membrane capacitance?
cell membrane
myelin

## Slide 21: Myelin
What good is myelin?
  Makes neurons propagate an action potential fast
  A big evolutionary step in our brains being useful 
Thick membrane → low C
  Q=CV: does low C means faster or slower?
Multiple sclerosis is an auto-immune disease where (among other issues) nerves get demyelinated
faster. Takes less Δq to make enough ΔV

## Slide 22: The problem with myelin
Neuron without myelin
  Action potential travels slowly
  Gets regenerated frequently
Neuron with myelin
  Ion channels cannot traverse the sheath
  Vmem wave spreads much faster. But…
  Without ion channels, action potentials cannot regenerate!
  Die out before reaching the other end of the neuron 
ion channels
Solution:
Nodes of Ranvier
Occasional gaps in the myelin sheath, big enough to allow AP regeneration

## Slide 23: That’s a neuron!
Takes inputs from upstream neurons
Generates an AP
The AP travels
Myelin makes it go fast
Drives downstream neurons

## Slide 24: This section
How a single neuron works
Lots of neurons – the nervous system

## Slide 25: Lots of neurons
The brain has 86B neurons.
Each dendrite takes inputs from 1000 other neurons and decides when to fire
  Each input pulse raises Vmem slightly; fires when it hits a threshold
An action potential then travels along the axon to the next downstream synapse(s)
synapse
Notes: For those of you who are into NNs, is this exciting? It’s a very nonlinear response, which ANNs depend on. Of course, your brain doesn’t really care if some computer scientist built an ANN like a real brain or not, but it’s probably comforting for the CS person :-).

## Slide 26: How neurons talk to each other
Driving neuron stores neurotransmitter molecules. AP → release them into the synapse
Neurotransmitter diffuses across the synapse, binds to receptor proteins
Receptor protein acts as an open ion channel, thus allowing a packet of charge to enter or leave it, changes receiver Vmem
Doesn’t this diffusion slow down the system?
  Cardiac lookahead – some neurons talk with GJs
synapse
Notes: Diffusion over short distances like a neural cleft is fine – the big diffusion issue is traveling for longer distances

## Slide 27
Central nervous system (CNS, red)
  brain + spinal cord
  controls most everything
  big mystery
Peripheral nervous system (PNS, blue)
  everything but the CNS
  CNS signals must usually traverse PNS to do anything
  typically 100s of neurons per nerve
  electroceuticals target here

## Slide 28
Sensory neuron
  Carries information towards the brain
  E.g., touch a hot stove
Motor neuron
  Carries information away from the brain
  e.g., control your muscles
  anything else?
Notes: First, we’ve skipped a neuron type – sensory, motor and interneurons (which connect the two, especially in reflexes).
Second – a motor neuron can drive a gland as well as a muscle. Glands produce & secrete various molecules, typically under nervous-system control. E.g., your sweat glands or your hormones.

## Slide 29: Reflexes
What is a reflex?
  A sensory nerve detects a signal
  Travels into spine
  Synapses with a motor nerve to come right back
Example: tap under your kneecap and your leg kicks
Lippincott Ch 11

## Slide 30: Why do we have reflexes?
Why not have all signals just travel to the brain and back?
CPG
Central Pattern Generator (CPG)
  small state machine in your spine
  Why might this be useful in addition to brain, reflexes?
  intermediate solution (faster than the brain, more powerful than reflexes)
  walking is likely controlled by a CPG
Notes: Talk about the tradeoffs involved. Reflexes can be very fast; getting to/from the brain takes at least 20ms each way (plus any actual thinking!). A CPG is an intermediate compromise. It also reduces upper-spinal-cord thickness and can give you some motion after spinal-cord injury.

## Slide 31: Mini-quiz
Take 5 minutes & check yourself in groups
  What is a refractory period?
  What does myelin do, and why?
  What do neurotransmitters do? They diffuse from one neuron to another – why doesn’t that slow down the system?
  What is the central vs. peripheral nervous system?
  What is a reflex?