## Slide 1: Verification
Spring 2021
Tufts University
Instructors: Joel Grodstein, Scott Taylor
Building a tracker

## Slide 2: Problem of the day
Problem to be solved: debugging is tedious!
  OK, that’s the problem for the whole course
  We won’t solve it all today
Subproblem
  Poring over 100 signals on a waveform display is ugly
  How else do you track a transaction around the DUT?
Is there a better way?

## Slide 3: Tracker (a.k.a. monitor)
Example problem
  launch packet “data=0x123, src_yx=(2,2), dst_yx=(1,1)
  It never arrives at the destination!
  How do we debug this?

## Slide 4: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 22 → 11

## Slide 5: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 22 → 11
Piece of cake 
But what if it didn’t work?

## Slide 6: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Trace the top-level signals one by one
This gets old fast!
And you still have to dive into the broken mesh stop 

## Slide 7: It can get much worse
Mesh may be bigger than 4x4
Packets may be multiple cycles long
  or a variety of formats
  difficult to find your packet among a sea of bus transactions

## Slide 8: Tracker to the rescue!
A tracker helps you debug efficiently
What is it?
  Crawls through the entire DUT
  Looks at the signals
Abstracts and beautifies
  Turns bits into transactions
  Presents the transactions in simple-to-understand text or graphics
  E.g., can hunt/trace one specified packet

## Slide 9: Sample output for us
Sample output:
  200. MS[2,2].DRV.FMem[0]: Data=5, from y,x=(2,2) -> (1,1)
  200. MS[2,2].DrvFOut: Data=5, from y,x=(2,2) -> (1,1)
  220. vert[3,2]: Data=5, from y,x=(2,2) -> (1,1)
  240. vert[0,2]: Data=5, from y,x=(2,2) -> (1,1)
  260. vert[1,2]: Data=5, from y,x=(2,2) -> (1,1)
  280. MS[1,2].VRxF.FMem[0]: Data=5, from y,x=(2,2) -> (1,1)
  280. MS[1,2].VRxFOut: Data=5, from y,x=(2,2) -> (1,1)
  300. hori[1,3]: Data=5, from y,x=(2,2) -> (1,1)
  320. hori[1,0]: Data=5, from y,x=(2,2) -> (1,1)
  340. hori[1,1]: Data=5, from y,x=(2,2) -> (1,1)
  360. MS[1,1].HRxF.FMem[0]: Data=5, from y,x=(2,2) -> (1,1)
  360. MS[1,1].HRxFOut: Data=5, from y,x=(2,2) -> (1,1)
  380. MS[1,1].HRxF.FMem[0]: Data=5, from y,x=(2,2) -> (1,1)
  380. MS[1,1].HRxFOut: Data=5, from y,x=(2,2) -> (1,1)
  400. MS[1,1].HRxF.FMem[0]: Data=5, from y,x=(2,2) -> (1,1)
  400. MS[1,1].HRxFOut: Data=5, from y,x=(2,2) -> (1,1)
Immediately tells you where to look!

## Slide 10: How do you build it?
“Just a small matter of software”
  turns out to be harder than it sounds!
Take 1 – just the main ring busses
  module tb_mesh;
  for (y=0; y<MESH_SIZE; ++y)
  for (x=0; x<MESH_SIZE; ++x)
      if (vert_ring[y][x] == hunted)
        $display (“%t. Vert_ring[%d,%d]=%s“,
        $time, y, x, print_ring_slot(hunted));
Easy enough so far 
  but now the fun begins

## Slide 11: How deep is enough?
Tracking a packet around the rings is easy, and is a big time-saver
  even more so for a 16x16 mesh, or multi-cycle packets
How about tracking inside the mesh stops?

## Slide 12
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
can_accept_data_from_venv

## Slide 13: How do you build it?
“Just a small matter of software”
  bites us in the posterior
Does this code work? (see mesh_NxN.sv)
  module tb_mesh;
  for (y=0; y<MESH_SIZE; ++y)
  for (x=0; x<MESH_SIZE; ++x)
      if(tb_mesh.M_NxN.yloop[y].xloop[x].MS.VRxF_out==hunted)
        $display (“%t. VRxF_out[%d,%d]=%s“,
        $time, y, x, print_ring_slot(hunted));
Compilation error
  Cannot index module instances as arrays with a variable as index!
Notes: It’s like the hierarchical signal name is just a big string, not a part of an array.

## Slide 14: Ugly workaround
This way does work
    if(tb_mesh.M_NxN.yloop[0].xloop[0].MS.VRxF_out==hunted)
      $display (“%t. VRxF_out[0,0]=%s“, $time, print_ring_slot(hunted));
    …
    if(tb_mesh.M_NxN.yloop[3].xloop[3].MS.VRxF_out==hunted)
      $display (“%t. VRxF_out[3,3]=%s“, $time, print_ring_slot(hunted));
Not very nice for the entire 4x4 array (let alone 16x16) 
  and multiple signals in each mesh stop
  and all of the FIFO-internal state
What to do?
Notes: Again: this version works because the hierarchical signal name is more like a big string, not a part of an array.

## Slide 15: Clever idea?
Pros?
  It works! (But where does “hunted” come from?)
  All mesh stops are taken care of automatically
  Verif. team need not know where all the mesh stops are
Cons?
  Must ensure this code isn’t synthesized 
  We’ve polluted the design
module mesh_stop #(parameter MY_Y=0, MY_X=0)
  Ring_slot VRxF_out;
  if (VRxF_out == hunted)
    $display (“%t: %s.VRxF_out=%s”, $time,
          $sformatf ("%m"), print_ring_slot(hunted));
  … rest of the mesh_stop module…
hierarchical instance name
Notes: You can probably play with global variables to get “hunted” in, but that’s ugly.
Polluting the design is the kiss of death. Cannot do this!

## Slide 16: Clever idea, v2
module mesh_stop #(parameter MY_Y=0, MY_X=0)
  Ring_slot VRxF_out;
  Tracker_module T1 (VRxF_out, “VRxF_out”);
  … rest of the mesh_stop module…
module automatic tracker_module
    (input Ring_slot RS, input string sig);
  Tracker track_inst = new();
  string signame = $sformatf ("%m%s“,sig);
  always @(RS) begin
    track_inst.add_signal (signame, RS);
  end
endmodule
class Tracker;
  static string names[$]
  static Ring_slot values[$];
  function add_signal (name, val);
    update names[], values[];
  function hunt (hunted)
    go through names[], values[] & print matches
endmodule
instance of a special module. Not quite as intrusive?
When VRxF_out changes…
tell the verif. env. about the new value
Class that makes it all work
“Static” means just one of these, not one per object
Now we always know the latest value 
Ver.env. calls this every cycle

## Slide 17: Clever idea, v2
module mesh_stop #(parameter MY_Y=0, MY_X=0)
  Ring_slot VRxF_out;
  Tracker_module T1 (VRxF_out, “VRxF_out”);
  … rest of the mesh_stop module…
module automatic tracker_module
    (input Ring_slot RS, input string sig);
  Tracker track_inst = new();
  string signame = $sformatf ("%m%s“,sig);
  always @(RS) begin
    track_inst.add_signal (signame, RS);
  end
endmodule
class Tracker;
  static string names[$]
  static Ring_slot values[$];
  function add_signal (name, val);
    update names[], values[];
  function hunt (hunted)
    go through names[], values[] & print matches
endmodule
Pros?
It works! (But where does “hunted” come from?)
All mesh stops are taken care of automatically
Verif. team need not know where all the mesh stops are
Cons?
Must ensure this code isn’t synthesized 
We’ve polluted the design
X
X
Notes: We’ve reduced the amount of verification-only code in the mesh_stop module, but we haven’t eliminated it -- yet

## Slide 18: Clever idea, v3
module mesh_stop #(parameter MY_Y=0, MY_X=0)
  Ring_slot VRxF_out;
  Tracker_module T1 (VRxF_out, “VRxF_out”);
  … rest of the mesh_stop module…
module automatic tracker_module
    (input Ring_slot RS, input string sig);
  as before…
endmodule
class Tracker;
  as before…
endmodule
module tb_mesh;
  bind mesh_stop tracker_module T1(DrvF_out, “DrvF_out”);
Bind() is a special sauce!
Find all mesh_stop instances
Stick a tracker_module instance in each one
With the same arguments as before
Notes: We’ve reduced the amount of verification-only code in the mesh_stop module, but we haven’t eliminated it -- yet

## Slide 19: Clever idea, v3
module mesh_stop #(parameter MY_Y=0, MY_X=0)
  Ring_slot VRxF_out;
  Tracker_module T1 (VRxF_out, “VRxF_out”);
  … rest of the mesh_stop module…
module automatic tracker_module
    (input Ring_slot RS, input string sig);
  as before…
endmodule
class Tracker;
  as before…
endmodule
module tb_mesh;
  bind mesh_stop tracker_module T1(DrvF_out, “DrvF_out”);
Pros?
It works! (But where does “hunted” come from?)
All mesh stops are taken care of automatically
Verif. team need not know where all the mesh stops are
Cons?
Must ensure this code isn’t synthesized 
We’ve polluted the design
X
X

## Slide 20: Software BKM
Yes, it’s complex
  Requires strong object-oriented programming skills
  We did warn you verification = HW + SW
Cost/benefit tradeoff always
  For us, just tracking main ring wires was easy
  Going inside the mesh stops has cost, incremental value
Next step
  Look inside of FIFO memory at a mesh stop

## Slide 21
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
VRxF_out
HRxF_out
DrvF_out
But about about tracking data inside the FIFOs?
can_accept_data_from_venv
Notes: It’s hard! You have to look at the rd* and wr* and figure out which entries are valid at any time.
Again – cost/benefit tradeoff.

## Slide 22: Summary
Trackers can automatically (i.e., in SW)
  hunt through the morass of busses & bits
  build higher-level objects (packets, transactions)
  print them as needed for debugging
It’s all just software
  but software can be easier said than done
Discussion
  What’s the difference between a tracker vs. monitor vs. checker?