## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
Checking correctness

## Slide 2: Outline of this lecture
Intro
No right time
No right answer
Reference models
Self-checking tests
Implementation

## Slide 3: Did your test pass?
You run a test
Obvious question
  how do you know if the DUT got the right answer?
Let’s look at what we did for our FIFO tests…

## Slide 4: Scoreboard
Same inputs to both models
Cycle by cycle comparison
test inputs
drivers
DUT
ref model
scoreboard
(compare
==?)
Verification environment

## Slide 5: Good enough?
Do you think this approach will be universally useful?
  Hint – this will be a very short lecture, if so!
  Answer – no, it’s not 
Rest of the lecture – why not, and what to do about it
test inputs
drivers
DUT
ref model
scoreboard
(compare
==?)
Verification environment

## Slide 6: What does correct mean?
Come on, this is easy, isn’t it?
  Yes – in some cases, definitely
Correct means…
  Should get the correct data!
  Push 0xAB into the FIFO, better not get 0xBA out!
  Data comes out at the correct time
  no off-by-one-cycle errors
What if there is no correct time?
What if there is no correct data?

## Slide 7: Outline of this lecture
Intro
No right time
No right answer
Reference models
Self-checking tests
Implementation

## Slide 8: No right time
The mesh
  it must deliver packets to their destination
  Do we spec the precise arrival cycle?
Cycle-by-cycle compare cannot work
Any examples other than the mesh?
  where the DUT is free to use whatever timing it wants
  but it has to get the right answer eventually
Notes: Most any router works like the mesh.
And any CPU is a perfect example! The ARM specs what instructions do, but not how long execution takes.
And we must reset within .5s, but faster is OK.

## Slide 9: Really, no right time!
Branch prediction
Does BP change the final output of a program?
  will a bug in the BP change the program output?
So how can you verify that the BP is working?
What state or timing does BP change?
  LD r1=MEM[r2]
  BZ L1
  ADD r4=r5+r6
L1: SUB r4=r5+r6
LD | F | D | EX | MEM | WB |  | 
BZ |  | F | D | EX | MEM | WB | 
ADD |  |  | F | D | EX | XX | 
SUB |  |  |  |  |  | F | D
Notes: For most tests, you actually will never know if the BP worked at all.
Writing a BP test is ugly; the verifier must learn how the BP works and then duplicate it, very much like we did with the FIFO. So yes, you must write a cycle-accurate model of the BP and then throw it away on the next project.

## Slide 10: Reset
How do you verify reset?
It’s actually quite hard! Any thoughts why?
  Most nodes power up as “X”
  Chip must reset to “enough” of a known value that subsequent execution works
  Reset must typically happen within a certain time period, but no exact spec
Something to think about…
Notes: we won’t talk much about reset in this course, but again – it can be ugly 

## Slide 11: Outline of this lecture
Intro
No right time
No right answer
Reference models
Self-checking tests
Implementation

## Slide 12: What does correct mean?
Come on, this is easy, isn’t it?
  Yes – in some cases, definitely
Correct means
  Should get the correct data!
  Push 0xAB into the FIFO, better not get 0xBA out!
  Data comes out at the correct time
  no off-by-one-cycle errors
we just did this
now for this one
Remember this slide?

## Slide 13: No right value
What if the DUT doesn’t spec the correct data?
Can you come up with any meaningful examples of this?
  what use is a system that doesn’t have a correct answer, anyway?
  engineers like our problems to have a right answer!
In fact, many such examples
  Liberal-arts majors will be happy today 

## Slide 14: Multithreaded code
What is the end-of-test value of mem[1000]?
Fundamental issue
  threads can execute in arbitrary order
  Most architectures make no guarantees
thread #1
store mem[1000]=3
thread #2
store mem[1000]=4

## Slide 15: Multithreaded code
Room-change announcement
  First – write room_location, change Halligan 102 → 111
  write an e-mail to the class
  what if the class sees the e-mail before the room-change write?
Memory
  coherency – all cached copies of a memory location have the same value
  consistency – ordering of two accesses is seen identically by all threads
Short exercise: does ARM guarantee you see the correct room?
  https://devblogs.microsoft.com/cppblog/hello-arm-exploring-undefined-unspecified-and-implementation-defined-behavior-in-c
thread #1
store mem[1000]=3
thread #2
store mem[1000]=4
≈ all CPUs, no GPUs
some CPUs
Notes: In fact, x86 is strongly ordered (two writes by one thread are seen in the same order by all threads). But ARM is just weakly ordered – two writes by a thread are seen in the correct order by that thread, but other threads may see the two writes in any order.

## Slide 16: But what to do?
What to do about multi-thread issues?
  Only write single-threaded tests
  Write very careful multi-threaded tests with only one answer
  Analyze your multi-thread tests & accept any reasonable answer
Pros and cons of each?
Bottom line – RCG for a multithreaded memory system is hard!
thread #1
store mem[1000]=3
thread #2
store mem[1000]=4
Notes: If you only write single-threaded tests, you’re leaving much of the memory system untested
Writing tests very carefully is great in principle – but expensive
Analysis, also, is sometimes easier said than done

## Slide 17: Error handling
Pick your favorite HW project from the last few years
  Did the assignment spec your project’s response to input data?
  To incorrect inputs?
Commercial projects are better
  not always perfect
  some chips specifically specify that certain results are unspecified!
  fun task – search for the term “Implementation defined” in the ARM Architecture Reference Manual
  or learn what “Imprecise exceptions” are
How can you handle these cases?
hopefully
sometimes
Notes: Most college classes sweep error handling under the rug (unfortunately).
Once again, the only real answer, often is to try and ensure that your general-purpose tests don’t trigger unspecified cases.
Then you’ll hand-write enough cases to convince your test plan that the feature is tested.
Are we getting a feel for why verification is expensive?

## Slide 18: Still more…
Can you think of any examples where there isn’t just one right answer?
  CPU with imprecise exceptions
  no guarantee which instructions complete after an exception happens
Any other examples?

## Slide 19: Outline of this lecture
Intro
No right time
No right answer
Reference models
Self-checking tests
Implementation

## Slide 20: But…
test inputs
drivers
DUT
ref model
scoreboard
(compare
==?)
Verification environment
DUT may not have a single right answer, known time
Two approaches
  make the reference model more flexible
  self-checking test doesn’t use a reference model
Now
Next

## Slide 21: Reference models
Three categories of reference models
Cycle accurate
  like our FIFO model
End-of-test accurate
  model gives you the desired answer
  no idea when it will show up!
  check results at end of test
Transaction accurate
  compromise
  try to check each transaction as it occurs
Easy 
Next
And then…

## Slide 22: End-of-test mesh checking
Start with our favorite example – the mesh
We can observe the incoming packets
How would you spec the end-of-test check?
test inputs
drivers
DUT
ref model
scoreboard
(compare
==?)
Verification environment
Notes: Actually, it’s quite easy. All the packets got to their correct destination by the end of the test.

## Slide 23: OOO CPU
Next example – an OOO CPU
  instructions launch in program order
  instructions execute in dataflow order
  instructions retire in program order
Few guarantees about execution order
Exercise – spec out your end-of-test CPU check
  like we did for the mesh
Notes: This one is pretty easy also. Just forget the OOO stuff, since it cannot change the end result.
Write a basic ARM-based model that just gets the right answer, and it will indeed get the right answer

## Slide 24: End-of-test checks
End-of-test checks look easy! 
  Because we haven’t looked very hard yet 
  No free lunch

## Slide 25: When are we done?
We said “check values at the end of the test”
  but how do we know when the test is ended?
  how many cycles do we wait?
Strategy – just wait a really really long time
  Problems?
  just how long is that anyway?
  now every test is really slow

## Slide 26: OOO CPU
What makes a CPU test take a really long time?
  cache misses can cause long delays
  paging is far worse
Any way to not wait 1M cycles after every test? 
  monitor the cache-miss signals
  only wait the max if there is indeed a cache miss
  lots more signals we can look at; any ideas?
Works fine. Any cost to it?
  test environment must be more sophisticated
  must adapt to signals in the DUT

## Slide 27: When is the mesh done?
Back to the mesh again…
Spec – no fixed interval for a packet to reach its output
So again – how do we know when the test is done?
Some ideas:
  wait until the inputs have stopped for a while, and we’ve observed as many output packets as input packets
  wait until all FIFOs are empty
Take a few minutes and try to poke holes in these ideas
Often the test will write an agreed-upon register when it’s “done” (e.g., has written all packets to the mesh)
  would this change the effectiveness of the two ideas above?
Notes: One idea; wait until the inputs have stopped for a while, and we’ve observed as many output packets as input packets. But that will have us wait forever if the mesh drops a packet.
Another – wait until all FIFOs are empty. That’s good, too, but what if a deadlock (or even just a simple control bug) prevents a FIFO from draining?
So we better also have a timeout, and only wait that long after the inputs have stopped.
How does a test tell the TB that it’s done? Usually, we write an agreed-on register.

## Slide 28: Legally waiting forever?
Further discussion
  Does Comcast spec how long you will ever wait for packet transmission?
  If your max interval is only probabilistic, how do you pick the timeout length?
  What will happen when a legal test case exceeds your chosen timeout length?
Observation: pick TIMEOUT too short → will have to manually debug some tests
  will give you insight into what makes your system slow
  will take lots of debug time!
Notes: If you pick your timeout length too low, you’ll wind up with tests failing, and have to manually triage them. That may not be bad; it will give you insight as to what kind of tests make the system slow. But it can be expensive to your schedule!

## Slide 29: More no free lunch
End-of-test checking is great, except…
  not always easy to know when the test is ended
  and…

## Slide 30: OOO CPU
OOO CPU strategy summary
  Run the whole program
  Wait the “smart-timeout” number of cycles
  Check for correct values in all registers, memory
Seems reasonable?
Consider this program
What if the DUT has a bug
  the first load to any reg is dropped
  will we catch it with this program?
  how can we catch it at all?
load R5=6
load R5=5
Notes: We will not catch the error with this program.
We need other programs that only write each register once, not twice.
I.e., lots of random loads and stores.

## Slide 31: More no free lunch
End-of-test checking is great, except…
  not always easy to know when the test is ended
  and you may lose test sensitivity
  and debugging is a PITA
Why is end-of-test debug so ugly?
  because the bug probably happened a really long time ago
  walking backwards 1M cycles is not fun at all 

## Slide 32: Making debug easier
Find failures sooner → debug is easier
But how do you do that?
Lots of assertions
  pipeline data moves along correctly
  mux controls are exclusive & match high-level transaction
  whatever else you can think of!
  but – careful not to rewrite the entire model in the assertion!
Notes: These assertions can quickly get way too complicated to be worth their ROI. E.g., pipelines often do *not* move smoothly in normal operation, so your assertion would have to be smart enough to handle that. At some point, you’re really rewriting the RTL model in the verification environment, which is not a wise move.

## Slide 33: Livelock/deadlock
Remember what these are?
  Deadlock: A waits for B, B waits for A, nobody moves
  Livelock: everyone moves but just in circles
Fun diversion – can you write examples of each?
Should the verification environment detect these?
How can it?
  Look for endless loops of the same few instructions
  Look for a lock instruction that repeatedly fails
draw out a picture of these cases
Notes: Deadlock: thread #1 executes the code “Grab lockA grab lockB; do work; release locks”. But thread 2 executes “Grab lockB; grab lockA; do work; release locks”. Then we get stuck where each thread has grabbed its first lock, but will never succeed at grabbing the other lock.
Livelock modifies the code slightly; it replaces the second “grab lock” in each thread with “if the lock is free then grab it, otherwise release my first lock and try both grabs again.” If both threads stay *perfectly* in sync, then this can do an infinite lock, release, lock, release, … loop in each thread.
We want to detect deadlock/livelock because otherwise we just wind up with a test that never finishes and it’s the usual hard-to-debug problem.

## Slide 34: Faster mesh failure
We want to find failures faster
Does this work?
  ref model delivers packets instantly
  scoreboard queues up inputs in a FIFO
  keep checking all DUT outputs for a match
  remove packet from SB FIFO when it matches
test inputs
drivers
DUT
ref model
scoreboard
(compare
==?)
Verification environment
==?
FIFO
FIFO
Notes: Doesn’t work – the mesh doesn’t even preserve packet ordering. So the scoreboard FIFO won’t work

## Slide 35: Mesh test – v2
Rules to check
  packet must get to the correct destination
  must take at least 1 cycle
  must take less than TIMEOUT cycles
Checking algorithm
  store copies of the packets that have launched.
  when a packet arrives anywhere, check that it was sent & mark the original packet as received.
  stop the sim TIMEOUT cycles after the final packet launch
  confirm that all packets were received
Does this work?
How is it better than end-of-test checking?
Brainstorm: how can we make our checking even tighter?
Notes: Yes, this does work. We can in fact add three more checks. First, that no packet was received twice. Second, that each individual packet meets the timeout rule. Third, that all FIFOs are empty at end of sim.

## Slide 36: Reference models
Three categories of reference models
Cycle accurate
  like our FIFO model
End-of-test accurate
  model gives you the desired answer
  no idea when it will show up!
  check results at end of test
Transaction accurate
  compromise
  try to check each transaction as it occurs
Easy 
Just talked about this
And wound up sort of talking about this
Notes: Our on-the-fly mesh test is starting to look like transaction-level verification

## Slide 37: Reference model summary
When are cycle-accurate models practical?
  worked fine for our FIFO
  and for other very simple chips
  or for a verifying one small piece of a larger DUT
And when they’re not…
  check as much as you can as soon as possible after it happens
  check the rest at the end of the test (but it will be hard to debug and may miss overwrite cases)

## Slide 38: Outline of this lecture
Intro
No right time
No right answer
Reference models
Self-checking tests
Implementation

## Slide 39: Reference models
DUT may not have a single right answer, known time
Two approaches
  make the reference model more flexible
  self-checking test doesn’t use a reference model
Now
Next
Remember this slide?
test inputs
drivers
DUT
ref model
scoreboard
(compare
==?)
Verification environment

## Slide 40: What if we don’t know
No right time → checked at end of test or sooner
What about no right data?
  How might we check for this within our strategy of checking against a reference model?
  Have the reference model return an X?
New idea
  a self-checking test decides pass/fail by itself
  doesn’t need a reference model to compare to!
But how can that be?

## Slide 41: Reversi
Reversi is an environment to verify CPUs
Observations
  How much is 4+3-3? Clearly 4
  How much is 4+x-x? Still 4, independent of x
  Yeah, so what?
Reversi strategy to verify add, subtract:
  load all registers with random values, remember what they are
  create instructions to add a random value from any register, subtract the same one
  randomly reorder those instructions
  run the test
  check the the register values haven’t changed
Don’t need a reference model!
make a nice animation

## Slide 42: Reversi
Clever?
Sure, but there’s a lot more to testing a CPU than just add/subtract?
Could it work for floating-point add/subtract?
  Only if you accept a “close-enough” answer… really not great
Floating-point mpy/divide?
Load & store?
Branches?
Does it fix our problem of what to do for undefined results?
Notes: Mpy/divide is similar to FP add/subtract, of course.
Load/store are as easy as integer add/subtract.
Branches actually work too (though they’re harder).
It doesn’t really fix our problem in general – but it shows that a self-checking test is possible. We will still need specific solutions for specific undefined cases.

## Slide 43: Outline of this lecture
Intro
No right time
No right answer
Reference models
Self-checking tests
Implementation

## Slide 44: Strategy & implementation
We’ve talked a lot about what to do
Next up – some implementation details
  which parts of our testbench do what, and why?
  it’s all about minimizing work: reuse, software layers
DUT
monitor
monitor
checker
checker
driver
high-level stimulus
high
low
Notes: Note there’s no scoreboard on this picture yet – that will come in a few slides

## Slide 45: Monitors
A monitor does
  observes data
  packages it for consumption
  abstracts bits → signals → transactions
A monitor does not
  do the checks
DUT
monitor
monitor
checker
checker
driver
high-level stimulus

## Slide 46: Checkers
A checker does
  take abstracted data from a monitor
  do the actual checks
  may include assertions, instantaneous checks, pipeline checks (built up over time)
A checker does not
  do the data abstraction
DUT
monitor
monitor
checker
checker
driver
high-level stimulus

## Slide 47: Layered system
Why bother with two layers?
  the usual reasons!
  allow people work productively without knowing the entire system
  allow reuse of checkers even if implementation changes
  simplify via reuse – one monitor can feed multiple checkers
DUT
monitor
monitor
checker
checker
driver
high-level stimulus

## Slide 48: Ref model
Where do we put a reference model?
  Do we want it to be at a high or low level?
DUT
monitor
monitor
checker
checker
driver
high-level stimulus
ref model
ref model
Notes: Start the discussion; what are the pros/cons of each choice?
High-level RM makes it easier to reuse as pinouts change from generation to generation; low-level RM probably means less total code for any given project. So the question – will the interface change from project to project?

## Slide 49: Ref model
DUT
monitor
monitor
checker
driver
high-level stimulus
ref model
scoreboard
Where do we put a reference model?
  Do we want it to be at a high or low level?
Notes: Another interesting note – one might argue that in this case, the SB is really just a fancy checker.

## Slide 50: Ref model
Where do we put a reference model?
  Do we want it to be at a high or low level?
DUT
monitor
monitor
checker
checker
driver
high-level stimulus
ref model
scoreboard

## Slide 51
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
This is the mesh (from mesh.pptx)
It contains 3 FIFOs
Notes: This slide is just a lead in to the next slide

## Slide 52: Reuse
Remember our FIFO testing?
  cycle-accurate scoreboard
  assertion checkers for no read/empty or write/full
Should we reuse the FIFO scoreboard and checkers when we test the full mesh?
Notes: The argument for no – because it takes time, and verification cycles are a scarce resource
The argument for yes for the assertion checkers – because read/empty or write/full are things that the mesh would do illegally, and if it does so then we want to catch it immediately. Removing those checkers will make a mesh-test failure harder to debug – or even worse, maybe a test will pass even though it’s doing something illegal.
But the argument for keeping around the FIFO scoreboard is somewhat less strong.

## Slide 53: BACKUP

## Slide 54: Reference model is too…
3. hard to write?
  what if it takes as much work to write the ref model as the DUT?
  How common might that be?
  DUT is a protocol handler
  the protocol is complex & the scoreboard would roughly be the DUT!
4. slow to run?
  Maybe you could do a reference model, but it would be too slow
  Sound weird? We’ll talk about post-silicon verification later