## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
joel.grodstein@tufts.edu
staylo20@tufts.edu
Building a FIFO

## Slide 2: Building a FIFO
FIFO = First In First Out
  Think of the line at a supermarket!
  But how do we build one?

## Slide 3: FIFO, take 1
Just four flops in a row
in
out
Is this a FIFO?
Is it a very good one?
D Q
D Q
D Q
D Q
Notes: Well, yes – it is a FIFO
But not a good one. It takes four cycles to get through even if you’re the first person in line!

## Slide 4: FIFO, take 2
D Q
D Q
D Q
D Q
Literally build the supermarket line
Input can hop right to the register if nobody else is in line
Otherwise, go to the end of the line (wherever that is)
Not shown – logic to keep track of who’s in line

## Slide 5: FIFO, take 3
Doesn’t quite mimic an actual supermarket line
But the mux control might be easier
You’ll do this to build your testbench scoreboard
in
out
D Q
D Q
D Q
D Q
flop0
flop1
flop2
flop3

## Slide 6: FIFO, take 3
Problems
  Hard to track who’s in what position
  Too much data movement!
  Doesn’t work with memories
in
out
D Q
D Q
D Q
D Q
flop0
flop1
flop2
flop3

## Slide 7: FIFO, take 4
Drawn as circular ring of flops
  hookup of write data to all D inputs not shown
  ditto for read data from all Q
Really a register file!
  FIFO input can write one location / cycle
  FIFO output gets read data from one location / cycle
D Q
D Q
D Q
D Q
Rd
Wr
in
out

## Slide 8: Example
FIFO starts out empty
Rd* = Wr*
Write 6
D Q
D Q
D Q
D Q
Wr
6
Rd

## Slide 9: Example
Write 7
D Q
D Q
D Q
D Q
Wr
6
Rd
7

## Slide 10: Example
Read → 6
D Q
D Q
D Q
D Q
Wr
6
Rd
7

## Slide 11: Example
Read → 7
FIFO is empty again
D Q
D Q
D Q
D Q
Wr
6
Rd
7

## Slide 12: Example
Write 8
D Q
D Q
D Q
D Q
Wr
6
Rd
7
8

## Slide 13: Example
Write 9
D Q
D Q
D Q
D Q
Wr
6
Rd
7
8
9

## Slide 14: Example
Write 10
D Q
D Q
D Q
D Q
Wr
6
Rd
7
8
9
10

## Slide 15: Example
Write 11
FIFO is full
Problem: how to tell empty from full?
D Q
D Q
D Q
D Q
Wr
Rd
7
8
9
10
11
Notes: With two-bit read and write pointers, there is *no way* to distinguish empty from full based on just the pointers.

## Slide 16
What’s missing?
  Clock, reset (what needs to be reset?)
  Outputs for Empty, Full
Regfile
Rd ptr
(2-bit ctr)
Wr ptr
(2-bit ctr)
Data_in
Data_out
WR
RD
Notes: The two counters must be reset; the regfile doesn’t (and typically cannot be).

## Slide 17
Trick for empty, full
  Empty = (rd_ptr[2:0] == wr_ptr[2:0])
  Full = (rd_ptr[1:0] == wr_ptr[1:0]) && (rd_ptr[2] != wr_ptr[2])
Drive regfile with only [1:0]
Now for an example to convince you that it works
Regfile
Rd ptr
(3-bit ctr)
Wr ptr
(3-bit ctr)
Data_in
Data_out
WR
RD

## Slide 18
Write 6
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
000
000
Empty=
Full=
1
0
6
0
0
001
X
6

## Slide 19
Write 7
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
001
000
Empty=
Full=
6
0
0
010
7
6

## Slide 20
Read → 6
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
000
Empty=
Full=
6
0
0
010
7
001
6
7

## Slide 21
Do another Read → 7
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
001
Empty=
Full=
6
0
0
010
7
010
7
1
0
X

## Slide 22
Write 8
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
Empty=
Full=
6
1
0
010
7
010
X
0
0
8
011
8

## Slide 23
Write 9
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
Empty=
Full=
6
011
7
010
0
0
8
100
8
9

## Slide 24
Write 10
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
Empty=
Full=
6
100
7
010
0
0
8
101
8
9
10

## Slide 25
Write 11
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
Empty=
Full=
101
7
010
0
0
8
110
8
9
10
11
0
1