## Slide 1: EE 194 Synthetic Biology
Fall 2018
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lecture 2: Single-input modules

## Slide 2: What will we learn
Single-input module
  A collection of gates that, viewed as a system, has only one input!
But we’ve already seen inverters and buffers. What else is there?
  timing: yes, one input seems to have limited usefulness. But we’ll get lots of mileage from timing
  setpoints: we’ll build systems with negative feedback to get (among other things) homeostasis
  memory: we’ll use positive-feedback single-input modules to build memory circuits (but not until the next lecture)
Today we’ll mostly just look at examples from nature

## Slide 3: Reference
An Introduction to Systems Biology: Design Principles of Biological Circuits, Uri Alon
On reserve at Tisch

## Slide 4: Circuit #1
Any idea what it does?
  Logically, it’s just a buffer: out=in. What?!?
  With the signal name “dly,” any ideas?
in
dly
out

## Slide 5
in
dly
out
Output pulse:
  shorter than the input
  only turns on if the input stays on for a while

## Slide 6
Pulse shrinkers are common in cells. Why might we want one?
  Any time an action is expensive, and the cell wants to only do it if an input is definitely present.
See Alon page 55 for a nice usage example.
  E.coli arabinose pathway: active when arabinose is present but not glucose
  Glucose is easier to metabolize (similar to Lac operon)
  As E.coli is swimming around, it may pass by transient regions of arab & !glucose – don’t want to turn on the expensive machinery unless the region is big

## Slide 7: Next SIM example
What does this circuit do?
  Logically, the output is always zero!
Think in terms of delays again
in
dly
out

## Slide 8: Next SIM example
Questions:
  why might a one-shot be useful?
  Will there be a pulse when ‘in’ falls?
  How might we get the pulse on ‘out’ to be higher than 35?
  What controls the width of the pulse?
in
dly
out

## Slide 9: But why do we care?
Input arrives:
  you create a pulse of an enzyme that builds a structure to deal with the input
  enzyme goes away shortly, since the structure will be fully built
And for another example…

## Slide 10: JIT
A sequence of buffers, each tap driving a pulse generator.
What do you think it does?
in
in_d2
in_d1
out1
out2
out3

## Slide 11: JIT
in
in_d2
in_d1
out1
out2
out3
pulse
generator
pulse
generator
pulse
generator

## Slide 12: Just-in-time manufacturing
What is JIT manufacturing?
  Each assembly-line input is delivered to the plant just before it is ready to be used
  Minimizes warehouse storage space
  Plus, some resources might spoil over time
Bacterial-chemotaxis example (Alon):
  Bacteria needs to swim to find food, and to change direction when needed
  This requires flagella, which self-assemble in multiple steps
  Each step requires an enzyme; enzymes appear just in time
  Enzymes break down over time

## Slide 13: Autoregulation
Autoregulation: a protein serving as its own TF
  its own activator → positive feedback. Can make memory (unit #3) or robust oscillators (unit #4).
  its own repressor → negative feedback. Let’s see why
LacI
LacI

## Slide 14: So what?
Lets the cell robustly control protein concentration
Creates homeostasis
  LacI↑  more repression  slower mRNA creation LacI↓
  LacI↓  less repression  faster mRNA creation  LacI↑
LacI
LacI

## Slide 15: Autoregulation
Multiple sims plotted on one graph
Each sim starts with a different [protein]
Over time, they all reach the same endpoint
Very much like QSS

## Slide 16: Autoregulation in nature
E.coli transcription network: 424 nodes, 519 edges
  Node = 1 operon. 519 edges is about 100 unique TFs
  Mutations are frequent  every arrow is a miracle 
  Random connections  about 1 self loop
  E.coli has 40 self loops! (34 are negative FB)
  So negative FB must be useful and practical (at least for E.coli)
in
dly
out
in dly out