## Slide 1: EE 193 – Embedded Medical Devices
Fall 2023
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Pan-Tompkins-Charles algorithm

## Slide 2: Today’s problem
Given an ECG:
  Find the QRS complex
  Compute the heart rate (HR)

## Slide 3: First-try algorithm
Find the peaks (using a derivative)
Peak at >1v  QRS
Then HR is easy
Problems?
  Everyone’s voltage is different
1V

## Slide 4: Algorithm v2
Get running high and low peaks over 10 seconds
Threshold = low + .9*(high-low) / 2
Any peak > threshold  QRS
Any problems with algorithm v2?
high
low
threshold

## Slide 5: 60Hz noise
Get running high and low peaks over 10 seconds
Threshold = low + .9*(high-low) / 2
Any peak > threshold  QRS
Any problems with algorithm v2?
SHOW AN ECG WITH 60HZ NOISE!!!???
high
low

## Slide 6: RBBB
RBBB ECG typically has two distinct peaks
  First is the small partial peak from RBB conduction
  Next is the bigger peak from LBB wraparound
SHOW MY RBBB ECG WITH TWO PEAKS!!!???
high
low

## Slide 7: Baseline drift
SHOW A BASELINE DRIFT ECG
Drift may be too fast for the algorithm to keep up
high
low
threshold

## Slide 8: Algorithm v3
Get running high and low peaks over 10 seconds
Threshold = (low + high) / 2
Any peak > threshold  QRS except if it’s in the lockout period
How do we set the lockout period?
Max HR of a 20 year old  200 beats/minute
  200 beats/minute = 60 sec/200 beat = .3 sec/beat
  So lockout for, say, .25 sec after any QRS
Does it work now?
In-class exercise

## Slide 9: Weird ECGs
Show a tall P or Q giving a fast HR
Exercise on your own: will lockout fix this?
Onto the “real” algorithm
In-class exercise

## Slide 10: Pan Tompkins Charles
1985: Jiapu Pan and Willis Tompkins published original algorithm
2023 Charles modified it for this course (unpublished)
  Working as an independent study
  Used Joel’s ECG, and got it to work just before the summer ended

## Slide 11: PTC idea #1
Keep the running min peak & max peak
Each new peak of height h
    min_peak = min (min_peak, h)
    max_peak = max (max_peak, h)
    thresh = (min_peak + max_peak) / 2
Every 2ms
    min_peak += delta
    max_peak -= delta
This one is from C (PT had a different scheme)

## Slide 12: PTC idea #2
Work in two tracks
  Track #1 is what we described. And track #2 is…
QRS is not only tall, but also pointy
  “Pointy” means high slope = high derivative
Process the signal with
  deriv_sq = (d(signal)/dt)2
  run_avg = running_avg_over_200ms (deriv_sq)
  then do the same peak detect + min/max/thresh + lockout as in track 1
Only declare QRS if both tracks have a peak above their threshold at the same time

## Slide 13: PTC pros and cons
Pros
  The “PT” part has been tested for over 35 years
  Unknown how much commercial usage
Cons
  The “C” part was done with a looming deadline
  Hence, tested on only one ECG (Joel’s)
Will it work on yours? If not, you get to fix it 

## Slide 14: Tour of the code
Look at main.c for lab #6

## Slide 15: Block diagram
sample
filtered
peak_1
thresh_1
peak_2
thresh_2
deriv_2
deriv_sq_2
avg_200ms_2
biquad filter
peak detect
moving threshold
5-point derivative
square
running average
peak detect
moving threshold
input > thresh
input > thresh
!refractory
dual QRS