## Slide 1: EE 193 – Embedded Medical Devices
Fall 2023
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Basics of embedded systems – part 2, O/S

## Slide 2: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 3: Operating systems
Our first in-your-face issue with embedded systems: no keyboard or monitor
Our second one: “what about the O/S?”
Who can roughly define the term “operating system?” Name a few desktop or phone O/S?
Which do you think run on most embedded systems?
  Often none!
  Huh? But an O/S is kind of useful, isn’t it?
Notes: A few popular O/Ss: Linux, Unix, Windows, IOS, Android, …

## Slide 4: What does an O/S really do?
Who remembers what kinds of things an O/S does?
  manage multiple users/threads. Tricks them into each thinking they own the machine
  files; paging/VM
  attach your keyboard/screen to a window(s)

## Slide 5
What an O/S does
  manage multiple users/threads Tricks them into each thinking they own the machine
  files; paging/VM
  attach your keyboard/screen to a window(s)
Which of those functions do we need on the Disco?
Do we really need an O/S?

## Slide 6: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 7: Bare metal
Cross-compile on the host  ARM binary
Download binary  Disco flash
Disconnect the board
Ship to customer. Turn it on  runs from flash
Host
USB
Bare metal is ≈ 26% market share
  it means no O/S at all!

## Slide 8: Bare metal
Bare metal = board boots to your program
What do you think are pros and cons?
  An O/S takes up flash space, so no O/S is cheap
  Files are useful (but our program can write/read flash)
  Multiple threads may be useful (more on that later)
  We have no “boot to a shell, where you can run any program you want” – but our embedded system only runs one program, anyway

## Slide 9: Linux?
What about Linux (or Windows)?
  Mainstream Linux needs 10GB hard drive and virtual memory
  STM32L476 has 1MB on-die flash
  Microcontrollers rarely support virtual memory
  So no mainstream Linux (or Windows!)
  “Tiny” versions can be down to 500KB
Notes: So even a tiny Linux is taking half of our flash. And we’ll do a comparison to FreeRTOS soon – which takes only about 7KB.

## Slide 10: Virtual memory
Virtual memory lets two users use the same hardware
Compile your C program
    extern a = 5
    a = a + 1
Compiler gives you, e.g.,
    mem[1000] = mem[1000] + 1
What if two users run this program at the same time?
  Do they each see a wind up as 7?
  How about three users?
It actually works fine – because of virtual memory
Notes: OK, most assembly languages won’t let you add 1 directory to memory. But I’m just keeping it simple

## Slide 11: Virtual memory
Virtual memory maps
address in your program
your user ID
actual address
Memory manager
virtual address | user # | physical address
1000 | 0 | 10000
1000 | 1 | 20000
1000 | 2 | 30000
Can’t really do a multi-user system without VM
Most microcontrollers don’t support VM
Notes: In fact, some might say that the definition of a microcontroller (as opposed to a microprocessor) is that it doesn’t support VM

## Slide 12: Exceptions
Anyone know a cheap-ish hobbyist Linux-ish board?
  Raspberry Pi
But how do they do it?

## Slide 13: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 14: Raspberry Pi use model
Remember our use model
Host
USB
Raspberry Pi is very different

## Slide 15: Raspberry Pi hardware
This is a single-board computer
Uses SD card instead of flash (the “hard drive”)
Power
SD card (holds O/S)
HDMI monitor
4x USB
LAN

## Slide 16: Raspberry Pi O/S
Raspberry Pi O/S is Linux
  Variant of Debian Linux
  All of the bells and whistles of Linux
  Class exercise: what are the consequences of that?

## Slide 17: How can a Pi run “Linux?”
 | Bits | Cores | MHz | On-chip flash | VM | Peripherals
STM32L476 | 32 | 1 | 80 | 1MB | No | tons
Broadcom BCM2837 | 64 | 4 | 1200 | ??? | Yes | few
Way more powerful CPU
But to avoid going over budget, few peripherals
  No analog GPIO pins; timers are few and simple
  Fine for hobbyists; they buy shields
  Hobbyist volumes can afford a few extra bucks, space
Requires ≥16GB SD card
Notes: The Pi specs are for a Raspberry Pi 3b (the 3b+ is1.4GHz rather than 1.2GHz)

## Slide 18: Raspberry Pi pros/cons
Pros
  fast, “cheap” ($35 for Pi 3b) computer
  can program it in your favorite language with your favorite editor
  fast enough to run Python easily
Cons
  STM32 = $1 to $10 or so
  standalone use without monitor or keyboard is hard (but can SSH in via ethernet or wireless)
  not a lot of peripherals (you need shields)
  bigger form factor than you may need (esp. w/shields)
  Needs ≥16GB SD card
  It’s not an RTOS (what???)

## Slide 19: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 20: RTOS
RTOS = Real-time O/S
The most popular one is called FreeRTOS
Any guesses why it’s the most popular? 
  Open source
  “Owned” by Amazon Web Services
  Can pay for support, and for FDA-friendly version

## Slide 21: RTOS
Pared-down bare-bones O/S
  No file system, VM  about 7KB!
  FreeRTOS gives you threads + inter-thread comms
  gives you alloc(), free() (but see later…)
  gives you real-time “guarantees”
Why do we care about threads?
  About ¼ of projects are bare metal and ¾ are RTOS
  Multiple threads are good (labs will show us why)
  Lets you put different functionality in different threads, making your code more modular

## Slide 22: RTOS superpower
RTOS can work in real time
Why does this matter? What embedded systems might need real-time response?
  Pacemaker, neural prosthetic, anti-lock brakes, …
A few definitions
  soft RTOS  almost always meet a deadline
  hard RTOS  meet a deadline deterministically
Notes: What does “deterministic” mean in this context? You yourself can write bad code that results in deadlines not being met. But at least the RTOS is deterministic, and good code on your part can work. The main thing that would cause an RTOS to not be deterministic is garbage collection.

## Slide 23
Slightly interesting opinions
https://www.embedded.com/are-all-rtoses-equivalent
https://www.embedded.com/why-a-bare-metal-developer-moved-to-operating-systems
https://www.embedded.com/how-to-select-your-embedded-systems-operating-system-selection-guidelines

## Slide 24: So many infrastructures…
How many embedded-programming environments can you think of?
  Arduino, Raspberry Pi, MicroPython, CircuitPython
  STM CMSIS, LL, HAL
  Infineon PDL, HAL
  C vs. C++ vs. assembly
Remember this?
Which of these counts as an O/S?
Notes: Hopefully this is an easy question to answer

## Slide 25: What we’ll cover & how
Main topics:
  What is an O/S and why is it useful?
  Living with no O/S: bare metal
  Raspberry Pi
  RTOS overview
  FreeRTOS details (prep for lab 2)

## Slide 26: Tour of FreeRTOS
Next up: enough FreeRTOS details to get you through lab #2

## Slide 27: FreeRTOS tasks
Concept #1: tasks
A task is (roughly)
  the basic thing that runs in FreeRTOS
  what the scheduler schedules
  others call it a thread (or, wrongly, a process)
Three tasks in lab #2
  green LED blinker
  red LED blinker
  UART
Any guess what the green LED blinker task does?

## Slide 28: UART
UART = Universal Asynchronous Receiver and Transmitter
Host
USB
Disco kit
serial to USB
476
UART
1B parallel
1b series
UART
Notes: UART takes 1B all at once and ships out 1b at a time (or vice versa).
USB changes from the simple UART format to the very complex USB format.
There’s a host-side USB chip too.

## Slide 29: UART for output
We write 1B to the UART
  it sends out 1b at a time to Disco USB
  Disco USB sends out 1b at a time to host USB
  serial term (Moba or other) on host prints
Disco kit
serial to USB
476
UART
Look at USART_Write() in UART.c
  it takes multiple bytes and spin-waits

## Slide 30: UART for input
Host terminal waits for keyboard input (one char)
Sends one char over USB to Disco kit
Disco kit USB chip receives 1B, serializes it
UART on 476 reassembles it as 1B
Look at USART_read()
  mostly just a big spin-wait loop
  can wait a long time for a keystroke!

## Slide 31: FreeRTOS and UARTs
Why are we talking about UARTs in the FreeRTOS slides?
Sending text to a screen helps us debug
  the sooner we learn that the better!
More tasks equals more fun on lab 2 
  UART will be a third task
Lots of spin waits in UART drivers
  FreeRTOS can help us multitask while we wait

## Slide 32: Create a FreeRTOS task
TaskHandle_t task_handle_red = NULL;
BaseType_t red_status = xTaskCreate (
      task_blink_red, // name of the task function
      "Blink Red LED", // for debugging
      100, // stack size in words
      NULL, // parameter passed into task
      tskIDLE_PRIORITY, // priority
      &task_handle_red);
if (red_status != pdPASS) …
Notes: The task handle is typically unused, but could be used to edit the task properties.

## Slide 33: More “what is a task?”
We haven’t really said exactly what a task is yet!
  We said “tasks are the things FreeRTOS schedules”
FreeRTOS makes it look like all these tasks are happening at the same time
  Of course they’re not
  We only have one core; only one thing can run at a time
  But we switch back-and-forth really fast

## Slide 34: Multitasking & the scheduler
Any examples of multi-tasking in your daily life?
  Daydreaming while listening to a boring lecture?
  Listening to music while studying?
Every multi-user OS does that
  A real time OS gives us more control on the switching
  Let’s talk about how that works
Notes: I can’t really listen to music and concentrate any more… not even when driving

## Slide 35: Scheduler in a nutshell
The heart of an RTOS is a scheduler
The scheduler…
  has a list of all tasks that want to run
  picks the highest priority one
What if there are several tasks ready to run at the same priority?
  Take turns (round robin)
xTaskCreate (task_blink_red, …,
      tskIDLE_PRIORITY,
      …);

## Slide 36: Can FreeRTOS hang?
Problem: who runs the scheduler?
  Is it that a task runs the scheduler when it wants to play nice & share the MCU?
If one task wants to run and run and run, and never calls the scheduler, will it succeed?
Will other tasks never execute?

## Slide 37: Who runs the scheduler
That scenario cannot happen
Two ways the scheduler gets control
  FreeRTOS has a tick (1ms for us). Hardware timer ticks every 1ms; interrupts whoever is running and runs the scheduler instead. The scheduler then does its thing to pick who goes next
  A task says I’m stuck until (say) 10ms from now. E.g., vTaskDelay(10)  pause me for 10 ticks
  Note it’s in ticks (and for us, 1 tick = 1ms)

## Slide 38: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Blinky starts running (it’s the high-priority task)
  Flips the GPIO pin
  Calls vTaskDelay(2) long before tick #1 occurs
  Will sleep 2 ticks (so, until tick #2)
0 1 2 3 4
Notes: Because we switch to the scheduler with an interrupt, we can return to the interrupted task. It takes a bit of doing (since usually we unroll the stack in LIFO order and the scheduler can instead do what it wants).
Also be sure to show the difference between preemption and cooperation.

## Slide 39: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

vTaskDelay(2) calls the scheduler
Control passes to , which computes happily along
0 1 2 3 4

## Slide 40: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Next tick interrupt happens (tick #1)
Blinky is blocked until tick #2, so  can keep running
0 1 2 3 4

## Slide 41: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Next tick interrupt happens (tick #2)
Blinky is now unblocked
 is pre-empted, Blinky runs again
0 1 2 3 4

## Slide 42: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Blinky flips the GPIO pins
Blinky calls VTaskDelay(2), sleeps until tick #4
VTaskDelay(2) calls scheduler, returns control to 
0 1 2 3 4

## Slide 43: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

And the beat goes on…
0 1 2 3 4

## Slide 44: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Every tick, the scheduler picks the highest-priority unblocked task
Calls to vTaskDelay() and other FreeRTOS kernel functions can re-schedule mid-tick
0 1 2 3 4

## Slide 45: Blinky and 
Two tasks:
  Low-priority background computes digits of  forever
  High-priority task blinks LED
Blinky

Thought questions: how would this diagram have changed if Blinkly and  had equal priority?
0 1 2 3 4

## Slide 46: RTOS vs Linux
The whole point of an RTOS
  you pick the timer tick
  you assign priorities
  (you pick the heap algorithm)
Result: you can guarantee mission-critical tasks happen on time
Do ps on a Linux system; so many weird tasks!