## Slide 1: EE 193 Embedded Medical Devices
Fall 2023
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
The human heart

## Slide 2: Table of contents
Cool cardiac facts & why we care
Cardiac basic operation
Electrocardiograms
Arrhythmias
Backup-system engineering
  2 to 3 billion cells; they break and die all the time

## Slide 3: Why do we care?
The next few labs will be measuring our ECG
Heart disease is the #1 killer in the U.S.
The mammalian heart is a super cool, well-engineered system

## Slide 4: Deaths/year in U.S.
2.8M deaths/year total (.9 / 100 people)
  Heart disease = 650K
  Cancer = 600K
  Coronavirus = 188K (9/6/2020)
  Accidents = 170K
  Chronic lower respiratory diseases: 160K
  Stroke = 150K
  Alzheimer’s = 120K
  Diabetes = 80K
Mostly heart attacks
(from https://www.cdc.gov/nchs/products/databriefs/db328.htm)
Notes: “Heart disease” actually includes all cardiovascular diseases.
But “stroke” is counted as a cerebrovascular disease, so it’s separate from heart disease!

## Slide 5
Heart attack = blocked artery starves heart muscle
  Plumbing problem
  Heart dies over hours to weeks
Cardiac arrest = heart stops beating
  Electrical problem
  Lose consciousness in seconds; die in minutes
  530K cases/year; 8% survival rate
  CPR, AED save lives
  PSA – learn how to use one!
one cause

## Slide 6: A miracle of engineering
The heart contains 2-3 billion independent cells
  Cells have high variability
  Cells are quite failure prone
They somehow link together
  to produce a coordinated, durable, and adaptable whole!
  The heart is really really really robust – a miracle of fail-safe engineering
  Multiple backup subsystems
  It’s really robust! Keeps beating and never stops
Except for the 99 varieties of heart disease…

## Slide 7
Galen of Pergamum, 130-200AD
  extracted heart keeps beating for a long period
  nobody knew why
Question: does your heartbeat originate in the brain and get sent to the heart via neurons?
Keith and Flack (1907)
  sinoatrial node initiates the heartbeat
Notes: From Galen’s experiment, we conclude that the brain is not the source of the heartbeat – if it were, the heart would stop beating as soon as we removed it from the body
Keith and Flack first found the SA node on a mole

## Slide 8: Table of contents – this unit
Cool cardiac facts & why we care
Cardiac basic operation
Electrocardiograms
Arrhythmias
Backup-system engineering

## Slide 9: Plumbing – the big picture
Two separate two-chambered pumps
Red = oxygenated
Blue = not
Two chambers = more efficient

## Slide 10: What does electricity do?
Electricity drives the muscles
Muscles drive the plumbing
Similar to the rest of your body
Notes: Of course, in this case the electrical signals are coming from an oscillator rather than from the brain
Note the timing – both atria contract at once, and both ventricles contract at once.

## Slide 11: The pumps in operation
https://www.youtube.com/watch?v=CWFyxn0qDEU
  Mayo Clinic
https://www.youtube.com/watch?v=-s5iCoCaofc
  Suitable for younger than college age 

## Slide 12: Atrial conduction
Sinoatrial (SA) node is the oscillator
Signal spreads over the atria at 1 m/s (100ms total)
  Atrial muscles contract
SA
Notes: Normal atrial conduction

## Slide 13: Conduction on the highways
Through the AV node (slowly)
Zoom through the bundle of HIS, left/right bundle branches
AV
SA
Notes: Normal atrial conduction

## Slide 14: Conduction on the highways
Then the Purkinje fibers
AV
SA
Notes: Normal atrial conduction

## Slide 15: Ventricular conduction
SA
AV
Purkinje fibers have seeded the AP on much of the ventricular surface
Now it squeezes the entire muscle all at once
Notes: Normal ventricular conduction

## Slide 16: Entrainment
Sinoatrial node has ≈ 500K cells
  Each one oscillates independently
  Potentially a slightly different frequency, phase
  How can your heart have a single unified beat?
Entrainment is the process of all the oscillators talking to each other and agreeing on a frequency
  Now it has a name 
  But how does it work?

## Slide 17: Gap junctions
  A resistor between two cells
  Interesting tidbit – it’s a voltage-controlled conductance
Tie oscillators together  force them to sync up
+10mV
-20mV
Cl-
Na+
Na+
Cl-
A gap junction (GJ) is a little tube that connects two cells
  GJs allow cells to talk to each other
Molecules can travel between the two cells
Notes: The GJs are drawn as six little tubes forming a big tube because, in fact, that’s more or less their anatomic structure.

## Slide 18: Mini-quiz
  What does plumbing vs electrical mean?
  What is a GJ?

## Slide 19: Table of contents
Cool cardiac facts & why we care
Cardiac basic operation
Electrocardiograms
Arrhythmias
Backup-system engineering

## Slide 20: What is an ECG?
Measures the heart’s “summed” action potential
Each AP in the cardiac wave → small current travels through the body to the ECG electrodes
Different heart cells are oriented in different directions; vector dot products cause different results depending on where electrodes are attached

## Slide 21: Atrial conduction
P wave = atrium firing
SA
P
Q
R
T
S
AV
Notes: Normal atrial contraction

## Slide 22: Ventricular conduction
AV
Purkinje fibers have seeded the AP on much of the ventricular surface
Now it squeezes the entire muscle all at once
Why is QRS complex taller & skinnier than the P wave?
P
Q
R
T
S
SA
Notes: The tall & skinny contraction is because you have such a strong, well-synchronized set of APs throughout the entire (huge and strong) ventricles.
The reason for the synchronization is because the Purkinje fibers work so well.

## Slide 23: Ventricular recovery
SA
AV
Ventricular recovery
  It takes current to recover from firing, too
  T wave
P
Q
R
S
T

## Slide 24: Electrocardiogram
Locate these
  SA node firing
  atrial firing
  atrial recovery
  ventricular firing
  ventricular recovery
P
Q
R
S
T
How can you read these delays?
  heartrate
  time to traverse atria + AV node
  time to traverse AV node
  total ventricular firing + recovery
Notes: SA node firing is the beginning of P
atrial repolarization is hidden by QRS
time to traverse the atria + AV node = PR interval = start of P to start of QRS
delay through the
AV node = PR segment = end of P to start of QRS. Note the PR interval and segment are perhaps badly named; they end at Q, not at R.
The lab asks for the HR, PR interval and PR segment.

## Slide 25: Table of contents – this unit
Cool cardiac facts & why we care
Cardiac basic operation
Electrocardiograms
Arrhythmias
  so many things can go wrong 
Backup-system engineering

## Slide 26: Atrial conduction – review
Sinoatrial (SA) node is the oscillator
Signal spreads over the atria at 1 m/s (100ms total)
  Atrial muscles contract
SA
AV
Notes: Normal atrial conduction

## Slide 27: Your heart, on AFib
Loop starts at an ectopic pacemaker
Goes round and round with no input from SA node
  Called a reentrant arrhythmia
  May take a slightly different path each time
  Waves spread out from the loop, some go through AV node and trigger ventricles
SA
AV

## Slide 28: Atrial fibrillation
No P wave – why?
HR is irregular – why?
Frequency usually about 150 bpm
  Ventricles pumping inefficiently but still pumping – why?
  You can limp to the phone to call 911
  Lookahead – we’ll talk about another backup system shortly
P
Q
R
S
T

## Slide 29
https://watchlearnlive.heart.org/index.php?moduleSelect=atrfib
Traditionally requires a one-way path
Notes: The question of *why* it requires a one-way path will be on the quiz

## Slide 30: Atrial fib causes
Causes:
  Congenital heart disease of many types
  Sedentary lifestyle (via diabetes, obesity, high blood pressure)
  “Excessive” endurance exercise!
  Exercise is a powerful drug, with a dose/response curve
Cures
  Various drugs
  Ablation
  Rest, sleep or time

## Slide 31: Ablation
Find the ectopic pacemaker
Surgically break the loop
SA
AV

## Slide 32: Ablation
Find the ectopic pacemaker
Surgically break the loop
  Either burn or freeze the relevant heart tissue
SA
AV

## Slide 33: Ablation
Find the ectopic pacemaker
Surgically break the loop
  Either burn or freeze the relevant heart tissue
  Like any procedure, it’s not risk free
Atrial fib: surgery or not?
  https://www.medscape.com/viewarticle/919228
  https://www.drjohnm.org/2011/03/the-best-tool-for-treating-atrial-fibrillation
Anyone have an interesting story?
SA
AV

## Slide 34: Bundle-branch block
What it is
  delay or blockage in left or right BB
Symptoms
  None (majority case)
  Fainting, dizzyness
Causes
  Prior heart attack, bacterial infection, high blood pressure, …
  Genetic
  Too much exercise
Consequences
  often none (explanation shortly)
SA
AV

## Slide 35: RBBB example
Diagnosis: wide QRS complex
  .1-.12s → partial block (not uncommon, especially in endurance athletes)
  >.12s → complete block (less common)
Is this ECG normal, partial RBBB or complete?
Notes: Do the math – there are 5x5=25 squares per second, so each square is .04 sec.
So I would call this about .12s – right on the border between partial and full. However, note that it has been separately read at .144 sec.

## Slide 36: RBBB – not a big problem
SA
AV
The RBBB is mine!
Any reason I’m still alive (and not overly concerned)?
Heart cells are quite interconnected
  Left branch crosses over to drive the right side
  Right side is “just” the lungs anyway 
Notes: Normal atrial conduction

## Slide 37: Group exercise
Why does RBBB cause wide QRS?
Would you expect a left BBB to be more dangerous than right, or less?
Notes: The wide QRS is because you’re still hitting the left ventricle with a nice sharp early pulse. But you’re hitting the right ventricle with a delayed and much less-sharp pulse. Combine the two and you typically get a single wide pulse (or, as we see here, what looks like the summation of two different pulses).

## Slide 38: Table of contents – this unit
Cool cardiac facts & why we care
Cardiac basic operation
Electrocardiograms
Arrhythmias
Backup-system engineering
STOP HERE
The rest of the material is covered in EE/BME 123

## Slide 39: Why have fail-safe circuits?
Remember our intro?
  Cardiac arrest = heart stops beating
  Lose consciousness in seconds; die in minutes
Keeping the heart beating is job #1!
But success seems unlikely
  Cells die all the time
  We just discussed so many things that can go wrong
  Biological cells are unreliable
So why are we alive?
  A miracle of beautiful system-level design

## Slide 40: Electrical system – review
Sinoatrial (SA) node is the oscillator
Signal spreads over the atria at 1 m/s (100ms total)
  Atrial muscles contract
Atrioventricular (AV) node conducts slowly to ventricles (.01-.05 m/s, 80ms total)
  Delay is on purpose
Bundle of HIS, left/right bundle branches
Purkinje fibers (2-4 m/s)
  Electrical highway
  ventricular muscles contract
SA
AV

## Slide 41: Triple redundancy
The main operation is simple – SA node oscillates ≈ 60 bpm
But what if the upstream rhythm breaks?
  Quick review: how can it break?
AV
SA
atria
ventricles

## Slide 42: Triple redundancy
The main operation is simple – SA node oscillates ≈ 60 bpm
But what if the upstream rhythm breaks?
  Quick review: how can it break?
The AV node can also oscillate!
  Now we have a backup in case of atrial fib, AV blocks
  AV-node cells have funny ion channels & are pacemakers
But what if the bundle of HIS, or LBB & RBB are both blocked?
AV
SA
atria
ventricles

## Slide 43: Triple redundancy
The main operation is simple – SA node oscillates ≈ 60 bpm
But what if the upstream rhythm breaks?
  Quick review: how can it break?
The AV node can also oscillate!
  Now we have a backup in case of atrial fib, AV blocks
But what if the bundle of HIS, or LBB & RBB are both blocked?
  The Purkinje fibers can also oscillate!
AV
SA
atria
ventricles

## Slide 44: System-level coordination
Three oscillators; only one is needed
What happens if they all turn on at once?
  chaos 
Can you devise a fail-safe system to control this?
  Requirement: KISS principle (less is more)
  Hint: SA node ≈ 60 bpm; AV node ≈ 40 bpm; Purkinje ≈ 20 bpm

## Slide 45: Normal operation
SA oscillator (60bpm)
Travels through AV node…
AV-node action potentials

## Slide 46: Normal operation
Here’s the next fire if input breaks (40 bpm)
SA oscillator (60bpm)
Travels through AV node…
So the ventricular rhythm gets driven by the SA node
AV-node action potentials
Notes: Funny channels haven’t reached the trigger threshold yet, when the upstream AP comes in through GJs and does hit the threshold.
So the funny channels are nearly irrelevant.
Note the drawing shows upward slope of phase 0 in the AV-node cells being less than that in the SA-node cells, since they have fewer funny ion channels.

## Slide 47
Each downstream oscillator is slower than the upstream one
Downstream ones never fire unless the upstream one is stopped
  Upstream AP comes in before downstream funny channels would cause refiring
  Funny channels are mostly irrelevant – for now
Lippincott, Fig 16.12
SA node: 60+ BPM

## Slide 48: What can go wrong?
Travels through AV node…
What could occur to break this coupling and cause the ventricles to fire from their own pacemaker?
SA oscillator (60bpm)

## Slide 49: If the SA node slows down…
Travels through AV node…
SA oscillator (60bpm)
AV oscillator (40bpm) all by itself

## Slide 50: If the SA node slows down…
AV oscillator (40bpm) all by itself
SA oscillator (38bpm)
Ventricles fire from AV pacemaker
Why doesn’t this fire the ventricles?
Notes: Why doesn’t the second SA pulse cause the ventricles to fire? Perhaps because they’re still refractory to their own second pulse (which has just fired). And if they’re refractory then they don’t fire on the SA depolarization – and if the SA repolarizes (and pulls the AV down) before the refractory period ends then the SA spike gets completely ignored.
The narration: AV pulse #2 does occur (running on the AV 40Hz clock), since the SA is running so slowly.
Then SA #2 doesn’t cause a new AV pulse (since AV is refractory as noted above).
But SA #3 probably does get through.
Note that this sequence has ventricular firing that looks almost exactly like a PVC (which is what we’ll look at next), though slow SA firing is typically

## Slide 51: Design choices
Frequencies:
  SA node ≈ 60+ bpm
  AV node ≈ 40 bpm
  Purkinje ≈ 20 bpm
Why did we get designed the way we did?
Pros/cons of
  AV node ≈ 45 bpm, Purkinje ≈ 25 bpm?
  AV node ≈ 35 bpm, Purkinje ≈ 15 bpm?
Notes: If the 40 creeps up much higher, an athlete with 45bpm resting pulse will be in trouble.
If the 20 bpm goes much lower, it’s not enough to keep you alive.

## Slide 52: PVCs
SA oscillator (50bpm)
Ventricular AP
Ectopic* focus
A random firing in the ventricles
Ventricles not full; little blood pumped
Doesn’t go anywhere (ventricles still refractory)
Premature Ventricular Contraction (PVC) sounds like a “skipped” pulse
*Ectopic=in the wrong place
Notes: We’re (mistakenly) assuming zero delay from SA to ventricles to make the drawing simpler. In reality, the ventricular AP should be shifted to the right a bit.
And as usual, my artwork isn’t great – a real ventricular AP has a flatter top than what I’ve drawn.

## Slide 53: PVCs
SA oscillator (80 bpm)
Ectopic* focus
could happen
SA oscillator (50 bpm)
Why are PVCs more likely with lots of endurance exercise and little sleep?
  lots of exercise → HR lowers (well known)
  lots of stress → more ectopic foci (hypothesized)
  benign except if you overdo it for a long time
Notes: The red zone is where an ectopic focus could cause a PVC. Really, the important thing is the ventricles and not the SA oscillator, but I drew it this way because it’s the SA oscillator that’s controlling the rhythm and thus setting the HR in the ventricles.

## Slide 54: PVCs
Backup circuits are great – what if they break?
  Yes, you have no backup. Or...
Backup circuit launches when it shouldn’t
  one way to make an ectopic focus
Too much exercise = more PVCs?
More info:
  https://www.drjohnm.org/2013/06/benign-pvcs-a-heart-rhythm-doctors-approach/
  https://www.drjohnm.org/2015/08/on-pvcs-think-anew-but-think-slowly/

## Slide 55
“The current record for number of dominoes toppled in one cascade is just shy of 4.5 million, a record set in the Netherlands on Domino Day 2009. It took a team of 89 builders 2 months to set up! Because a misplaced foot or finger could easily trigger the entire array, it had to be designed with breaks that were completed immediately before the competition began
Because the myocardium does not have such safety features, every cell in the heart has the potential to become the primary pacemaker should its membrane become unstable. “Ectopic” pacemakers are responsible for common mishaps leading to premature ventricular contractions, which are typically one-off events in young, healthy hearts. In aging hearts, ectopic pacemakers may become established, posing a constant and potentially lethal threat to cardiac function.”
Lippincott’s Physiology, 2nd edition, Chapter 16

## Slide 56: Can you find the PVC?

## Slide 57
Do you think that PVCs would get more or less frequent as HR rises?
  More while you’re exercising?
  Or while sleeping?
Notes: This should be an easy question to answer; we just answered it about 4 slides ago!

## Slide 58
Bigeminy: 2 consecutive PVCs
Trigeminy: 3
Conclusions?
Notes: And yes, the most PVCs (206) came at 4am, when the HR was lowest (44).
The bigeminy and trigeminy, interestingly, were not in that period; I’m not sure why. But they were in how-HR periods.

## Slide 59: Electrical control of HR, BP
Sympathetic nervous system increases heart rate:
  releases norepinephrine, which helps to open HCN channels and thus speed up phase 4
  it also makes the AP triggering voltage more negative
Parasympathetic nervous system slows HR:
  releases acetylcholine, which decreases [cAMP]
  does the opposite of the above
Baroreceptors: arterial stretch receptors
  detect changes in arterial pressure and communicate this to the medulla oblongata in the brainstem
  … which then controls heart rate as described above, as well as changing circulatory muscle tone
  End goal: feedback loop controlling blood pressure
  Salt seems to affect it; nobody knows why
  Your brain is the mysterious box controlling it all

## Slide 60: CVRx
Barostim-NEO device
  one in three high-blood-pressure patients is resistant to drugs
  they are the target audience
Mechanism:
  activate baroreflex; reduces sympathetic activity and increases parasympathetic activity
Results:
  http://www.barostimtherapy.com/en-gb/node/86
  FDA approval Aug 2019 (implantable device)
  Medicare/Medicaid approval 2020
Also used for heart-failure patients
  Often, too much sympathetic (too little para) activity causes pathological myocardial remodeling that worsens the condition

## Slide 61: Mini quiz
  Why is QRS tall and skinny?
  What is AFib?
  Describe the redundancy system

## Slide 62
a