## Slide 1: EE 193 – Embedded Medical Devices
Fall 2023
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Flash tour of DSP

## Slide 2: What we’ll cover
Main topics:
  Why do we care about DSP
  The frequency domain
  Building DSP filters
  Cascading DSP filters

## Slide 3: Why learn about DSP?
Today’s lecture: digital signal processing (DSP)
The usual question: why do we care? What does DSP have to do with embedded medical devices?
Answer: the world is a noisy place!
  The signals we read typically have a low signal-to-noise ratio
  DSP can often remove the noise without losing the signal
What are some noise sources?
Notes: Some common noise sources: 60Hz noise everywhere; road vibration in an ambulance; lots of electrical equipment in a hospital.

## Slide 4
Show my ECG sitting at a desk: slide_4()
In-class exercise: measure the noise frequency
Any idea what the noise is?
Goal: keep the baby, throw away the bathwater
  Only possible if you can tell one from the other!
Often frequency is the distinguishing factor
  If so, a filter can keep the signal, remove the noise
Notes: This lecture uses the file 4_DSP_lecture_aid.py. It’s in dropbox\ee_115\lectures_pptx.
The noise is 60Hz powerline hum. Zoom in to count it.

## Slide 5: DSP is great!
Throwing away the bathwater is magic
EE 125 is a full semester DSP course
Today’s lecture, rephrased
  Many embedded systems live in noisy environments
  Learn just enough DSP to clean them up
And maybe convince you to take EE/ME 125 
Some short videos
  https://www.youtube.com/watch?v=spUNpyF58BY
  https://www.jezzamon.com/fourier

## Slide 6: What we’ll cover
Main topics:
  Why do we care about DSP
  The frequency domain
  Building DSP filters
  Cascading DSP filters

## Slide 7: The frequency domain
Most filters are best understood in the frequency domain: e.g., remove the 60 Hz noise
What does a “frequency domain representation of a signal” even mean?
  Covered in BME 10, ME 31, EE 20-23
  We’ll review a bit right now

## Slide 8
Do my 10 and 15 Hz example: slide_8()
Play with the weighting factors to pick just 10Hz, just 15 Hz, and weightings
We see the analog sum and the DFT
Conclusion
  With weighted sum, it’s not obvious from the time plot what the coefficients are!
  But it’s very obvious from the DFT

## Slide 9: Arbitrary signals
If your signal is just the sum of a few sine waves…
  then a frequency domain representation makes sense
But what if you have an arbitrary signal?
  What does a frequency-domain representation mean?

## Slide 10: DFT of an ECG
Discrete Fourier Transform = DFT
Amazing fact: you can express any signal as weighted sum of sine waves!
Let’s take the DFT of an ECG: slide_10()
Observations about the frequency spectrum?
When we take the inverse DFT, it restores the original signal! Is there something deep about that?
Notes: The big observation: there’s a huge spike at 60Hz. We also have spikes at 180Hz and 300Hz; I don’t know why.
Taking the inverse of a DFT means that the DFT coefficients really do represent everything in the original signal. I.e., the sine waves are a basis function for the original sampled signal.

## Slide 11: Filtering with a DFT
Easy trick: we can “fix” our noisy ECG
  Take the DFT
  Then just zero out the 60Hz component!
  slide_11()
Does the noise problem look fixed?
Class exercise
  Does it look like there’s some 60Hz component to the hypothetical noise-free ECG?
  If so, is that a problem?
Notes: We made a big stride, but it’s not totally fixed. It looks like there’s still a bit of 60Hz-ish noise (maybe 59.5 or 60.5), as well as the 180Hz and 300Hz harmonics.
It looks like there really is some 60Hz signal (though not a ton)
And yes, it’s a problem: you can only remove the noise if you can distinguish it from the signal

## Slide 12: On-the-fly filtering
Next problem…
We can’t take the DFT of the signal until we have the whole signal; but we really want on the fly beat-by-beat processing
  Look at the code for slide_11() to see that
The way to do that is with digital filters

## Slide 13: Skip to the fun part
Time for a “skip all the hard stuff” alert
Skipping…
  Z transforms (DSP version of Fourier transforms)
  Correspondence between Z transform & difference equations
Going straight to…
  using Python to design digital filters
  sticking them into our embedded C program

## Slide 14: Summary so far
What have we learned
You can take any waveform
  express it as the sum of sine waves with a DFT
  zero out any frequencies we don’t want
  re-sum the sine waves to get a cleaner signal
Only useful if your noise is at a different frequency than your signal

## Slide 15: What we’ll cover
Main topics:
  Why do we care about DSP
  The frequency domain
  Building DSP filters
  Cascading DSP filters

## Slide 16: Bandstop filters
A bandstop filter passes all frequencies except for a small band
  We’ll build a 60Hz bandstop filter
slide_16()
How are the results?
How does this filter shape compare to our kill-the-60Hz-band filter?
Notes: Before we made a perfect notch that killed only the 60Hz bin; this one is a bit wider window. And it looks like it works a bit better (but it’s still not perfect).

## Slide 17: Second-order section
y[n] = b0x[n] + b1x[n-1] + b2x[n-2] - a1y[n-1] - a2y[n-2]
x[n]
delay
x[n-1]
delay
x[n-2]
weighted sum
delay
y[n-1]
delay
y[n-2]
b0
b1
b2
y[n]
current input sample
previous input samples
filter output
previous filter outputs

## Slide 18: Code
Look at the Pan-Tompkins code for a single biquad
  (biquad = second-order section)
x[n]
delay
x[n-1]
delay
x[n-2]
weighted sum
delay
y[n-1]
delay
y[n-2]
b0
b1
b2
y[n]

## Slide 19: What we’ll cover
Main topics:
  Why do we care about DSP
  The frequency domain
  Building DSP filters
  Cascading DSP filters

## Slide 20: More poles
We’ve used a single second-order section
  DSP-speak is that we built a two-pole filter
Slide_20() shows a four-pole filter
  implemented as two cascaded second-order sections

## Slide 21: Four-pole implementation
Cascading second-order sections is easy
x[n]
delay
delay
weighted sum
delay
delay
y[n]
x[n]
delay
delay
weighted sum
delay
delay
y[n]

## Slide 22: 2 vs. 4 poles?
More poles equals
  better rejection of the unwanted signal
  slower software and more distortion
  No free lunch!
Notes: The “more distortion” is above our expertise level right now. It’s because the phase of the gain varies by frequency.

## Slide 23: 2 vs. 4 poles?
Four poles is slower – does it practically matter?
Exercise: compute how fast
  CPU = 80 MHz, say 1 instruction every 2 cycles
float xn = (float)sample / (float)( 1 << samplebits );
float yn = co->b0*xn + co->b1*state->x_nm1 + co->b2*state->x_nm2
- co->a1*state->y_nm1 - co->a2*state->y_nm2;
state->x_nm2 = state->x_nm1;
state->x_nm1 = xn;
state->y_nm2 = state->y_nm1;
state->y_nm1 = yn;
Notes: Don’t bother with stalls & such.
Rough guess: 2 cvt to float, 1 <<, 5*, 4+, 4 copy => 16 operations -> 32 cycles -> less than .5usec. So it’s quite fast.

## Slide 24: Cascading filters
A four-pole filter didn’t help us much
But cascading filters of different types can be quite effective
What problems did we see after the 60Hz noise was removed?
  Some 180Hz and 300Hz noise
Any obvious ideas for how to fix that?
Cascade a 60Hz bandstop with 180Hz and 300Hz bandstops

## Slide 25: Baseline drift
slide_25() shows a baseline drift signal
Typical causes
  breathing or other slow, rhythmic body movement
  electrode movement
Remove it with a high-pass filter
  How much did that help?
  Any idea why?
Notes: The original signal had a big peak at 2Hz, with smaller peaks at 1 and 3 Hz. The drift signal is about .5Hz (we added two cycles of drift sine wave to 4 seconds of data).
In our case (which, admittedly, has a made-up drift signal), the high-pass filter distorted the ECG a fair amount.
One problem is that the frequency of the baseline drift is quite close to frequencies that are strongly present in the signal. Another problem is that trying to deal with a .5Hz signal when we only have 4 seconds of data is not easy!
So: another reason why automated analysis is hard!

## Slide 26: Types of filters
Bandstop: kill a band of frequencies
Bandpass: pass a band of frequencies
Low-pass: keep all frequencies below f0
High-pass: keep all frequencies above f0
Can you think of uses for each filter type?

## Slide 27: Two AD8232 boards
AD8232 chip is a bio preamp
  Made by Analog Devices
  Aimed at commercial ECG market
  Add a few R, C  add a bandpass filter
We use a Sparkfun AD8232 board
  Built-in .5-40Hz bandpass filter
  Targeted at hobbyists
Cardiologists want signal up to 150 Hz
  Wideband Sparkfun boards pass .5-150Hz