## Slide 1: EE 193 – Embedded Medical Devices
Fall 2023
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Basics of embedded systems – part 3, languages

## Slide 2: What we’ll cover
Main topics:
  C vs. Python
  Heap and the stack
  C vs. C++

## Slide 3: So many languages
Today’s issue: what language do we write programs in?
What’s your favorite language?
Your current project is programmed mostly in…
Notes: C and C++ dominate everything else. They’re 70% total, and the next competitor is at 5%.

## Slide 4: MicroPython
What is MicroPython?
  “Mostly” Python
  Subset, so the interpreter fits into flash
  Supports 32-bit integers
  Classes for “most” STM32F4 peripheral functionality
  Supports interrupts easily
Original plan for this course
  Teach it in MicroPython
  Gave up on that plan during course development
  Time to dive into why…

## Slide 5: C vs. Python
Anyone have any pros/cons of C/C++ vs Python?
  Python may have faster time to market
  C/C++ are compiled and Python is interpreted
compiler
x86 code
C program
JIT compiler
Python bytecode
Python program
C has slow-ish compilation that generates very fast less-portable code
Python has fast-ish compilation that generates slow but more portable code

## Slide 6: Why do we care?
So C/C++ will run much faster. How does that translate into money?
In the non-embedded world, many people prefer Python. Any reasons why?
  Python can give you shorter time-to-market (large number of open-source libraries out there)
  That’s money too!
Given the pros and cons, why do you think the vote is so lopsided?
Notes: Different people will have different reasons for their choice. But the consumer market is very price sensitive and power sensitive. And the incremental cost of upgrading your existing project to a new MCU isn’t so much higher in C/C++ than Python. And there are nice web-stack libraries for embedded C. But Python *really* uses garbage collection a lot, which is what we’ll talk about next.

## Slide 7
Do a PyBoard demo and show how slow it is

## Slide 8: What we’ll cover
Main topics:
  C vs. Python
  Heap and the stack
  C vs. C++

## Slide 9: The heap is evil
Tech alert – time for a refresher in CS
How many people have taken CS 40?
  a really time-intensive course…
  … but they teach what the heap & stack are
It turns out we care about the heap & stack
  so time to pack pieces of CS 40 into 20 minutes 
small

## Slide 10: Reentrant code
Has anyone heard of the term “reentrant?”
  Typical context: asking if a particular library function is reentrant or not
A function f() is reentrant if you can
  call f() from some function foo()
  interrupt the call in the middle and start running a different task bar()
  And bar() also calls f()
  And it all works fine!
Usually a function is reentrant if it doesn’t modify any global state
Malloc() and free() are rarely reentrant 

## Slide 11: Stack example
Walk through a stack example on the board. Show how
  local variables become stack space
  compiler issues SP-relative addresses so it works
  parameters go on bottom of stack, so called function can access them
  unrolling the stack is trivial
  It works fine for “int foo[4]”

## Slide 12: Heap example
Walk through a heap example
Start with four 64B free blocks
A function requests four blocks of 34B and then frees them
Another function requests one 64B block – time to garbage collect 

## Slide 13: Heap vs. stack – recap
Allocating storage on the stack is dependably fast (most of the work at compile time)
Allocating/freeing storage on the heap can incur garbage collection: unpredictably slow
The heap uses malloc()/free(), which can break if interrupted & re-called
struct foo {int a, b};
void f (struct foo foo1) {
  struct foo f2;
  struct foo *f3=malloc (sizeof (struct foo));
  …
  free (f3)
}
allocated on the stack
allocated on the heap

## Slide 14: FreeRTOS and the heap
Needing to allocate memory dynamically is very common in programming
  but can be dangerous in real-time embedded systems
  no silver bullets
FreeRTOS offers multiple choices
  no heap use allowed after the scheduler starts
  turn off the scheduler during malloc(), free()
  incremental garbage collection (coalesce blocks when they are freed)

## Slide 15: Class exercise
FreeRTOS offers multiple choices
  no heap use allowed after the scheduler starts
  turn off the scheduler during malloc(), free()
  incremental garbage collection (coalesce blocks when they are freed)
For each of the above options
  Which issue does it fix, and at what cost?
  Allocating/freeing storage on the heap can incur garbage collection: unpredictably slow
  The heap uses malloc()/free(), which can break if interrupted & re-called

## Slide 16: C vs. Python
Anyone have any pros/cons of C/C++ vs Python?
  Python may have faster time to market
  C/C++ are compiled and Python is interpreted
  Python does tons of memory allocation on the heap, with automatic garbage collection 
What types of applications might MicroPython be acceptable for?
  Not speed-critical
  Only one thread, or it’s OK to disable thread switches during any memory op (i.e., no fast responses needed)
  Example: point of care 10-minute test (ellume.com)

## Slide 17: What we’ll cover
Main topics:
  C vs. Python
  Heap and the stack
  C vs. C++

## Slide 18: C vs. C++
Remember our Feb 2023 poll? 52% C, 18% C++
What are some pros/cons of C vs. C++?
  Big pro of C++ is that it’s more object oriented
  Usually that’s a big advantage
  Zen of embedded: the biggest strength of C++ is also its biggest weakness
C++ tends to create objects on the heap behind your back
  Any obvious examples?
Notes: The most obvious example is vector; but hidden heap allocation is almost a definition of using objects (since they encapsulate their inner function from you).

## Slide 19: Arrays
A bit of functionality in C and C++
void foo() {
void foo_C() {
  int i[4]={0,1,2,3};
  stuff…;
}
void foo_CPP() {
  vector<int> i {0,1,2,3};
  stuff…;
}
draw the stack and heap in each case

## Slide 20: Summary
In the embedded world, speed is money
  But so is time to market
The heap is slow (garbage collection)
The heap is dangerous (usually not reentrant)
Python does most everything on the heap, with unpredictable garbage collection
C++ promotes encapsulation, which often means behind-your-back use of the heap
Interrupts happen frequently – must make them fast