## Slide 1: EE 193: Parallel Computing
Fall 2017
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Introduction to advanced architecture

## Slide 2: Introduction to advanced architecture
The next 2-3 weeks will cover
  EE126/COMP46, Computer Engineering
  EE194, Advanced Computer Architecture
  all in two weeks 
Why do we care?
  The hard part in achieving high performance is usually getting data to the execution units. So learning about caches is important.
  Most multicore CPUs share their last-level cache. So we have to learn a bit about what that means, and about MESI
GPU vs. CPU:
  GPU gives up OOO, speculative, branch predict
  In return, gets SMT over a very large number of threads
  To understand when to use a GPU, we should know what these words and acronyms mean 

## Slide 3: Disclaimer
First time offering this class at Tufts
Tufts also has Comp 50 – Concurrency
  Not sure how the two courses will play together in the future
Looking for feedback:
  is 2-3 weeks of architecture useful?
  next time around, should we expand it or shrink it?

## Slide 4: Instruction-Set Architecture (ISA)
A simple RISC ISA
  Arithmetic instructions read two operands from registers, do a computation, and write the result back to a register
  Loads read an address from a register, read "memory," and put the result into a register
  Stores read an address and data from registers, and write "memory."

## Slide 5: 5-stage pipeline
We call this a pipeline because the instructions can overlap each other
“Real” pipelines can be 5-40 stages deep.
Fetch instruction from memory
Read operands from regFile (issue)
Do the computation (execute)
Load/store
writeback to regFile

## Slide 6: Pipelined instructions
Notes:
  Fetch, issue, execute, memory and WB are all real physical resources; only one instruction can use a given resource at a given time
  Just like any assembly line: two different cars cannot be at the same station at once
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
load r2=mem[r1] | fetch | read R1 |  | access cache | write r2 |  | 
add r5=r3+r4 |  | fetch | read r3,r4 | add r3,r4 |  | write r5 | 
add r8=r6+r7 |  |  | fetch | read r6,r7 | add r6,r7 |  | write r8
store mem[r9]=r10 |  |  |  | fetch | read r9,r10 |  | store

## Slide 7: Hazards
Hazards occur when one computation uses the results of another
What to do?
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
load r2=mem[r1] | fetch | read R1 |  | access cache | write r2 |  | 
add r5=r3+r2 |  | fetch | read r3,r2 |  |  | write r5 | 
add r8=r6+r7 |  |  | fetch | read r6,r7 | add r6,r7 |  | write r8
store mem[r9]=r10 |  |  |  | fetch | read r9,r10 |  | store

## Slide 8: Stall
Simplest solution is to stall until the data is ready
Compiler solution: rearrange the instructions so that this never happens
How successful will this be?
  Not so easy: dependencies are very frequent
  But compilers can be very smart
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
load r2=mem[r1] | fetch | read R1 |  | access cache | write r2 |  | 
add r5=r3+r2 |  | fetch | stall | stall | read r3,r2 | write r5 | 
add r8=r6+r7 |  |  |  |  | fetch | read r6,r7 | add r6,r7
store mem[r9]=r10 |  |  |  |  |  | fetch | read r9,r10

## Slide 9: Stall
Compiler solution: rearrange the instructions so that this never happens
How successful will this be?
  Not so easy: dependencies are very frequent
  But compilers can be very smart, especially if it can interleave multiple independent computations
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
load r2=mem[r1] | fetch | read R1 |  | access cache | write r2 |  | 
add r5=r3+r2 |  | fetch | stall | stall | read r3,r2 | write r5 | 
add r8=r6+r7 |  |  |  |  | fetch | read r6,r7 | add r6,r7
store mem[r9]=r10 |  |  |  |  |  | fetch | read r9,r10

## Slide 10: Life is harder because…
You never know how long a load will take to happen
  depends whether the data is in cache, and which cache
  makes a compiler's life much harder
Hardware solution:
  out-of-order machine (but the hardware isn't simple)
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
load r2=mem[r1] | fetch | read R1 |  | access cache | write r2 |  | 
add r5=r3+r2 |  | fetch | stall | stall | read r3,r2 | write r5 | 
add r8=r6+r7 |  |  |  |  | fetch | read r6,r7 | add r6,r7
store mem[r9]=r10 |  |  |  |  |  | fetch | read r9,r10

## Slide 11: What else causes stalls?
Branches (e.g., from an "if" statement)
  cannot even fetch the “add” until you know if the branch happened
Hardware solution: speculative machine + branch prediction
  make a guess if the branch will be taken
  unroll everything if you guessed wrong
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
load r2=mem[r1] | fetch | read R1 |  | access cache | write r2 |  | 
branch if r2=0 |  | fetch | stall | stall | read r2 |  | 
add r8=r6+r7 |  |  |  |  | fetch | read r6,r7 | add r6,r7

## Slide 12: Symmetric multithreading
Avoiding stalls is easier when successive instructions have no dependencies
One way to do this: symmetric multithreading (SMT)
  Processor keeps multiple threads ready at all times
  by definition, different threads have no dependencies (they each have their own set of registers)
Whenever a dependency would cause a stall, the machine instantly switches to the other thread without losing any cycles
  and if that thread would stall, it switches to yet another thread, …
  Intel calls this hyperthreading, and only keeps two threads around
Notes:
  I've oversimplified. Real SMT works on superscalar machines, where multiple instructions can issue in one cycle – and then lets instructions from different threads all issue together
  SMT is perhaps a GPU's biggest trick. It's much more than 2-way