## Slide 1: ECEC 194: High Performance Computer Architecture
Spring 2016
Tufts University
Instructor: Prof. Mark Hempstead
mark@ece.tufts.edu
Lecture 3: Memory Hierarchy and Caches

## Slide 2: Outline
Memory Hierarchy
Cache review

## Slide 3: Histogram, done poorly
I wrote a histogram program
  I did a really, really bad job.
  On purpose (mostly)
500M pieces of input data.
int input_vals_per_thread = input_data.size() / n_threads;
for (int i=0, idx=me; i<input_vals_per_thread; ++i) {
  ++my_hist[input_data[idx]];
  idx += n_threads;
}

## Slide 4: Histogram, done poorly
Explanations?
  We’ll revisit this example at the end of our cache tutorial
1 thread | 2 th | 4 th | 8 th | 16 th | 32 th | 64 th | 128 th
1.3s | 1.2s | 1.7s | 2s | 4.9s | 5s | 4.9 | 4.9s
int input_vals_per_thread = input_data.size() / n_threads;
for (int i=0, idx=me; i<input_vals_per_thread; ++i) {
  ++my_hist[input_data[idx]];
  idx += n_threads;
}

## Slide 5
Memory Hierarchy Review
Appendix B and Chapter 2

## Slide 6: Since 1980, CPU has outpaced DRAM
CPU
60% per yr
2X in 1.5 yrs
DRAM
9% per yr
2X in 10 yrs
10
DRAM
CPU
Performance
(1/latency)
100
1000
1980
2000
1990
Year
Gap grew 50% per year
Q. How do architects address this gap?
A. Put smaller, faster “cache” memories between CPU and DRAM.
Create a “memory hierarchy”.

## Slide 7: Memory Hierarchy: Dell with Core i7 (Nehalem)
 | Reg | L1 Inst | L1 Data | L2 | L3 | DRAM | Disk (SSD) | Disk (HD)
Size | 1.25K | 32K | 32K | 256K | 8M | 4G | 120G | 1 TB
Latency Cycles, Time | 1, 0.4 ns | 4, 1.6 ns | 3, 1.6 ns | 11, 4.4 ns | 39, 15.6 ns | 107, 42.8 ns | 5*105 , 200us | 8.7*106, 3.2 ms
Let programs address a memory space that scales to the disk size, at a speed that is usually as fast as register access
Managed
by compiler
Managed
by hardware
Managed by OS,
hardware,
application
Goal: Illusion of large, fast, cheap memory

## Slide 8: Locality is the key
The first time you reference a piece of data, you must fetch it from disk
  Even if you have fast caches
  Because at startup, the data isn’t in those caches
But the next time you reference that same data, you can grab it from your cache.
  Hopefully. But not always.
This is called temporal locality (i.e., one location, referenced repeatedly over time)
  If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)

## Slide 9: Spatial locality
If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
When you access a piece of data for the first time, the CPU actually loads an entire cache line of data into your cache (e.g., 64B)
  The next time you access any data in that line, it gets fetched from the cache, and hence accessed quickly

## Slide 10: The Principle of Locality
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Locality is a property of nearly all programs that is exploited in machine design.
  Programs that don’t actually have locality won’t benefit from caches. Example: copy one column from one matrix to another (for row-major storage)
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 11: Locality Example
j=val1;
k=val2;
for (i=0; i<10000;i++) {
A[i] += j;
B[i] += k;
}
What temporal locality is here?
What spatial locality?
j, k, i
A, B

## Slide 12: Locality applies to instructions
j=val1;
k=val2;
for (i=0; i<10000;i++) {
A[i] += j;
B[i] += k;
}
For the instructions:
  What temporal locality is there?
  What spatial locality?
all of them
the inner loop

## Slide 13: Exploiting Locality: Memory Hierarchy
Hierarchy of memory components
  Upper components
    Fast  Small  Expensive
  Lower components
    Slow  Big  Cheap
Connected by “buses”
  Which also have latency and bandwidth issues
Most frequently accessed data in M1
  M1 + next most frequently accessed in M2, etc.
  Move data up-down hierarchy
Optimize average access time
  latencyavg = latencyhit + %miss*latencymiss
  Attack each component
CPU
M1
M2
M3
M4

## Slide 14: Concrete Memory Hierarchy
0th level: Registers
1st level: Primary caches
  Split instruction (I$) and data (D$)
  Typically 8KB to 64KB each
2nd level: 2nd and 3rd cache (L2, L3)
  On-chip, typically made of SRAM
  2nd level typically ~256KB to 512KB
  “Last level cache” typically 4MB to 16MB
3rd level: main memory
  Made of DRAM (“Dynamic” RAM)
  Typically 1GB to 4GB for desktops/laptops
    Servers can have 100s of GB
4th level: disk (swap and files)
  Uses magnetic disks or flash drives
  10s of GB or over 1 TB
Processor
D$
L2, L3
Main
Memory
I$
Disk
Compiler
Managed
Hardware
Managed
Software
Managed
(by OS)
Regs

## Slide 15: Bigger caches = slower
Each subsequent memory level is slower
L1 cache
L2 cache
regfile
A bigger memory takes longer to access (just common sense, and in fact it's true)
The wires to bigger caches tend to have less bandwidth than those to smaller caches
  They run longer distances, and so having wide busses is more expensive
disk, memory, L3

## Slide 16: Evolution of Cache Hierarchies
Intel 486
8KB
I/D$
1.5MB L2
L3 tags
64KB D$
64KB I$
Intel Core i7 (quad core)
Chips today are 30–70% cache by area
8MB L3
(shared)
256KB L2
(private)

## Slide 17: Cache tradeoffs
Caches have LOTS of transistors; the potential for wasting power is correspondingly huge.
Caches take up lots of area, which implies long wires, and thus unavoidable latencies.
If we try to improve bandwidth by using wider buses or more pipelining, both will (as usual) cost power.
  More details to come.

## Slide 18: Where do misses come from?
Classifying Misses: 3 Cs
  Compulsory—First access to a block. Also called cold start misses or first reference misses. (Misses in even an Infinite Cache)
  Capacity—If the cache cannot contain all the blocks needed during execution of a program, capacity misses will occur due to blocks being discarded and later retrieved. (Misses in Fully Associative Cache)
  Conflict—If block-placement strategy is set associative or direct mapped, conflict misses (in addition to compulsory & capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. Also called collision misses or interference misses. (Remaining Misses)
4th “C”: Coherence - Misses caused by cache coherence.
Notes: Intuitive Model by Mark Hill

## Slide 19: 3Cs Absolute Miss Rate (SPEC Benchmarks)
Conflict
Miss rate

## Slide 20: Cache Organization?
Assume total cache size not changed. Which of 3Cs is obviously affected (if any) if we
Change Block Size:
2) Change Compiler:
Increased block size means fewer compulsory misses. It also means fewer blocks, which might increase conflict misses. And if it decreases spatial reuse, then it increases capacity misses.
A compiler might do a better job of making accesses local, which would lessen compulsory and conflict misses.
Notes: Ask which affected?
Block size
1) Compulsory
2) More subtle, will change mapping

## Slide 21: How far should we go?
How many transistors should we spend on big caches?
  Caches cost power & area, and don't do any computing
  We already see pretty good hit rates
  If you organize your code very cleverly, you can often get it to run fast without needing a lot of cache
But
  taking the time to organize your code cleverly takes time
  and time is money
  and most customers like to buy cheap software

## Slide 22: Histogram, done poorly
Let's look at how we access memory with different numbers of threads
1 thread | 2 th | 4 th | 8 th | 16 th | 32 th | 64 th | 128 th
1.3s | 1.2s | 1.7s | 2s | 4.9s | 5s | 4.9 | 4.9s
int input_vals_per_thread = input_data.size() / n_threads;
for (int i=0, idx=me; i<input_vals_per_thread; ++i) {
  ++my_hist[input_data[idx]];
  idx += n_threads;
}

## Slide 23: Memory patterns
Look at one cache line. Who accesses each 4B chunk of the 64B line?
1 thread
16 threads
1
0
2
3
5
4
6
7
9
8
10
11
13
12
14
15
8 threads
1
0
2
3
5
4
6
7
1
0
2
3
5
4
6
7
4 threads
1
0
2
3
1
0
2
3
1
0
2
3
1
0
2
3
2 threads
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 24: How many cache lines?
With just one thread, how many cache lines must that thread pull in?
  (500M elements) * (4B/element) * (1 line/64B)  32M lines
With 2 threads, how many lines must each thread pull in?
  No different!
What about 4, 8 or 16?
  Again, each thread must pull in every cache line!

## Slide 25: Histogram, done poorly
Any explanations for this behavior now?
  With so little work other than the loads and stores, memory accesses will almost certainly dominate the execution time.
  Every thread must still access every line
  So now we now why more threads (up to 16) don't make things faster.
  But why do more threads make execution slower? And why do things stop getting worse after 16 threads?
1 thread | 2 th | 4 th | 8 th | 16 th | 32 th | 64 th | 128 th
1.3s | 1.2s | 1.7s | 2s | 4.9s | 5s | 4.9 | 4.9s
int input_vals_per_thread = input_data.size() / n_threads;
for (int i=0, idx=me; i<input_vals_per_thread; ++i) {
  ++my_hist[input_data[idx]];
  idx += n_threads;
}

## Slide 26: More threads = slower
Remember that there are multiple levels of cache
L1 cache
L2 cache
regfile
Load data comes to the regfile from disk via all of the cache levels
There are never enough wires to transfer data quickly between levels
  Bandwidth on those wires is likely our critical path
How does this affect us?
  When we load entire cache lines and only use some of it, we're wasting bandwidth
  More threads → any thread uses less of each cache line → wastes more bandwidth → runs slower.
disk, memory, L3

## Slide 27: >16 threads = no more slowdown
Look at one cache line. Who accesses each 4B chunk of the 64B line?
1 thread
16 threads
1
0
2
3
5
4
6
7
9
8
10
11
13
12
14
15
8 threads
1
0
2
3
5
4
6
7
1
0
2
3
5
4
6
7
4 threads
1
0
2
3
1
0
2
3
1
0
2
3
1
0
2
3
2 threads
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 28: >16 threads = no more slowdown
With 16 threads, how many cache lines must each thread pull in?
  (500M elements) * (4B/element) * (1 line/64B)  32M lines
With 32 threads, how many lines must each thread pull in?
  Now each thread's stride is big enough that it only touches half of the cache lines
  So each thread touches  16M lines
With 64 threads, how many lines must each thread pull in?
  About 8M
Thoughts on why things stop getting slower after 16 threads?
  Sure, that makes sense now. But why don't we suddenly get lots faster after 16 threads?
  Because just throwing more threads at a problem doesn't help if it's memory limited.

## Slide 29: Histogram, done poorly
What went wrong?
  Our application does very little computation, and so is very dominated by memory access.
  In 2017, DRAM no longer can keep up with a CPU; we depend on caches
  Caches only works well when you have temporal or spatial locality (or both)
  Our histogram only used input data once → no temporal locality
  We divvied up data between threads in a way that has less and less spatial locality the more threads we use

## Slide 30: What would you fix?
Any suggestions for how to change the code?
int input_vals_per_thread = input_data.size() / n_threads;
for (int i=0, idx=me; i<input_vals_per_thread; ++i) {
  ++my_hist[input_data[idx]];
  idx += n_threads;
}

## Slide 31: What have we learned?
If you have a program that
  has lots of memory accesses and little computation (i.e., runtime is dominated by memory access)
  doesn't cache well (little temporal or spatial locality)
  then more threads may make things slower rather than faster
But now we're smarter than that, right?
  We'll divvy up work between threads to ensure each thread has spatial locality

## Slide 32: How many cache lines?
Assume we divide the data between threads so as to have spatial locality. With just one thread, how many cache lines must that thread pull in?
  (500M elements) * (4B/element) * (1 line/64B)  32M lines
With 2 threads, how many lines must each thread pull in?
  16M each, so 32M total
With N threads, how many lines must each thread pull in?
  32M/N each, so 32M total

## Slide 33: More threads
We still have lots of memory accesses and little computation
  Thoughts on what happens when we add more threads?
More threads definitely adds more adders, more multipliers, and more computes.
  How much does that matter?
But what does it do to memory-access rate?
  It's really hard to say. More on this shortly
Not a lot

## Slide 34: Even simpler program
Simple program: just sum up the elements of a vector
The outer loop just repeats the entire thing 10 times, to minimize cold-cache effects
Like the histogram, it's dominated by memory access.
How does the time to run this code change as you increase N?
How does time/N change as you increase N?
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 35: Even simpler program
How does the time to run this code change as you increase N?
How does time/N change as you increase N?
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];
time/N
N

## Slide 36: Walk through
Assume N=64, and L1 cache has 4 lines of 64B.
Assume each box below is 4B (one integer)
Let's look at the cache as we walk through the code execution
L1 line 0
L1 line 1
L1 line 2
L1 line 3

## Slide 37: Walk through
Here is a snapshot of the L1 cache
  when i=0, after j=0 code is done
  Why is the entire line #0 loaded, and not just 4B?
  Because caches work in entire lines
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 38: Walk through
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];
Here is a snapshot of the L1 cache
  when i=0, after j=15 code is done
  The L1 cache is still the same; j=1 through j=15 all hit in the L1 cache.

## Slide 39: Walk through
Here is a snapshot of the L1 cache
  when i=0, after j=16 code is done
  As before, the entire line #1 is loaded
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 40: Walk through
Here is a snapshot of the L1 cache
  when i=0, after j=32 code is done
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 41: Walk through
Here is a snapshot of the L1 cache
  when i=0, after j=63 code is done
Now the L1 cache has reached capacity (i.e., it's full)
Fortunately, our inner loop is finished (since N=64)
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 42: Walk through
Next up: i=1, and i=2, etc.
Predictions: will these loops run faster?
  Yes: everything will now hit in the L1 cache
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 43: Walk through
So with N=64, the first loop (i=0) is slow
And the rest are fast
What if N=65? Predictions?
  Everything will still hit in the L1? Nothing?
  64 out of 65 accesses will hit? 48 out of 65?
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 44: Walk through
At the end of i=0, j=63, we're at the same place as before
The L1 cache is full, with vec[63:0]
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 45: Walk through
What happens with we execute the j=64 code?
We want to pull in another line (vec[79:64], but there's no place to put it!)
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 46: Walk through
Evict one line – but which one?
Choose the one who has been in the cache longest
L1 line 0
[14]
[15]
[13]
[12]
[10]
[11]
[9]
[8]
[6]
[7]
[5]
[4]
[2]
[3]
[1]
[0]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 47: Walk through
When i=0, after j=64 code is done
L1 line 0
[78]
[79]
[77]
[76]
[74]
[75]
[73]
[72]
[70]
[71]
[69]
[68]
[66]
[67]
[65]
[64]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 48: Walk through
OK, we've reached the end of our loop, and summed the entire array.
Now it's on to i=1
L1 line 0
[78]
[79]
[77]
[76]
[74]
[75]
[73]
[72]
[70]
[71]
[69]
[68]
[66]
[67]
[65]
[64]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 49: Walk through
Any predictions for how many cache hits we'll get?
  None! All it takes is increasing N by 1 to go from everything hits in the L1 to nothing hits!
L1 line 0
[78]
[79]
[77]
[76]
[74]
[75]
[73]
[72]
[70]
[71]
[69]
[68]
[66]
[67]
[65]
[64]
L1 line 1
L1 line 2
L1 line 3
[30]
[31]
[29]
[28]
[26]
[27]
[25]
[24]
[22]
[23]
[21]
[20]
[18]
[19]
[17]
[16]
[46]
[47]
[45]
[44]
[42]
[43]
[41]
[40]
[38]
[39]
[37]
[36]
[34]
[35]
[33]
[32]
[62]
[63]
[61]
[60]
[58]
[59]
[57]
[56]
[54]
[55]
[53]
[52]
[50]
[51]
[49]
[48]
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];

## Slide 50: Even simpler program
How does the time to run this code change as you increase N?
How does time/N change as you increase N?
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];
time/N
N

## Slide 51: Even simpler program
How does the time to run this code change as you increase N?
How does time/N change as you increase N?
for (int i=0; i<10; ++i)
  int sum=0;
  for (int j=0; j<N; ++j)
    sum = sum + vec[j];
time/N
N
Ignore the i=0 loop to keep things simple
N is small enough to fit into L1
N is small enough to fit into L2
N is small enough to fit into L3

## Slide 52
We ran this example for a cache-line size of 64B
Would the results change if it were 32B? 16B?
  Not at all
What if it were 1B?
  Still not
This is purely because we are streaming data larger than the cache size; it has nothing to do with cache-line size.

## Slide 53: Moral of the story
Streaming data is bad for little caches
  Either data fits (and the cache works perfectly)
  Or it doesn't (and the cache is completely useless)

## Slide 54: Dell24: one CPU
One CPU:
  Eight two-threaded cores (this will make more sense when we talk about SMT)
  Each core has two 16KB L1 caches (one for each thread!)
  6MB of L3 cache, 2MB L2 cache
On multiple-CPU systems, each one is called a socket.
  Dell24 is an 8-socket system
  100GB main memory

## Slide 55: Dell24: the system
Each chip has its own local DRAM
Sockets talk to each other with a proprietary protocol (AMD is Hypertransport)
  I've drawn a cube
CPU0
DRAM
CPU1
DRAM
CPU2
DRAM
CPU3
DRAM
DRAM
CPU4
DRAM
CPU5
DRAM
CPU6
DRAM
CPU7

## Slide 56: Dell24: the system
What happens when one core wants to access memory that lives on another socket?
  It must travel over the links
For a thread that lives on, eg., a core in CPU0, is all memory equally fast to access?
  Not even close. This is called a Non-Uniform-Memory-Access (NUMA) system
CPU0
DRAM
CPU1
DRAM
CPU2
DRAM
CPU3
DRAM
DRAM
CPU4
DRAM
CPU5
DRAM
CPU6
DRAM
CPU7

## Slide 57: NUMA and the O/S.
Different cores have different-length paths to different DRAMs
So how does the O/S know which core to assign each thread to?
  Based on future memory accesses? No 
  Based on past memory accesses? This only works well if we have temporal locality.
  In actuality, I don't believe does much of either; it mostly tries to load balance, and lets caches handle the rest.
  Plus, there is the mapping of virtual pages to physical pages, and interleaving to deal with.

## Slide 58: NUMA and you
How do you write code to deal with NUMA?
  C++ threads doesn't let you assign threads to cores.
  Even if you could, virtual memory gets in the way (each time you run a program, the virtual-to-physical mapping may be different).
Interleaving.
  BIOS interleaves DRAM banks in physical memory
  The O/S interleaves pages in the virtual-to-physical mapping
  You can reverse-engineer both of these, and it may not be too hard; but I don't know how.

## Slide 59: Repeatability
Streaming rate from a core's L1 to the core is very reliable
The L3 is shared by many cores; its streaming rate depends on other traffic, but is still reasonably reliable
Streaming rate from DRAM is hard to predict
The further you go from the cores, the harder it is to predict runtime.
Moral: Be Smart, and do lots of computes on small pieces of a big dataset.

## Slide 60: Backup

## Slide 61: Memory-size info
Our histogram input data was 500M elements (4B each)
Dell 24 is made of AMD Opteron 6278 machines:
  Two 16KB L1 data caches per core (for 2 threads)
  2MB L2 per core
  6-16MB L3 per chip (lscpu disagrees with papers!)
  Tons of external DRAM