## Slide 1: ECEC 621: High Performance Computer Architecture
Spring 2016
Tufts University
Instructor: Prof. Mark Hempstead
mark@ece.tufts.edu
OOO and Tomusulo
[Chapter 3]

## Slide 2: Out of order machines
The architectural spec is easy:
  execute instructions one by one
  execute them in order they're written
  only execute the ones you're supposed to
In reality, as we've seen, in order to run faster:
  pipelining breaks #1
  speculative execution breaks #3
In fact, almost all machines nowadays execute out of order, breaking #2. What does that mean?

## Slide 3: What is data flow
Here’s a short program.
Here are the dependencies
LD F6, 34(R2)
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
DIVD F10, F0,F6
ADDD F6, F8,F2

## Slide 4: Data flow
Our machine executes instructions in this order; i.e., as soon as the data is ready.
LD F6, 34(R2)
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
DIVD F10, F0,F6
ADDD F6, F8,F2
LD F6, 34(R2)
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
DIVD F10, F0,F6
ADDD F6, F8,F2
Let’s rearrange them a bit.

## Slide 5: Data flow
LD F6, 34(R2)
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
DIVD F10, F0,F6
ADDD F6, F8,F2
LD F6, 34(R2)
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
DIVD F10, F0,F6
ADDD F6, F8,F2
The DIVD is supposed to execute next to last
  It will probably execute pretty early
  There's a problem with that 

## Slide 6: Data flow
What if R3 holds an illegal address? What's supposed to happen?
  It should take an exception, and later instructions do not happen.
  But the DIVD may have already finished, and written F10!
Speculative execution had the same problem; we had to undo things that already wrote the regfile, but shouldn't have
LD F6, 34(R2)
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
DIVD F10, F0,F6
ADDD F6, F8,F2
LD F6, 34(R2)
DIVD F10, F0,F6
LD F2, 45(R3)
MULT F0, F2,F4
SUBD F8, F6,F2
ADDD F6, F8,F2

## Slide 7: Reorder buffers
The solution to both of these problems is a reorder buffer
Essentially, any instruction that "finishes" actually stores its results in the reorder buffer – until we know for sure that the instruction was supposed to happen
  Then it writes the register file for real
  So the register file is never written until we know it is supposed to be

## Slide 8: Takeaways
What we have to know for out of order:
  instructions actually execute as soon as their operands are ready, no matter what order that is
  this reordering on the fly takes a lot of silicon area, and takes even more power
  a lot of the area and power is due to needing a reorder buffer – which is really needed for speculative execution anyway
Not having out-of-order results in unacceptable single-stream performance
  just as with speculative execution and branch prediction

## Slide 9: BACKUP

## Slide 10: Administration
Reading
  We’ll hand out & review the midterms ½ hour before the end of class today.
  This week’s material comes from Chapter 3. HW (#5) on it (due Wed. after spring break) will cover it.
  Next up will be Spring break .
  Then the 2nd half of the course.

## Slide 11: Limits of pipelining
So far our simple 5-stage pipe has worked well.
  No stalls after arithmetic operations (EXE→EXE bypass)
  One-cycle after load→use stall
  Stalls after a branch can be avoided with branch prediction.
  But real life doesn’t always have such a happy ending.

## Slide 12: Forwarding, Bypassing
Cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Add R3, R2, R1 | IF | ID | EX | MEM | WB |  |  | 
Add R4, R3, R5 |  | IF | ID | EX | MEM | WB |  | 
Add R6, R3, R5 |  |  | IF | ID | EX | MEM | WB | 
Ld R7, (30)R5 |  |  |  | IF | ID | EX | MEM | WB
Add, R9,R7,R1 |  |  |  |  | IF | ID | ID | EX

## Slide 13: Long pipes = lots of stalls
Our 5-stage pipe may be a 15-stage pipe. Why?
  Smaller stages with less logic → higher frequency
  Dependencies now imply more stalls.
  Loads & branches similarly get worse.
Cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  |  |  |  | 
Add R3, R2, R1 | F1 | F2 | D1 | D2 | E1 | E2 | E3 | M1 | M2 | W1 | W2 |  |  | 
Add R4, R3, R5 |  | F1 | F2 | D1 | D2 | D2 | D2 | E1 | E2 | E3 | M1 | M2 | W1 | W2

## Slide 14: Load misses = even worse
Even with a 5-stage pipe, load misses can cause numerous stalls:
What’s really dumb about this stall?
  The final Sub is stalled, but it doesn’t use R3 or R4, and the ALU is sitting idle.
Cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
Ld R3, 10(R1) | IF | ID | EX | M | M | M | M | M | M | WB |  |  | 
Add R4, R3, R5 |  | IF | ID | ID | ID | ID | ID | ID | ID | EX | M | WB | 
Sub R7, R8, R9 |  |  | IF | IF | IF | IF | IF | IF | IF | ID | EX | M | WB

## Slide 15: Not so easy to fix this
I
M
R
e
g
D
M
R
e
g
A
L
U
Ld R3, 10(R1)
Add R4, R3,R5
Sub R7, R8,R9
Problems:
  The ID and Mem pipe stages are full. The Sub cannot just hop over them (not without lots of new wires)
  Remember when we talked about exceptions? What if the Sub finishes before the Ld and Add, but then the Ld or Add takes an exception?

## Slide 16: Baby steps to fix it
Let’s take one step at a time, and ignore the other daunting problems ahead of us .
So first let’s try to get our independent instructions into the pipeline without bouncing. But how?

## Slide 17: Multiple small pipes
How about one pipe for Ld/St and one for arithmetic (add, sub, and, or, etc.)?
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arithmetic pipe
Ld R3, 10(R1)
Sub R7, R8,R9

## Slide 18: Multiple small pipes
The sub enters ID
The load issues into the load pipe
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Sub R7, R8,R9

## Slide 19: Multiple small pipes
The Sub issues into the Arithmetic pipe.
The load advances in the load pipe
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Sub R7, R8,R9

## Slide 20: Multiple small pipes
The load stalls due to a load miss.
The Sub advances in the Arith. Pipe.
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Sub R7, R8,R9

## Slide 21: Multiple small pipes
The load is still stalled.
The Sub retires.
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Sub R7, R8,R9

## Slide 22: Unintended consequences
We’ve had an unrelated instruction that would have been stuck behind a stalled load.
  We let it advance past the load into its own mini-pipe
  But it retired OOO. Won’t that cause problems with exceptions?
  And it still doesn’t solve all of our problems 
  Consider this sequence:
    Ld R3, 10(R1)
    Add R4, R3,R5
    Sub R7, R8,R9
Yes!

## Slide 23: Multiple small pipes
Start with the Add and Ld in the pipe.
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Add R4, R3,R5

## Slide 24: Multiple small pipes
The load issues into the load pipe, the Add advances and the Sub is fetched.
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
    Add R4, R3,R5
Sub R7, R8,R9

## Slide 25: Multiple small pipes
The load advances in the load pipe.
The Add is stalled in ID waiting for R3
Sub is stalled behind it, with no dependencies!
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Add R4, R3,R5
Sub R7, R8,R9

## Slide 26: Multiple small pipes
And here we sit, stuck, until the load miss finishes . Any ideas?
I
M
R
e
g
A
L
U
D
M
A
L
U
R
e
g
MUX
Ld/St pipe
Arith. pipe
Ld R3, 10(R1)
Add R4, R3,R5
Sub R7, R8,R9

## Slide 27: We’ve fixed just one problem
We fixed the problem of a load miss stalling all upstream arithmetic instructions (even unrelated ones).
But a load miss still stalls an upstream arithmetic instruction that needs the load result.
And that arithmetic instruction will, in turn, stall all upstream arithmetic instructions (whether or not they’re really waiting for the load data).

## Slide 28: Next idea
Each inst. grabs whichever of its regs are available, then waits in a reservation station for the other regs needs to be available.
When all of its operands are ready, it issues into its pipe.
The pipe (almost) never stalls.
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Res.St
Res.St
Reg
IM
Reg
Res.St
Res.St

## Slide 29: Next idea
Let’s run our example again.
The load and add start just as before.
Res.St
Res.St
Reg
IM
Res.St
Res.St
Ld R3, 10(R1)
Add R4, R3,R5
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg

## Slide 30: Next idea
The load moves to a reservation station (after grabbing R1).
The Add & Sub advance as usual.
Res.St
Res.St
Reg
IM
Res.St
Ld R3, 10(R1)
Add R4, R3,R5
Sub R7, R8,R9
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg

## Slide 31: Next idea
The load issues to the load pipe (since it has R1).
The Add advances to a reservation station – but without R3!
The Sub advances as usual.
Res.St
Res.St
Reg
IM
Res.St
Add R4, R3,R5
Sub R7, R8,R9
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg
Ld R3, 10(R1)

## Slide 32: Next idea
The load calculates its effective address and goes to M.
The Add sits still, waiting for R3
The Sub grabs R8 & R9 and goes to a res. station
Reg
IM
Res.St
Add R4, R3,R5
Sub R7, R8,R9
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg
Ld R3, 10(R1)
Res.St

## Slide 33: Next idea
The load misses & waits in M for fill data.
The Add sits still, waiting for R3… again
The Sub has its operands, and enters the pipe
Reg
IM
Res.St
Add R4, R3,R5
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg
Ld R3, 10(R1)
Res.St
Sub R7, R8,R9

## Slide 34: Next idea
The load is still waiting in M for fill data.
The Add is still waiting for R3… again
The Sub retires to the register file and is done.
And here we wait… until the load returns data.
Reg
IM
Res.St
Add R4, R3,R5
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg
Ld R3, 10(R1)
Res.St
Sub R7, R8,R9

## Slide 35: Next idea
Now assume the load has finally gotten its data (e.g., from L2).
The load advances to the RF and is done.
The Add grabs the R3 bypass data & enters the pipe.
Reg
IM
Res.St
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg
Ld R3, 10(R1)
Res.St
Add R4, R3,R5
Res.St

## Slide 36: Next idea
The Add finishes, goes to the RF and is done.
Reg
IM
Res.St
Res.St
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Reg
Res.St
Add R4, R3,R5
Res.St

## Slide 37: That’s (mostly) Tomusulo
We’ve (more or less) built Tomusulo
  It’s a dataflow machine that can execute out of order.
  Instructions mostly enter the appropriate pipe as soon as their operands are ready
  “Bypassing” is officially called the Common Results Bus, and loads/store are a bit different than we drew.
We’ve made precise exceptions even harder: why?
  The SUB (in principle the 3rd instruction) finished before the ADD; but what if the ADD had an exception?
And we’ve added two new problems: WAW and WAR hazards.

## Slide 38: WAW &WAR hazards
We’ve built a machine where instructions execute when their operands are ready… pretty much regardless of program order.
But that’s not how our ISA worked. Instructions must always appear to execute one at a time, in order (even if they actually don’t, as with pipelining).
Tomusulo has thoroughly broken that agreement.

## Slide 39: WAW &WAR hazards
Consider the following code snippets, where the Sub finishes early as in our example.
    Ld R3, 10(R1) Ld R3, 10(R1)
    Add R4, R3,R5 Add R4, R3,R7
    Sub R4, R8,R9 Sub R7, R8,R9
WAW: R4 has the wrong final value. Why?
  The Add writes it after the Sub does
WAR: the Add gets the wrong R7. Why?
  Again, the Sub writes R7 before the Sub issues.
  Actually, our reservation station doesn’t have this problem, since the Add grabbed R7 before the Sub even entered the pipe. But other implementations might.
WAW
WAR

## Slide 40: Register renaming
We can fix the WAW problem by register renaming.
    Ld R3, 10(R1) Ld R3, 10(R1)
    Add R4, R3,R5 Add R400, R3,R5
    Sub R4, R8,R9 Sub R4, R8,R9
It seems dumb of the compiler to reuse R4 like that; wasn’t it just asking for trouble?
  Not all ISAs have a ton of registers; the compiler may have been forced to reuse R4.

## Slide 41: Register renaming
We can fix the WAR problem too:
    Ld R3, 10(R1) Ld R3, 10(R1)
    Add R4, R3,R7 Add R4, R3,R7
    Sub R7, R8,R9 Sub R700, R8,R9
Same compiler issues as for WAW.

## Slide 42: Register renaming
Why is register renaming a big deal?
  A smart compiler, with lots of registers available, shouldn’t really need it much.
  And Tomusulo fixes WAR hazards anyway.
Again, x86 is pretty important; and the number of registers is always finite.
But there’s a more important issue: loops.

## Slide 43: Renaming and loops
Consider this code:
  for (i=100; i>=0; --i) ++mem[array_base+i]
Assembly:
  Loop: Ld r2, 100(r1)
  Add r2, r2, #1
  St r2, 100(r1)
  Sub r1,r1,1
  BNZ r1, loop
Load-to-use hazard on R2 will cause substantial stalls on a highly-pipelined machine.

## Slide 44: Unrolling
What if we unroll the loop a bit?
    for (i=0; i<∞; i+=2)
      { ++mem[array_base+i]; ++mem[array_base+i+1]; }
  In assembly,
    Loop: Ld r2, 100(r1)
    Add r2, r2, #1
    St r2, 100(r1)
    Ld r2, 101(r1)
    Add r2, r2, #1
    St r2, 100(r1)
    Sub r1,r1,1
    JNZ r1, loop
We’ve not really helped anything at all; just made more code.

## Slide 45: Unrolling
But now let’s rename r2 on the second load/store.
  In assembly,
    Loop: Ld r2, 100(r1)
    Add r2, r2, #1
    St r2, 100(r1)
    Ld r200, 101(r1)
    Add r2, r200, #1
    St r200, 100(r1)
    Sub r1,r1,1
    JNZ r1, loop
  If we unroll N iterations, we can do N loads before we use any of the load data; and avoid stalling as long as the load-to-use penalty is <N cycles.
    Loop: Ld r2, 100(r1)
    Ld r200, 101(r1)
    Sub r1,r1,1
    Add r2, r2, #1
    St r2, 100(r1)
    Add r2, r200, #1
    St r200, 100(r1)
    JNZ r1, loop
Still not done much? But remember our dataflow machine.

## Slide 46: Renaming
Problems with compiler-based unrolling:
  Takes a lots of extra memory for the instructions.
  The compiler does not know if an instruction will hit in the L1 or not
Smart hardware (which HW #5 will steer you towards) can rename registers automatically
Given this, Tomusulo will automatically and dynamically unroll the loop as much as needed…
  Amazing but true.

## Slide 47: Hardware renaming and unrolling
Consider our Tomusulo algorithm, and assume:
  Renaming happens automatically via hardware.
  We have plenty of reservation stations.
  We can fetch a new instruction every cycle: i.e., branches are predicted correctly, and our ICache always hits.

## Slide 48: Renaming
Renaming has done everything we want, with one exception: namely, precise exceptions.
With enough effort, we can make renaming also deal with precise exceptions… but first, let’s discuss a somewhat-easier way.

## Slide 49: Summary of where we are
We execute instructions without unneeded stalls.
But we have problems, resulting from:
  instructions writing the RF out of order,
  or before an earlier instruction takes an exception.
How can we fix this?
The key is to never update architectural state until: all earlier instructions are “really, truly finished”
  We know that earlier branch directions are correct
  All exceptions in earlier instructions are dealt with
  All earlier instructions have updated their arch. state

## Slide 50: Reorder buffer
Definition: an instruction commits when we update architectural state with its results.
  The key is to execute out of order, but commit in order.
So we must somehow:
  Even as we put instructions into multiple pipes in dataflow order, still remember which instruction came first in the program.
  After an instruction finishes, save its results until it commits & we can thus write the RF.
A reorder buffer (ROB) is the magic trick to do both of these
  It’s really not magic, or even very hard.

## Slide 51: ROB details
The ROB is a FIFO.
An instruction will:
  Enter the ROB when it gets fetched
  Store its result in its ROB entry when the result is calculated (i.e., when it exits the appropriate pipe)
  Leave the ROB when it commits. Then move its results to the RF.
When can it commit?
  Its results must be in the ROB with it
  All earlier instructions must be committed (i.e., it must be at the head of the FIFO).
The FIFO is usually a circular buffer with head/tail pointers.
OK, let’s do our simple example yet again!

## Slide 52: Same example, with ROB
Load issues. It also enters the ROB.
A
L
U
D
M
A
L
U
MUX
Ld/St pipe
Arith. pipe
Res.St
Res.St
Reg
IM
Reg
Res.St
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 

## Slide 53: Same example, with ROB
Add issues & enters the ROB
Load moves to ID
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Res.St
Res.St
Reg
IM
Reg
Res.St
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Add R4, R3,R5

## Slide 54: Same example, with ROB
Sub issues & enters the ROB
Add moves to ID
Load moves to reservation station with R1.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Res.St
Res.St
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 
Add R4, R3,R5
Sub R7, R8,R9
Res.St

## Slide 55: Same example, with ROB
Sub moves to ID
Add moves to reservation station with R5 but without R3.
Load moves to EX.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Res.St
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 
Add R4, R3,R5
Sub R7, R8,R9
Res.St
Res.St

## Slide 56: Same example, with ROB
Sub grabs R8,R9 and moves to a reservation station
Add is stuck waiting for R3.
Load moves to Mem and has an L1 miss.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 
Add R4, R3,R5
Sub R7, R8,R9
Res.St
Res.St

## Slide 57: Same example, with ROB
Sub has both operands; it enters the arith. pipe
Add is still stuck waiting for R3.
Load waits in Mem for the L2 to return data.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 
Add R4, R3,R5
Sub R7, R8,R9
Res.St
Res.St

## Slide 58: Same example, with ROB
Sub exits the pipe, but cannot commit until the add does; its result is saved in the ROB.
Load is still waiting for the L2; Add is waiting for the load.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 
Add R4, R3,R5
Sub R7, R8,R9
Res.St
Res.St
0x12

## Slide 59: Same example, with ROB
Sub is out of the pipe, but still in the ROB (R7 is not updated)
Load is still waiting for the L2; Add is waiting for the load.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 0x12
Add R4, R3,R5
Res.St
Res.St

## Slide 60: Same example, with ROB
L2 returns data. Load finishes, forwards its data to the ADD, and updates the ROB.
The Add enters the arithmetic pipe.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
Ld R3, 10(R1)
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 0x12
Add R4, R3,R5
Res.St
Res.St
0x34
Res.St

## Slide 61: Same example, with ROB
The load is at the top of the ROB & has data. It commits.
The Add exits the pipe and puts its result into the ROB.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
ROB FIFO | 
Load R3,10(R1) | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 0x12
Add R4, R3,R5
Res.St
Res.St
0x34
Res.St
0x56

## Slide 62: Same example, with ROB
The Add is at the top of the ROB & has data. It commits.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
ROB FIFO | 
Add R4,R3,R5 | 
Sub R7,R8,R9 | 0x12
Res.St
Res.St
Res.St
0x56

## Slide 63: Same example, with ROB
Now (finally!) the Sub is at the top of the ROB, and so can commit.
A
L
U
D
M
A
L
U
Ld/St pipe
Arith. pipe
Reg
IM
Reg
Res.St
ROB FIFO | 
Sub R7,R8,R9 | 
Res.St
Res.St
Res.St
0x12

## Slide 64: That’s (mostly) Tomusulo+ROB
When instructions are fetched, they enter the ROB (as well as entering the ID stage as usual), and then go to a reservation station to wait for operands.
  If there were no dependencies, then they will have their operands at this point.
Instructions enter their appropriate pipe (from a reservation station) as soon as their operands are available (but no sooner)
They run through the pipe and (almost) never stall.
When they exit the pipe, they forward results to any reservation stations that are waiting, and to the ROB.
They commit from the ROB in strict program order.

## Slide 65: What’s left in Tomusulo?
We’re almost there, except:
  We haven’t dealt with exceptions, or branch prediction.
  There’s one more hazard left: hazards through memory.
But those are all easy, now that we’ve built the infrastructure.

## Slide 66: Exceptions
Precise exceptions are easy.
  We’ve already ensured that instruction #n does not change architectural state until instruction #n-1 is really truly done.
  We’ve already talked about not letting an instruction signal an exception until the WB stage
  Those two guarantee precise exceptions.
All that’s left: flush the ROB and all reservation stations after an exception, and then restart the PC afterwards.

## Slide 67: Branch prediction
Branch prediction is easy too.
  No instruction can commit until we know it should really execute.
  all earlier branch predictions are guaranteed to be correct.
The details:
  Do branch prediction and branch-target buffer as usual.
  After any mispredict, flush the ROB of all instructions after the mispredicted branch
  Restart the PC with the correct branch target

## Slide 68: Loads and stores
Consider the following code:
    DIVD F3,F1,F2
    ST F3, 0(R1)
    LD F10, 0(R1)
Problem:
  The divide is slow
  The store depends on the divide (via R3), so it waits
  The load happens right away – before the store.
  We load the wrong value!
Is this a new kind of dependency that we’ve ignored?

## Slide 69: Loads and stores
Is R1 the dependency?
    DIVD F3,F1,F2
    ST F3, 0(R1)
    LD F10, 0(R1)
Well, perhaps, but that’s not quite it. Consider
    DIVD F3,F1,F2
    ST F3, 0(R1)
    LD F10, 10(R1)
And consider
    DIVD F3,F1,F2
    ST F3, 0(R1)
    LD F10, 0(R10)
Actually, the dependency is the address.
No problem, even though R1 looks the same
A big problem if R1==R10

## Slide 70: We need more rules
Memory is architectural state, just like the RF
  I.e., once you write it, it’s hard to undo.
  And it’s a way to pass values from one inst. to another.
  So put in similar interlocks as for registers.
The new rules:
  Stores do not actually happen (i.e., do not go to any cache) until they commit. So they happen in order.
  Loads cannot leave their reservation station if there is a store with the same address ahead of them.
  In practice, after computing the effective address, stores are kept in the ROB and not in any reservation station or pipe.

## Slide 71: Dynamic unrolling
Observation #1:
  With enough reservation stations, we will issue 1 new instruction from the ID stage into a reservation every single cycle. Why is this true?
  We assumed that we can fetch a new instruction every cycle.
  With Tomusulo, new instructions do not stall at the ID stage waiting for operands; they just enter the reservations stations with as many operands are available.
Conclusion: we will keep running around the loop at full speed, putting more instructions into reservation stations.

## Slide 72: Dynamic unrolling
Observation #2:
  If instructions are stalled in a Reservation Station due to not having operands available, the number of RS in use will keep increasing.
  And if >1 instruction in an RS unstalls at the same time, the number of RS in use will decrease. Why?
    Because we said that new instructions just keep coming into the Reservation stations…
    And if rain steadily fills a bucket, then how fast you bail the water out will determine if the bucket gets fuller, emptier or stays the same.

## Slide 73: Dynamic unrolling
Observation #3:
  The more times you unroll, the less stalls you will have on average. Why?
  More unrolling means you can put more loads in a row before the first use of them. We already showed this.
So the system will at some point reach a steady state where you’ve unrolled enough times that the number of RS in use will be steady.
At that point, the # of RS in use will correspond to just the right number of loop unrollings.

## Slide 74: How far should we go?
How many transistors should we spend on OOO infrastructure?
  Lots of reservation stations and a big ROB cost area and power, and don't do any computing
  Instructions per cycle is hitting a wall; there's just not that much parallelism in most code (no matter how hard your OOO transistors try)
But
  OOO makes a really big difference in single-stream performance.

## Slide 75: Backup

## Slide 76: Dynamic Scheduling
Scheduling tries to re-arrange instructions to improve performance
Previously:
  We assume when the ID stage detects a hazard that cannot be hidden by bypassing/forwarding pipeline stalls
  AND, we assume the compiler tries to reduce this
Now:
  Re-arrange instructions at runtime to reduce stalls
  Why hardware and not compiler?

## Slide 77: Goals of Scheduling
Goal of Static Scheduling
  Compiler tries to avoids/reduce dependencies
Goal of Dynamic Scheduling
  Hardware tries to avoid stalling when present
Why hardware and not compiler?
  Code Portability
  More information available dynamically (run-time)
  ISA can limit registers ID space
  Speculation sometimes needs hardware to work well
  Not everyone uses “gcc –O3”

## Slide 78: Dynamic Scheduling: Basic Idea
Example
    DIVD F0, F2, F4
    ADDD F10, F0, F8
    SUBD F12, F8, F14
Hazard detection during decode stalls whole pipeline
No reason to stall in these cases: Out-of-Order Execution
  Reduces stalls, improved FU utilization, more parallel execution
  To give the appearance of sequential execution: precise interrupts
  First, we will study without this, then see how to add them
Dependency
Independent

## Slide 79: Loop unrolling example
  Loop: Ld r2, 100(r1)
  Add r3, r3, r2
  Add r1,r1,#1
  J loop