## Slide 1: EE 193: Parallel Computing
Fall 2017
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Simultaneous Multithreading (SMT)

## Slide 2: Threads
We've talked a lot about threads.
In a 16-core system, why would you want to have >1 thread?
  If you have <16 threads, some of the cores will just be sitting around idle.
Why would you ever want more than 16 threads?
  Perhaps you have 100 users on a 16-core machine, and the O/S rotates them around for fairness
  Today we'll talk about another reason

## Slide 3: More pipelining and stalls
Consider a random assembly program
The architecture says that instructions are executed in order.
  The 2nd instruction uses the r2 written by the first instruction
load r2=mem[r1]
add r5=r3+r2
add r8=r6+r7

## Slide 4: Pipelined instructions
Pipelining cheats! It launches instructions before the previous ones finish.
Hazards occur when one computation uses the results of another – it exposes our sleight of hand
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7 | Cycle 8
load r2=mem[r1] | fetch | read R1 | execute nothing | access cache | write r2 |  |  | 
add r5=r3+r2 |  | fetch | read r3,r2 | add r3,r2 | load/st nothing | write r5 |  | 
add r8=r6+r7 |  |  | fetch | read r6,r7 | add r6,r7 | load/st nothing | write r8 | 
store mem[r9]=r10 |  |  |  | fetch | read r9,r10 | execute nothing | store | write nothing

## Slide 5: Dependence
Pipelining works best when instructions don't use results from just-previous instruction
  But instructions in a thread tend to be working together on a common mission; this isn't good
Each thread has its own register file, by definition
  They only interact via shared memory or messages
  One thread cannot read a register that another thread wrote
Idea: what if we have one core execute many threads? Does that sound at all clever or useful?

## Slide 6: Your pipeline, on SMT
We still have our hazard (from loading r2 to the final add)
The intervening instructions are not hazards; even though they (coincidentally) use r2, each thread uses its own r2.
By the time thread 0 uses r2, r2 is in fact ready
No stalls needed 
Instruction | Thread | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7 | Cycle 8
load r2=mem[r1] | 0 | fetch | read R1 | execute nothing | access cache | write r2 |  |  | 
add r4=r2+r3 | 1 |  | fetch | read r3,r2 | add r3,r2 | load/st nothing | write r5 |  | 
add r6=r2+r7 | 2 |  |  | fetch | read r6,r7 | add r6,r7 | load/st nothing | write r8 | 
add r5=r3+r2 | 0 |  |  |  | fetch | read r2,r3 | execute nothing | store | write nothing

## Slide 7: Problems with SMT
SMT is great! Given enough threads, we rarely need to stall
Everyone does it nowadays (Intel calls it hyperthreading)
How many threads should we use?

## Slide 8: Your pipeline, on SMT
What if mem[r1]is not in the L1, but in the L2? It will take more cycles to get the data. But then the final add will have to wait 
Could we just stick an extra few instructions from other threads between the load and add, so we don't need the stall?
  (Note we've drawn an OOO pipe, where the "add r4" can finish before the load)
Instruction | Thread | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7 | Cycle 8
load r2=mem[r1] | 0 | fetch | read R1 | execute nothing | L1 miss | L1 miss | L1 miss | L1 miss | write r2
add r4=r2+r3 | 1 |  | fetch | read r3,r2 | add r3,r2 | load/st nothing | write r5 |  | 
add r6=r2+r7 | 2 |  |  | fetch | read r6,r7 | add r6,r7 | load/st nothing | write r8 | 
add r5=r3+r2 | 0 |  |  |  | fetch | read r2,r3 | execute nothing | store | write nothing

## Slide 9: Problems with SMT
Intel, AMD, ARM, etc., only use 2-way SMT. There must be a reason…
  SMT is great because each thread uses its own regfile
  If we have 10-way SMT, how many regfiles will each core need?
  So why don't we do 10-way SMT?
The mantra of memory: there's no place to fit lots of memory all situated on prime real estate.
  Too much SMT → register files become slow
  So we're stuck with 2-way SMT
  SMT is perhaps a GPU's biggest trick. It's much more than 2-way. More on that later
In practice, we don't just alternate threads. We issue instructions from whichever thread isn't stalled.