## Slide 1: EE 193: Parallel Computing
Fall 2017
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
What have we learned about architecture?

## Slide 2: Caches
Why do we have caches? When do caches work well, and not so well?
  While main-memory density has greatly increased over the years, its speed has not kept up with CPU speed
  Caches let you put a small amount of high-speed memory near the CPU so it doesn't spend lots of time waiting for memory
  They work well when your program has temporal and spatial locality. Otherwise, not.

## Slide 3: Branch predictors
What is branch prediction?
  Instead of stalling until you know if a branch is taken, just make your best guess and execute your choice
  If your guess turns out correct, then good. You run fast
  If not, then undo everything you've done (at considerable energy cost), using a Reorder Buffer
  Making your best guess usually relies on past history at each branch

## Slide 4: Out of order
What is OOO?
  Forget about executing instructions in program order
  Look ahead at the next 10-100 instructions to find any of them whose operands are ready
  Execute in dataflow order (i.e.., whoever is ready)
  If something goes wrong (like an earlier instruction takes an exception), then undo all instructions after the exception (using a reorder buffer)

## Slide 5: SMT
What is SMT?
  One core has several threads to choose from
  Whenever one thread would be stalled, it switches to another thread
  Requires (essentially) a separate register file for each thread
  Allows one core to execute many threads with minimal stalling
  Does not help single-thread execution speed

## Slide 6: How far should we go?
How many transistors should we spend on big caches?
  Caches cost power & area, and don't do any computing
  We already see pretty good hit rates
  If you organize your code very cleverly, you can often get it to run fast without needing a lot of cache
But
  taking the time to organize your code cleverly takes time
  and time is money
  and most customers prefer software to be cheap or free

## Slide 7: How far should we go?
How many transistors should we spend on branch prediction?
  The BP itself costs power and area, but does no computation.
  A BP is necessary for good single-stream performance
  We already saw diminishing returns on bigger BHTs
  The difficult-to-predict branches are often data dependent; a better/bigger algorithm won't help much
It would be really nice if we just didn't care about single-stream performance
  But we do – usually.

## Slide 8: How far should we go?
How many transistors should we spend on OOO infrastructure?
  A big ROB costs area and power, and doesn't do any computing
  Instructions per cycle is hitting a wall; there's just not that much parallelism in most code (no matter how hard your OOO transistors try)
But
  OOO makes a really big difference in single-stream performance.

## Slide 9: So what do we do?
Keep adding more transistors?
  Bigger caches, bigger branch predictors, more OOO
  Will cost more and more power for very little execution speed
Everybody stopped doing this 10 years ago
Instead: more cores
  And, in fact, single-stream performance is no longer improving very quickly

## Slide 10: CPU vs. GPU, once more
How can a GPU fit so many cores in the same area?
  Their cores do not have OOO, speculation, BP, large caches, …
But won't a GPU have lousy single-thread performance?
  Yes. That's not their market
 | Haswell Server | Nvidia Pascal P100
# cores | 18 | 3840
Die area | 660 mm2 (22nm) | 610 mm2 (16nm)
Frequency | 2.3 GHz normal | 1.3 GHz
Max DRAM BW | 100 GB/s | 720 GB/s
LLC size | 2.5 MB/core (L3) | 4 MB L2/chip
LLC-1 size | 256K/core(L2),64B/c | 64 KB/SM (64 cores)
Registers/core | 180 per 2 threads | 1000
Power | 165 watts | 300 watts
Company market cap | $160B | $90B

## Slide 11: CPU vs. GPU, once more
How can GPU get away with so little cache?
  programmer is responsible for highly optimizing algorithms
But won’t the software be hard to write?
  Yes
 | Haswell Server | Nvidia Pascal P100
# cores | 18 | 3840
Die area | 660 mm2 (22nm) | 610 mm2 (16nm)
Frequency | 2.3 GHz normal | 1.3 GHz
Max DRAM BW | 100 GB/s | 720 GB/s
LLC size | 2.5 MB/core (L3) | 4 MB L2/chip
LLC-1 size | 256K/core(L2),64B/c | 64 KB/SM (64 cores)
Registers/core | 180 per 2 threads | 1000
Power | 165 watts | 300 watts
Company market cap | $160B | $90B

## Slide 12: CPU vs. GPU, once more
Why does a GPU have so many registers?
  Because it depends on SMT to get multi-thread performance
 | Haswell Server | Nvidia Pascal P100
# cores | 18 | 3840
Die area | 660 mm2 (22nm) | 610 mm2 (16nm)
Frequency | 2.3 GHz normal | 1.3 GHz
Max DRAM BW | 100 GB/s | 720 GB/s
LLC size | 2.5 MB/core (L3) | 4 MB L2/chip
LLC-1 size | 256K/core(L2),64B/c | 64 KB/SM (64 cores)
Registers/core | 180 per 2 threads | 1000
Power | 165 watts | 300 watts
Company market cap | $160B | $90B

## Slide 13: Power Implications of Parallelism
Consider doubling number of cores, same power budget
  By reducing clock frequency and voltage... but how much?
First, a few equations (approximate, first order)
  Frequency ~ Voltage (higher voltage -> transistors switch faster)
  Dynamic Power ~ Transistors * Frequency * Voltage2
  Thus, Dynamic Power ~ Transistors * Frequency3
How?
  Doubling number of cores (transistors) will double the power
  Reducing frequency & voltage by 20% will cut power in half (0.83 is 0.5)...
  2x # of cores, each 20% slower →1.6x performance increase
Parallelism is great
  If we can write software for it!

## Slide 14: Approaches to the serial problem
Rewrite serial programs so that they’re parallel
  This is usually slow & error prone
Write translation programs that automatically convert serial programs into parallel programs.
  This is very difficult to do.
  Success has been limited.
No magic bullet has been found yet

## Slide 15: What kind of multicore?
We will build multicore CPUs
  Everyone has conceded this
  Even the Iphone X is a six-core chip.
But what kind of cores?
  "Big" cores, with lots of cache, OOO, BP
  Less power efficient, but gives you good single-thread performance
  Intel Xeon has followed this route
Small cores: much less cache, OOO, BP
  More power efficient; more cores can fit. So multithread performance is better
  But single-thread performance is unacceptable, and programming is challenging
  GPUs have taken this route, to the extreme. The one feature they've kept is SMT

## Slide 16: What to remember
Caches:
  Write your code to have temporal and spatial locality
  Easier said than done sometimes!
  But extremely important
  And try to make it fit in cache (or break it into sub-problems)
Branch prediction:
  big, power-hungry and usually still necessary for single-stream perf
  data-dependent branches are slow
OOO:
  big, power-hungry and usually still necessary for single-stream perf
SMT
  Can reduce stalls without needing as much BP and OOO
  Can only go so far before the regfile explodes