## Slide 1: EE 193: Parallel Computing
Fall 2017
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lecture 3: Ring caches and coherence

## Slide 2: Goals
Primary goals:
  Learn how caches work on many multi-core processors
  Learn what cache coherence is, and why it can make writes slower than reads

## Slide 3: BRIEF Introduction to Cache Coherence [5.2, 5.4]

## Slide 4: Cache Coherence in Multicores
Two cores on one die each have their own L1, but share some higher-level cache (e.g., L2).
The issue is a cache coherence problem. It only occurs when two processes share the same memory space.
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
X = 1
Notes: For lecture
Assumes a write through L1 cache

## Slide 5: A Coherent Memory System
The problem: when processors share slow memory, data must move to local caches in order to get reasonable latency and bandwidth. But this can produce unreasonable results.
  The solution is to have coherence and consistency.
  Coherence – defines what values can be returned by a read
  every private cached copy of a memory location has the same value
  guarantees that caches are invisible to the software, since all cores read the same value for any memory location
The issue on the last slide was a coherence violation. We'll focus on coherence in this course.

## Slide 6: Consistency
Consistency defines the ordering of two accesses by the same thread to different memory locations
So, core #0 writes mem[100]=0 and then mem[200]=1. Will all cores see mem[100]=0 before they see mem[200]=1?
  Surprisingly, the answer is not always "yes."
  Different models of memory consistency are common (SPARC and x86 support Total Store Ordering, which answers "no" at times)
  However, whichever write happens first, all cores will see the same ordering
Much more info: “A Primer on Memory Consistency and Cache Coherency” online at Tisch. Reading one chapter is a good final project

## Slide 7: Cache coherence strategies
Coherence is usually implemented via write invalidate
  As long as processors are only trying to read a cache line, as many people can all cache the line as desired
  If a processor P1 wants to write a cache line, then P1 must be the only one caching the line. If a different processor P0 then wants to read the line, P0 must first write its modified cache line back to memory and is no longer allowed to write the line.
This is the key to everything: the rest is all implementation details
Notes: For repeated writes by one P to the same address, write broadcast requires a full broadcast of each write, and negates much of the advantage of having a writeback cache in the first place.

## Slide 8: Cache Coherence Protocols
Next question: Assuming we do write-invalidate, how do you get all of the invalidates to the Ps who need them? The first common solution was snoopy.
  Just send the invalidate everywhere. Implementation is usually that the write happens via a shared bus, and all other Ps watch the bus to “snoop” on writes.
Notes:   Reading from multiple copies is not a problem!! Only writes cause issues. What happens if two processors try to write to the same shared data word in the same clock cycle? The bus arbiter decides which processor gets the bus first (and this will be the processor with the first exclusive access). Then the second processor will get exclusive access. Thus, bus arbitration forces sequential behavior.
  This sequential consistency is the most conservative of the memory consistency models. With it, the result of any execution is the same as if the accesses of each processor were kept in order and the accesses among different processors were interleaved.
Each line needs an additional state bit – owner - which indicates that a line may be shared, but the owning core is responsible for updating any other processors and memory when it changes the line or replaces it.
An alternative to snooping is a directory based cache coherence protocol where the directory keeps the sharing status of lines of physical memory. They have slightly higher implementation overhead but can reduc traffic between caches and thus scale to larger core counts.

## Slide 9: Example of Snooping Invalidation
Start with X=0 in the shared L2.
Core #1
Core #2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = I
X = 0
skip this part (5 slides)
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a line may be shared, but the owning core is responsible for updating any other processors and memory when it changes the line or replaces it

## Slide 10: Example of Snooping Invalidation
Core #1 reads X.
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = I
X = 0
Read X
X = 0
Core #1
Core #2
skip this part (5 slides)
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a line may be shared, but the owning core is responsible for updating any other processors and memory when it changes the line or replaces it

## Slide 11: Example of Snooping Invalidation
Next, core #2 also reads X.
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = I
X = 0
X = 0
Read X
X = 0
Core #1
Core #2
skip this part (5 slides)
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a line may be shared, but the owning core is responsible for updating any other processors and memory when it changes the line or replaces it

## Slide 12: Example of Snooping Invalidation
X = I
X = 0
Now the fun begins. Core #1 writes X=1. The write goes to the bus (even though core #1’s L1 is writeback and hit); core #2 snoops the write and invals its L1.
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 1
X = 0
Core #1
Write X=1
X = I
skip this part (5 slides)
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a line may be shared, but the owning core is responsible for updating any other processors and memory when it changes the line or replaces it

## Slide 13: Example of Snooping Invalidation
Next, core #2 reads X again. The L1 read miss goes to the bus; core #1 sees it and responds with data (which also updates the L2)
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = I
X = 1
X = I
Core #1
Core #2
Read X
X =1
X = 1
skip this part (5 slides)
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a line may be shared, but the owning core is responsible for updating any other processors and memory when it changes the line or replaces it

## Slide 14: Snoopy, power and scaling
Snoopy requires sending lots of messages to every P in the system. But there are lots of Ps, and they are far apart
  we must send lots of data on lots of long wires.
  slow and power hungry.
Big busses are thus not a realistic form of interconnect nowadays. Let’s look at one alternative.

## Slide 15: Ring cache
A type of shared-memory microprocessor (used on numerous Intel Xeon & IBM Power servers)
P0
P1
P2
P3
L20
L21
L22
L23
P4
P5
P6
P7
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 16: Average latency
Lots of the threads communicating via shared memory means you need fast communication
Considering only the clockwise ring, and disregarding the Ps, what is the average latency from L22 to another L2?
  Equally likely to go to L23 (1 cycle) L24 (4 cycles), L25 (5 cycles), L26 (6 cycles), L27 (7 cycles), L20 (8 cycles), L21 (9 cycles).
  Average latency = 1/7 * (1+4+5+6+7+8+9) = 5.7 cycles.
Potential quiz question: what if we can choose from both rings?

## Slide 17: Ring cache
There is just one L2 cache; it is physically divided into slices. Each L2 slice statically owns its piece of physical memory.
P0
P1
P2
P3
L20
L21
L22
L23
P4
P5
P6
P7
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 18: Physically distributed L2
Again, each L2 slice statically owns some portion of memory.
  E.g., L20 owns addresses 0-0xFFFF L21 owns 0x10000-0x1FFFF, L22 owns 0x20000-0x2FFFF, …
The alternative – having numerous independent, large L2 caches on one die – would be impractical.
But, yes – this implies that cached L2 data may be far from a P that uses it.
  If a P uses the data a lot, data will move to that P’s L1
  And the ring is really fast, anyway.
Why is this not a problem?

## Slide 19: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 20: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 21: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 22: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 23: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 24: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 25: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 26: Ring cache
Example: P1 wants data from L23, and P2 wants data from L27.
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 27
The genius of a ring cache (or of most modern distributed interconnect) is that many messages can be in flight at the same time, each using a small part of the interconnect.
Would this still be true if we only had one ring instead of two?
P0
P1
P2
P3
L20
L21
L22
L23
P7
P6
P5
P4
L27
L26
L25
L24
MC0
MC1
yes, but we would have less bandwidth
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 28: Directories
When we modify a cached address, we must ensure that everyone else caching that address evicts it
But we cannot send a message to everyone.
  That would fill the entire ring with just our messages
What if we could send messages only to the cache(s) that actually do hold our data?
  Tremendously fewer messages to be sent.
  But that implies somebody is keeping track, for every line of data, which caches are storing it and if they’ve modified it.
  Will that become another bottleneck?

## Slide 29: Directories – the big picture
On a memory access to a line, we need to:
  Locate additional copies.
  Find out about the state of the line in other caches.
  Communicate with other copies when appropriate.
Approach must scale well so that it can be used in very large systems.

## Slide 30: Basic Directory Approach
Every address in the system has a home node, which manages coherency for that address.
For time being, assume just one big home node somewhere.
Each memory line has a directory entry, which tracks copies of line and state information.
Read and write operations change the state information via network transactions.

## Slide 31: State Bits
M is a dirty (i.e., modified) bit.
Why would we want it? Isn’t this info also in the higher-level caches?
  Yes, but having two copies lets the home node make decisions more quickly.
Presence bits track which P(s) currently owns this line.
Only one presence bit can be set for a modified line; many can be set on reads.
One such entry for every line cached by any P.
M P0 P1 P2 P3 P4 P5 P6 P7
Directory state for one line

## Slide 32: State Bits
What would this set of bits mean?
M P0 P1 P2 P3 P4 P5 P6 P7
0 1 0 0 1 0 0 0 0
1 0 0 0 1 0 0 0 0
1 1 0 0 1 0 0 0 0
Cores #0 and #3 are reading this line
Core #3 has modified this line
Illegal: if one core modifies a line, no other core’s cache can hold the line.

## Slide 33: Ring cache
Let’s add a home node to the ring. It stores the status of every line in the L2 or in anybody’s L1.
We’ve created a huge bottleneck – everyone talking to one HN. Nearby links get swamped.
P0
P1
P2
P3
L20
L21
L22
L23
L27
L26
L25
L24
HN
MC
Bottom Ps not drawn
Notes: This is a ring cache. It is a fairly scalable form of interconnect. There are two counter-rotating rings, one clockwise and one counter-clockwise. Having two rings doubles your bandwidth. Making them rotate in opposite directions shortens your average distance between any two processors. So P0 would send a message to P1 using the clockwise ring; P1 would reply to P0 using the counter-clockwise ring.
The rings are pipelined, so it is perfectly possible for, e.g., 0 to send a message to 1, 4 to send a message to 5 and 6 to send a message to 0 all at the same time, and for similar things to happen at the same time on the other ring.
MC is a memory controller. Each memory controller talks to external memory via package pins. You can add more or less memory controllers as per market-segment demands.

## Slide 34: One home node
No one goes there nowadays, it’s too crowded
  Yogi Berra
But how can we do better? Any suggestions?
P0
P1
P2
P3
L20
L21
L22
L23
L27
L26
L25
L24
HN
MC

## Slide 35: How do we fix this bottleneck?
Having one Home Node created a bottleneck.
  Why don’t we distribute it?
  In fact, why don’t we distribute it exactly how we distributed the L2?
Slice up the physical address space to make multiple Home Nodes.
  Each L2 slice pairs itself with one Home Node slice, both covering the same address range.
  For any address, we get one-stop shopping for the L2 data and for finding out which L1’s have the address and what state it’s in.
  One-stop shopping minimizes the number of ring messages that need to be sent.

## Slide 36: Ring cache with home nodes
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
P7
P6
P5
P4
L27+HN7
L26+HN6
L25+HN5
L24+HN4
MC0
MC1
This is a big picture! From now on we’ll just show the top half.

## Slide 37: Example: read miss on clean line
The read miss at the local node (e.g., P1) triggers a read request sent to home node (e.g., HN2), which has directory for that line.
HN2 sees the line is held by P0 and P4, and dirty bit is off. It turns on presence bit for requester, and responds with data from the L2.
M=0 1 0 0 0 1 0 0 0
Initial directory state
Final directory state
M=0 1 1 0 0 1 0 0 0

## Slide 38: Read miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held by P0 and P4.
P1
Message: read request by P1

## Slide 39: Read miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held by P0 and P4.
P1
Message: read request by P1. HN2 gets it, notes that the line is still clean.

## Slide 40: Read miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held by P0 and P4.
P1
Message: read data response

## Slide 41: Read miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held by P0 and P4.
P1
Message: read data response

## Slide 42: Example: read miss on line not in the L2
Same example, but this time the line is not in any caches. Instead, we must fetch it from memory.
M=0 0 0 0 0 0 0 0 0
Initial directory state
Final directory state
M=0 0 1 0 0 0 0 0 0

## Slide 43: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: read request by P1

## Slide 44: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: read request by P1. HN2 gets it, notes that the line is not in the L2 at all.

## Slide 45: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: memory read request by HN2

## Slide 46: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: memory read request by HN2. MC0 gets it and goes off-chip to read external memory.

## Slide 47: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: data returned from memory.

## Slide 48: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: data returned from memory. HN2 gets it, updates L22 and forwards the data to P1.

## Slide 49: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: read data response

## Slide 50: Read miss on line not in L2
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2
P1
Message: read data response

## Slide 51: Read Miss on Dirty line
The read miss at the local node (e.g., P1) triggers a read request sent to home node (e.g., HN2), which has directory for that line.
Read request sent to HN2.
HN2 sees dirty bit is on, tells P3 to write back data.
HN2 forwards data to P1.
M=1 0 0 0 1 0 0 0 0
Initial directory state
Final directory state
M=0 0 1 0 0 0 0 0 0

## Slide 52: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: read request by P1

## Slide 53: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: read request by P1. HN2 receives it, notices P3 holds the line dirty.

## Slide 54: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: evict, writeback to HN.

## Slide 55: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: evict/writeback to HN. P3 gets it and evicts the data from its L1.

## Slide 56: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: writeback data.

## Slide 57: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: writeback data. L22 receives it and updates L2 data and HN state.

## Slide 58: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: read data response

## Slide 59: Read miss on dirty line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Read miss from P1 to a line owned by HN2, held dirty by P3.
P1
Message: read data response

## Slide 60: Write Miss on Clean line
Core #1 wants to write an address.
HN2 sees the line is held by P0 and P2, and dirty bit is off.
HN2 sends invalidates to P0 and P2
HN2 tells P1 it can proceed with the write, and sets appropriate directory state.
M=0 1 0 1 0 0 0 0 0
Initial directory state
Final directory state
M=1 0 1 0 0 0 0 0 0

## Slide 61: Write miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Write miss from P1 to a line owned by HN2, held clean by P0 and P2.
P1
Message: write request by P1

## Slide 62: Write miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Write miss from P1 to a line owned by HN2, held by P0 and P2.
P1
Message: write request by P1. HN2 gets it, notes that the line is held clean by P0 and P2.

## Slide 63: Write miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Write miss from P1 to a line owned by HN2, held by P0 and P2.
P1
Message: GO to P1
Message: invalidate to P2
Why don’t we also send an invalidate to P0?
One ring slot can only hold one message at a time.

## Slide 64: Write miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Write miss from P1 to a line owned by HN2, held by P0 and P2.
P1
Message: GO to P1
Message: invalidate to P0

## Slide 65: Write miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Write miss from P1 to a line owned by HN2, held by P0 and P2.
P1
Message: invalidate to P0

## Slide 66: Write miss on clean line
P0
P1
P2
P3
L20+HN0
L21+HN1
L22+HN2
L23+HN3
MC0
Write miss from P1 to a line owned by HN2, held by P0 and P2.
P1
Message: invalidate to P0

## Slide 67: Interleaving
We said that cache lines are statically allocated to cache/HA slices. But how?
Which addresses should belong to each slice?
L20+HN0
L21+HN1
L22+HN2
L23+HN3
L27+HN7
L26+HN6
L25+HN5
L24+HN4
MC0
MC1

## Slide 68: Interleaving
Consider a 32-bit address, and one 8-core chip. There are two obvious ways to allocate lines to slices. What are the advantages to each? (Assume A5:0 = offset within line):
A31:9=index,tag within the cache; A8:6=slice
  Spreads consecutive lines all over the die, and minimizes hot spots.
A31:29=slice; A28:6=index,tag within the cache
  If the compiler+OS can have each thread use mostly the slice next to it, then this can be very fast.

## Slide 69: Interleaving across chips
Now assume four 8-core chips.
Each of the 32 HAs owns 1/32 of the address space. We do not give each chip the entire space (1/8 per HA).Why?
  Any 2 of the 32 P’s can share memory between them, even across chips. There must always be one HA controlling each address.
Assume address[5:0]=offset always.
A31:9=index,tag within the cache; A10:9=chip; A8:6=slice
  Spreads consecutive lines all chips! But off-chip wires are slow.
A31:30=chip; A29:27=slice; A26:6=index,tag
  Again, can work if you trust the compiler+OS
  But really we're asking them to predict future behavior
Most chips provide both choices; it would be interesting to know what Linux chooses. Final project?

## Slide 70: Summary
Cache coherence makes the existence of caching invisible to the software
  ensures that every thread has the same opinion about the value of any address
Coherence requires lots of communication between different cores and caches
Coherence is:
  fast when lines are only read but not written
  slow when lines are shared and also written, especially if they are written by multiple threads

## Slide 71: Beyond the ring
Counter-rotating rings are a great for medium numbers of cores (4-20 or so).
Not so good for 50 cores; an average latency of 12 hops is not great.
What is the next architecture after a ring?

## Slide 72: Mesh: a ring of rings
https://software.intel.com/en-us/articles/what-disclosures-has-intel-made-about-knights-landing

## Slide 73: Hot spots and π
Let's use some of what we've learned about caches
  Remember the π program?
  int owner=0;
  void pi_func (int me, int stride) {
    for (int i=me; i<N_TERMS; i += stride) {
      bool pos = ((i&1) == 0);
      while (owner != me)
        ;
      sum += (pos? term : -term);
      owner = (owner+1) % N_THREADS;
    }
  }

## Slide 74
  void pi_func (int me, int stride) {
    for (int i=me; i<N_TERMS; i += stride) {
      bool pos = ((i&1) == 0);
      while (owner != me)
        ;
      sum += (pos? term : -term);
      owner = (owner+1) % N_THREADS;
    }
  }
What might be a hot spot(s)? Why?
  The variable owner is accessed by every thread near continuously, and is written by each thread in turn.
  Every time it's written, the writer must invalidate every other copy.
  Then the other threads must re-fetch the line… all very tedious, and all over the ring. The more threads we have, the more invalidates we need
  Now we know why this was so slow!

## Slide 75: BACKUP

## Slide 76: Why add complexities?
Optimization usually implies complexity
The network is the computer (Sun motto)
People are willing to pay for a faster network
In your career, it seems:
  unlikely that you will be asked to design a new ISA
  probable that you will be asked to work on or with a new networking technology
And so the complexity is about to get worse – right now .

## Slide 77: Optimize a common case
Common case: i=i+1 in P1
  LD R1,R0(100); ADD R1,R1,#1; ST R1,R0(100)
When the ST occurs, P1 holds MEM[100] clean in its L1. Then the ST hits in the L1. What next?
  Can P1 just modify its L1, without asking the Home Node’s permission?
  No. What if another P also is holding MEM[100] clean and wants to write it?
This is a really common case; it would be nice if it were fast.
  Note it applies to both Directory and also Snoopy.

## Slide 78: MESI
Each L1 already needs Modified & Valid bits
MESI: each L1 can hold a line in one of 4 states:
  Modified: I have this line, and it’s dirty.
  Exclusive: I have a read-only copy, nobody else does
  Shared: More than one L1 has a read-only copy
  Invalid: OK, we actually don’t hold it at all .
Why do we need an “invalid” state?
  So that an empty entry doesn’t randomly match a tag.
The rules:
  The HN grants an L1 a line in M, E or S.
  An L1 can upgrade from E to M without telling the HN. The Home Node must take this into account.
  What is the consequence?
If the HN grants P1 a line in E, and then P2 requests a load, the HN must downgrade P1 from E to S.

## Slide 79: MESI changes the ISA
We now need two types of load
  Regular load, requesting data in S
  Read for ownership (RFO), requesting data in E.
RFO is a new instruction.
  Or a slight modification of the usual load instruction.
Compiler knows if it’s doing i=i+1
  Issues LD or RFO accordingly

## Slide 80: Example message set
P to HA messages:
  RFO, RdReqS: two different load requests
  ST: store request
  WBDataI: Writing back a dirty line, no longer hold it.
  WbDataS: ditto, but still hold it in S.
HA to P messages:
  DataS, DataE: data returned in S or E.
  DataM/Go: Here is data; you may own in M and store.
  Go-M: You may store in this line that you already own
  Evict: your L1 must evict a dirty line
  Inval: your L1 must invalidate a clean line
  DownM2S: you must downgrade from M to S.

## Slide 81: MESI example
P1: RFO R1, 100(R0)
  P1→HN: RFO
  HN→P1: DataE
P2: LD R1, 100(R0)
  P2→HN: RdReqS
  HN→P1: DownM2S
  HN→P2: DataS
Result: L1/P1 and L1/P2 both hold MEM[100] in S.

## Slide 82: Another MESI example
P1: RFO R1, 100(R0)
  P1→HN: RFO
  HN→P1: DataE
P1: ADD R1,R1,#1; ST R1,100(R0)
  No messages sent, but now L1/P1 holds 100 in M.
P2: LD R1, 100(R0)
  P2→HN: RdReqS ;; P2 wants data.
  HN→P1: DownM2S ;; P1 cannot have
                ;; exclusive rights
  P1→HN: WbDataS ;; Now P1 owns in S
  HN→P2: DataS ;; Now so does P2.

## Slide 83: Yet another
P3 does a store.
  P3→HA: ST;
  HA→P3: DataM/Go
P1 does a load.
  P1→HA: LD
  HA→P3: DownM2S ;; P3 owned it exclusively.
  P3 →HA: WbDataS ;; P3 writes back dirty data,
                ;; owns in S
  HA→P1: DataS ;; Now both P1 and P3 own in S.

## Slide 84: One final example
P1 does a load (not an RFO).
  P1→HA: LD;
  HA→P1: DataS
P1 & P2 both do a store, P2 wins the race
  P1 →HA: ST and P2→HA: ST ;; both want to write
  HA→P1: Inval ;; P2 wins, so P1 must evict.
                ;; P1 is surprised, but obeys.
  HA→P2: DataM/Go ;; HA says P2 can store.
  HA→P2: Evict ;; But now P1 gets its turn.
  P2→HA: WBDataI ;; So P2 evicts.
  HA→P1: DataM/Go

## Slide 85: Try this on your own
P1 does an RFO
P1 does a store
P3 does a store.
P1 does a load.
P1 & P2 both do a store, P2 wins the race

## Slide 86: Write Miss on Dirty line
Guess what? This one will be in the homework.