## Slide 1: EE 193: Parallel Computing
Fall 2017
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lecture 8: GPUs

## Slide 2: Goals
Primary goals:
  Learn about GPU architecture
  Compare it with CPU architecture
  Understand what each is good at
Secondary goals
  Learn about GPU programming
  HW #4 will require programming in CUDA

## Slide 3: CPU vs. GPU, once more
It's finally time to understand what's going on here
 | Haswell Server | Nvidia Pascal P100
# cores | 18 | 3840
Die area | 660 mm2 (22nm) | 610 mm2 (16nm)
Frequency | 2.3 GHz normal | 1.3 GHz
Max DRAM BW | 100 GB/s | 720 GB/s
LLC size | 2.5 MB/core (L3) | 4 MB L2/chip
LLC-1 size | 256K/core(L2) | 64 KB/SM (64 cores)
Registers/core | 180 per 2 threads | 500
Power | 165 watts | 300 watts
Company market cap | $160B | $90B

## Slide 4: The history of GPUs
Some history:
  In the early 90s, we had massively parallel machines from Cray and Thinking Machines. They had some great successes, but no widespread adaptation.
  They were displaced by clusters of cheap μprocessors.
  But then μprocs stopped getting faster.
  Early GPUs were great for graphics, but required custom software in a shading-focused language
  Then CUDA (Compute Unified Device Architecture) came along; it’s a small set of extensions to C.

## Slide 5: Computes vs. memory
Maximum DRAM bandwidth = 720 GB/sec
How many floats/sec can you get?
  (720 GB/sec)*(1 float/4B) = 180 Gfloats/sec
How many floating-point operations can you get?
  (1.3G cycles/sec)*(1 op/cycle)*(3840 cores)= 5000 Gflop/sec
  (5000 Gflop/sec)*(2 operands/flop) = 10000 G floats/sec
Compute/mem ratio = 10000 / 180 = 50

## Slide 6: GPU architecture, take 1
This doesn’t work well
  No cache means DRAM is the only way to drive the cores
  50:1 compute-to-memory ratio is too high to feed the cores from DRAM
  Conclusion: so many cores, and no way to get data to them.
10 bazillion little cores
Little really means:
pretty much no cache
no OOO, speculative, branch prediction, etc.
8 DRAM controllers

## Slide 7: GPU architecture, take 2
It's still no good for streaming data and only using it once.
Suddenly it works really well for block-matrix problems
Shared memory is big enough to hold 3 blocks that are big enough to deal with a 50:1 compute/memory ratio.
GPU people call them tiles rather than blocks.
A few dozen Streaming Multiprocessors (SM). Each has
no OOO, speculative, branch prediction, etc.
just enough memory for block-matrix algorithms
8 DRAM controllers
shared memory
shared memory
…

## Slide 8: In-class exercise
An NxN matrix multiply:
  uses 3N2 floats
  requires N3 FLOPs
For block matrix, the above is true for each block triplet.
The NVidia Pascal has 64 KB of shared mem per SM. What size blocks can fit in there, and what is the computes/memory ratio for that block size?
  64KB = ?? floats
  That's 3 blocks of ?? floats each
  ?? floats = ?? block size.
  # of computes = ??3  ??
  Amount of data required = 3*??2  ??
  Ratio≡ (computes/sec)/(bytes/sec) = ??/??  ??
It's not quite 50x, but still enough to keep most of the cores busy most of the time.
  And remember that some of the blocks don’t need to be fully in cache
16K floats
5333 floats each
5333 floats = 73x73 block size
733 = 390000
3*732 = 16000
390000/16000  24

## Slide 9: GPU architecture, take 2
A few dozen Streaming Multiprocessors (SM). Each has
no OOO, speculative, branch prediction, etc.
just enough memory for block-matrix algorithms
8 DRAM controllers
shared memory
shared memory
…

## Slide 10: More on SMs
Pascal has 64 cores/SM. Why so many? How did they pick 64?
  It’s about the right amount of compute power to handle one block in about how long it takes to load it.
  Because we have to in order to get reasonable performance. The cores have no OOO, branch prediction, etc.
  Because we can . Unlike C++ threads, CUDA lets us decide which threads work together to share a cache (well, more precisely, which threads share ShMem). So more threads really can work well together

## Slide 11: The individual cores are not good
Again: no OOO, speculation or branch prediction
So why aren't they almost always stalled?
  Lots of SMT.
  Lots of threads available, and switch on every stall.
  Of course, none of this can fix a low compute/memory ratio; but block-matrix already fixed that

## Slide 12: The scheduling problem
Solution: the warp
  threads are grouped into warps of 32 threads/warp.
  the threads in a warp always travel together
  we schedule entire warps, not individual threads
The scheduling problem just got 32x easier 
Pascal numbers: each SM has
64 FP32 cores, 32 FP64 cores, 16 LD/ST cores
up to 1000 or so threads
Building a scheduler that swaps 1000 threads in and out every cycle is not really practical.
8 DRAM controllers
…
shared memory
1000 threads + scheduling
shared memory
1000 threads + scheduling

## Slide 13: More detail on a warp
What does it mean for 32 threads to be "grouped"?
  In any given cycle, every thread executes the same instruction.
  All 32 threads proceed in lockstep, executing the same instruction.
Nvidia's term: Single Instruction Multiple Threads (SIMT)
  Arguably, it sounds a lot like SIMD. One instruction, 32 data values
The downsides:
  If one thread has a memory miss, they all stall
  If one thread is waiting for an operand, they all stall
What if there's an "if" statement and some threads branch and some don't?
  Don't even think about it for now!

## Slide 14: A rose by any other name
Why is “warp” called a warp?
  Common usage for weaving on a loom: a warp is a group of parallel threads.
  It got adapted by Nvidia.
  Cute? Not everybody thinks so

## Slide 15: History
GPGPUs mostly driven by Nvidia, and they picked their own names.
  Both for the hardware, and software (CUDA)
  Some say they're not as descriptive as they could be.
ATI (bought by AMD in 2006) also makes GPUs.
  They didn't like Nvidia's names
  Apple developed OpenCL (with help from ATI & others)
OpenCL changed all of the names
In case that's not enough…

## Slide 16: If that's not bad enough…
Hennessy and Patterson: the classic book(s) on computer architectures
  Added a chapter on GPGPUs. But guess whose terminology they picked?
  You guessed it. H&P didn't like Nvidia's terminology or OpenCL's . And so they made up their own.
  Now there are three completely different ways to say the same thing, for pretty much every concept.
We’ll stick with the Nvidia naming in this course.

## Slide 17: The table of terminology
w
Nvidia | OpenCL | Henn & Patt
Streaming multiprocessor | Compute unit | 
CUDA core | SIMD unit | 
Shared memory | Local memory | 
Grid | NDRange | Vectorized loop
Block | Workgroup | Body of a vectorized loop
Warp | Wavefront | Thread of SIMD instructions
Thread | Work item | Sequence of SIMD lane ops
Gigathread scheduler |  | Thread-block scheduler

## Slide 18: Where to put the registers?
Consider the following:
  warp #1 is running in cores #0-31
  warp #1 stalls and gets swapped out.
  warp #2 is ready, and gets put into cores #0-31
  warp #1 becomes ready, but warp #2 is still in cores #0-31, so warp #1 gets put into cores #32-63.
The bottom line: if you want to keep the cores busy as much as possible, you must let threads migrate from core to core easily.
Any processor needs registers
even a dumpy little processor.
Should we put the regs into the cores?
Pro: that's kind of the standard place to put them!
8 DRAM controllers
…
shared memory
1000 threads + scheduling
shared memory
1000 threads + scheduling

## Slide 19: Registers
Problem:
  if you want to keep the cores busy as much as possible, you must let threads migrate from core to core easily
  but a thread needs to keep the same register values as it gets swapped out & back in.
  keeping the registers in the cores would mean swapping registers in and out frequently to some backup storage.
Alternate solution:
  Store the registers for all cores in a SM outside of the cores. Yes, it's one very big regfile! (But very little cores)
  Each thread keeps a pointer into the regfile for its base.

## Slide 20: GPU architecture, take 3
Warps can now move from one set of 32 cores to a different set very easily. They use the same registers no matter which core they live in.
The 64K registers can limit the total number of threads that can live in a SM
(# of threads/SM) must be < 64K / (# of regs/thread)
Pascal has 64K regs/SM, or roughly 500/core.
8 DRAM controllers
…
shared memory
64K registers
1000 threads + scheduling
shared memory
64K registers
1000 threads + scheduling

## Slide 21: Compare this to a CPU
Modern CPUs have many more actual (physical) regs/core than the architecture states. Why?
  To support multithreading
  Register renaming for OOO, loop unrolling
GPUs have thrown away the second usage, and reused the resulting area to expand the first usage (from 2 threads to hundreds)

## Slide 22: CPU vs. GPU, explained
We can explain a fair amount of this now!
Key concept: remove cache (leaving only enough to hold blocks)…
 | Haswell Server | Nvidia Pascal P100
# cores | 18 | 3840
Die area | 660 mm2 (22nm) | 610 mm2 (16nm)
Frequency | 2.3 GHz normal | 1.3 GHz
Max DRAM BW | 100 GB/s | 720 GB/s
LLC size | 2.5 MB/core (L3) | 4 MB L2/chip
LLC-1 size | 256K/core(L2) | 64 KB/SM (64+ cores)
Registers/core | 180 per 2 threads | 500
Power | 165 watts | 300 watts
Company market cap | $160B | $90B
use the resulting space for lots of small cores
Enough regs to quickly swap many threads

## Slide 23: Pascal die photo
Memory controller (x8)
SM
L2 cache

## Slide 24: Streaming multiprocessor photo
Core
Register file
Shared memory
Warp scheduler

## Slide 25: Haswell server
Compare how much of the die is L3 cache!

## Slide 26: Scale a vector
void scale (int N, int a, float *x) {
  for (int i = 0; i < N; i++)
    x[i] = a*x[i];
}
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  // Run kernel on 1M elements on the CPU
  scale (N, 2.0, x.data());
}
This is our first GPU program.
  OK, it doesn't actually use the GPU!
  But we can compile it with nvcc anyway.
C++ shorthand: says to initialize the array with N elements, all of which are 3.0
.data() gets a pointer to the first data element.

## Slide 27: Scale a vector
__global__ void scale (int n, int a, float *x) {
  for (int i = 0; i < n; i++)
    x[i] = a*x[i];
}
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,1.0);
  // Run kernel on 1M elements on the CPU
  scale (N, x.data(), y.data());
}
First part: tell nvcc that the scale() function should live on the GPU.
Problem: the GPU does not have access to CPU memory
says that this function will live on the GPU, not the CPU.
this will crash now.

## Slide 28: Board-level architecture
The CPU and GPU can talk to each other
  neither can talk to the other's memory
Why not?
  Controlling memory is not easy (must coordinate Home Agents, coherence, etc)
  The latest GPUs can do this (as of Pascal)
  Our labs don't have Pascal GPUs (yet).
GPU
GPU memory
CPU
CPU memory

## Slide 29: Scale a vector
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  float *device_array;
  cudaMalloc ((void **)&device_array, 4*N);
  cudaMemcpy (device_array, x.data(), 4*N,
  cudaMemcpyHostToDevice);
  scale (N, 2, device_array);
}
Now we have moved the input data to GPU memory
The scale() call no longer crashes 
pointer into GPU memory
allocates GPU memory, sets device_array. Returns cudaSuccess (hopefully)
Copies from host to GPU memory. Also returns status. Argument order is dest, src, nBytes, mode

## Slide 30
__global__ void scale (int n, int a, float *x) {
  for (int i = 0; i < n; i++)
    x[i] = a*x[i];
}
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  float *device_array;
  cudaMalloc ((void **)&device_array, 4*N);
  cudaMemcpy (device_array, x.data(), 4*N,
  cudaMemcpyHostToDevice);
  scale (N, 2, device_array);
}
Now scale() gets a pointer into GPU memory, so it runs fine.
But where does it place its results?
GPU memory 
The output is stuck in GPU memory 

## Slide 31
Now everything is copacetic
  It all works.
  I never promised this would be painless 
  If we wanted to pass multiple arrays, we would have to do all of this multiple times.
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  float *device_array;
  cudaMalloc ((void **)&device_array, 4*N);
  cudaMemcpy (device_array, x.data(), 4*N,
  cudaMemcpyHostToDevice);
  scale (N, 2, device_array);
  cudaMemcpy (x.data(), device_array, 4*N,
  cudaMemcpyDeviceToHost);
}
copies in the reverse direction.
copies in the reverse direction.

## Slide 32: We're not done yet
We still haven't talked about threads
  And that was kind of the whole point of GPUs
We’ve learned how to use C++ threads, but that’s not relevant on a GPU. Time to learn how CUDA does it.
What problems would we like to solve?
  creating a new thread with C++ threads was slow
  C++ threads did not allow us to specify which threads worked together in one core
GPUs create lots of threads
GPU hardware has 50+ small cores sharing SM – we must be able to divide the work accordingly

## Slide 33: Start with C++-like threading
Many, many function calls → it will be slow
So just get rid of the loops 
And we will add “stuff” to tell CUDA about the loops we removed
__global__ void scale (int me, int a, float *x) {
  for (int i=me*ELE_PER_TH; i< (me+1)*ELE_PER_TH; ++i)
    x[i] = a*x[i];
}
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  float *device_array;
  cudaMalloc, etc…
  for (int th = 0; th < N_THREADS; ++th)
    threads.push_back (thread (scale, th, 2, device_array);
  for (auto &th:threads)
  th.join();
}
scale <<<stuff>>> (2, device_array)

## Slide 34: Start with C++-like threading
Groups of 256 threads work together on one streaming multiprocessor with the same shared memory
There are N_THREADS/256 such groups
Now we can declare which threads work together and share a “cache.”
__global__ void scale (int me, int a, float *x) {
  for (int i=me*ELE_PER_TH; i< (me+1)*ELE_PER_TH; ++i)
    x[i] = a*x[i];
}
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  float *device_array;
  cudaMalloc, etc…
  scale <<<stuff>>> (2, device_array);
}
scale <<<N_THREADS/256, 256>>> (2, device_array)

## Slide 35: CUDA threading
All of the threads together are called a grid.
You manually divide the grid into thread blocks.
  The threads in any one thread block work together using shared memory; different thread blocks interact very little
Scheduling:
  The GPU allocates thread blocks to streaming multiprocessors
  Each SM breaks its thread block into warps of 32 threads (invisibly to you), and schedules warps on cores.
I think this is another weaving term
__global__ void scale (int me, int a, float *x) {
  for (int i=me*ELE_PER_TH; i< (me+1)*ELE_PER_TH; ++i)
    x[i] = a*x[i];
}
int main(void) {
  int N = 1<<20; // 1M elements
  vector<float> x(N,3.0);
  float *device_array;
  cudaMalloc, etc…
  scale <<<N_THREADS/256, 256>>> (2, device_array);
}
But what about this?

## Slide 36
Now each thread knows who it is, and can figure out what to work on.
We essentially did the same thing with our C++ threads code – we passed a threadID to each thread
  This is the same, but with more hierarchy
  It fixes the problem of not being able to assign which threads work together.
__global__ void scale (int n, int a, float *x) {
  int i = blockIdx.x * blockDim.x + threadIdx.x; x[i] = a*x[i];
}
int main(void) {
  …
  scale <<<N_THREADS/256, 256>>>
  (N, 2, device_array);
  …
}
Special variables tell each thread who it is.
blockIdx tells a thread which thread block it's in; from [0,N/256)
blockDim is 256 here
threadIdx gives the thread # within a block; so [0,255].
We'll talk about the ".x" shortly…

## Slide 37: A few details
One thread block can have at most 32 warps (1024 threads)
Remember: you want many more threads than cores on each SM
  Pascal has 64+ cores, so one thread block can more than keep them busy.
  The GPU may put multiple thread blocks in one SM if each thread block doesn't use too much shared memory, registers; this is not under your control.

## Slide 38: In-class exercise
Roughly how long does the function we wrote take to run?
Our vector had 1M floats
GPU speed=1.3 GHz, 3840 cores.
GPU
GPU memory
CPU
CPU memory
100 GB/s
720 GB/s
16-80 GB/s
Communication between CPU↔GPU is 16 GB/s over PCI/E or 80 over NVlink. Assume 80.

## Slide 39: In-class exercise
Memory:
  1M floats = ??MB
  It must travel from CPU memory→CPU→GPU memory→GPU and back.
  Memory time: roughly speaking, assume 80 GB/s is the weak link in the chain.
  Then 4MB * 2 * (80000MB/s)-1 = .1ms.
Computes:
  Compute capability: 1.3GHz * 3840 cores  ?? GFLOPS
  Compute time: (1M computations) * ??
GPU
GPU memory
CPU
CPU memory
100 GB/s
720 GB/s
16-80 GB/s
Communication between CPU↔GPU is 16 GB/s over PCI/E or 80 over NVlink. Assume 80.
It's often the case that it takes longer to get the data to/from the GPU than to do the computation.
4MB
5000 GFlops
(5000 GFLOPS)-1=.2us

## Slide 40: Where are we?
We have a first-cut understanding of the hardware
We've seen how a simple program works
We know that the trick to using a GPU efficiently is to find a problem that uses lots of computes on the relatively small amount of data.
Our next example… you guessed it
  Matrix multiply 

## Slide 41: Matrix multiply for a CPU
This was our first attempt. Remember why we chose the ordering rB, kB, cB?
  Prevent the B matrix from being accessed in column-major order
Is this still an issue for a GPU?
  Our goal is to have all 3 blocks fit in one multiprocessor’s shared memory, so perhaps access will be fast no matter what.
for rb=0…Nb-1
  for kb=0..Nb-1
    for cb=0..Nb-1
      for ri=0..Ni-1
        for ki=0..Ni-1
          for ci=0..Ni-1
            r = rb*Ni+ri; k = kb*Ni+ki; c = cb*Ni+ci;
            C[r,c] += A[r,k]*B[k,c];
Pick the block
One thread per block triplet

## Slide 42: Matrix multiply for a GPU
Let's change the ordering to be more conventional
  motto: don’t add complexity until we know we need it
Our first job: decide how to divvy up the work into thread blocks; i.e., how much work goes on one multiprocessor
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];

## Slide 43: Matrix multiply for a GPU
Suggestions?
  One obvious solution: each block triplet goes to a thread block.
  The block triplet will go into shared memory
How many thread blocks will we have?
  Nb3
Each thread block is in the same grid, and all can potentially execute at once (if we had enough thread blocks)!
The GPU can give thread blocks to SMs in any order
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
This code goes into a thread block
Each instance of this thread block (no matter how many threads it is) all gets executed by one SM and can share memory

## Slide 44: Matrix multiply for a GPU
Next problem: divide the thread block into threads
How many FLOPs in one thread block?
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
One thread block per block triplet
Ni3

## Slide 45: Matrix multiply for a GPU
Can we use 1 thread for all Ni3 FLOPs?
  No. In any SM, we want many more threads than cores
How about Ni threads, each with Ni2 FLOPs?
  64x64 blocks would mean 64 threads/SM; still not enough threads.
How about Ni3 threads, each with 1 FLOP?
  That's a bit silly, even for a GPU
OK, only one choice left 
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
One thread block per block triplet

## Slide 46: Matrix multiply for a GPU
Ni2 threads, each with Ni FLOPs
Each thread does one full ki loop, and works on one element of C.
Good enough for now. Time to code it.
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
Ni2 threads
Each thread does this
This is one thread block

## Slide 47: Matrix multiply for a GPU
Next, write main()
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
Ni2 threads
Each thread does this
This will go into main()
This will go into main()
This will be our thread function

## Slide 48: Matrix multiply for a GPU
Get rid of the per-thread metacode
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
This will go into main()
This will go into main()
This will be our thread function

## Slide 49: Matrix multiply for a GPU
Put it into main() and add the call to make a thread
This isn't quite it; remember that CUDA has a different syntax to spawn threads
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
This will go into main()
This will go into main()
main() {
}
spawn a thread();

## Slide 50: Matrix multiply for a GPU
Here's our start – tell CUDA the number of thread blocks per grid, and threads per thread block.
  Of course, the product of those two will equal total # of threads.
main() {
  int thBlocks_per_grid=Nb3,
    threads_per_thBlock = Ni2;
  one_thread <<<thBlocks_per_grid, threads_per_thBlock>>> ()
}
Look back to foil 43 if we forgot where these numbers came from

## Slide 51: Matrix multiply for a GPU
We still have to write the per-thread code
Any problem with this code?
  How does one_thread know rb, ri, cb, cb and kb?
  We can't pass them from main() as parameters; they’re no longer in main().
main() {
  int thBlocks_per_grid=Nb3,
    threads_per_thBlock = Ni2;
  one_thread <<<thBlocks_per_grid, threads_per_thBlock>>> ()
}
__global__ one_thread () {
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}

## Slide 52: Special variables
Remember what we did for our vector scaling?
Let’s do it again for matrix multiply
__global__ void scale (int n, int a, float *x) {
  int i = blockIdx.x * blockDim.x + threadIdx.x; x[i] = a*x[i];
}
int main(void) {
  …
  scale <<<N/256, 256>>> (N, 2, device_array);
  …
}
Special variables tell each thread who it is.
blockIdx tells a thread which thread block it's in; from [0,N/256)
blockDim is 256 here
threadIdx gives the thread # within a block; so [0,255].

## Slide 53: Matrix multiply for a GPU
Yes, we can – let’s see how
main() {
  int thBlocks_per_grid=Nb3,
    threads_per_thBlock = Ni2;
  one_thread <<<thBlocks_per_grid, threads_per_thBlock>>> ()
}
__global__ one_thread () {
  given blockIdx.x, blockDim.x and threadIdx.x, can we figure out rb, ri, cb, ci, and kb?
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}

## Slide 54
Assume that the matrix is a 16x16 array of blocks (so Nb=16). Then blockIdx.x ranges from …?
  0 to 163 (so, 12 bits)
How would we decompose blockIdx.x into rb, cb, kb?
  Say, bits[11:8]→rb, bits[7:4]→ cb, bits[3:0]→ kb.
Let each block be 32x32 elements (so Ni=32). So threadIdx.x ranges from …
  0 to 322 (so, 10 bits)
How would we decompose threadIdx.x into ri, ci?
  Say, bits[9:5]→ri, bits[4:0]→ ci.
main() {
  one_thread <<<Nb3, Ni2>>> ()
}
__global__ one_thread () {
  decompose blockIdx.x into rb, cb, kb;
  decompose threadIdx.x into ri, ci;
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            …
One thread block per block triplet
Ni2 threads

## Slide 55
This seems a bit too much work. We put together a 12-bit blockIdx.x, and then broke it into rb, cb, kb. And similar for threadIdx.
  Can we avoid this work?
  And the complexity?
main() {
  one_thread <<<Nb3, Ni2>>> ()
}
__global__ one_thread () {
  decompose blockIdx.x into rb, cb, kb
  decompose threadIdx.x into ri, ci
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}
for kb=0…Nb-1
  for rb=0..Nb-1
    for cb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            …
One thread block per block triplet
Ni2 threads

## Slide 56
No more decomposition needed 
Note: CUDA uses dim3 even for 2D things!
  Unspecified dimensions default to 1. There is no dim2
main() {
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni)
  one_thread <<<thBlocks, threads>>> ()
}
__global__ one_thread () {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            …

## Slide 57
This is starting to look like a nice GPU program. But we have a few more odds and ends left.
main() {
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni);
  one_thread <<<thBlocks, threads>>> ();
}
__global__ one_thread () {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}

## Slide 58
We still need to use cudaMalloc (), cudaMemcpy () to move data between CPU↔GPU
  It's tedious, since we must deal with all three matrices
  For clarity, let's not… and say we did 
  And we have to pass the data’s location to one_thread()
main() {
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni);
  one_thread <<<thBlocks, threads>>> ();
}
__global__ one_thread () {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    C[r,c] += A[r,k]*B[k,c];
}

## Slide 59: Moving the data
Move the data
  cudaMalloc (), cudaMemcpy ()
GPU
GPU memory
CPU
CPU memory

## Slide 60
main () {
  cudaMalloc ((void **)&d_A, 4*N2);
  cudaMalloc ((void **)&d_B, 4*N2);
  cudaMalloc ((void **)&d_C, 4*N2);
  // use cudaMemcpy() to move A and B from host to device
  cudaMemcpy (d_A, A.data(), 4*N2, cudaMemcpyHostToDevice);
  cudaMemcpy (d_B, B.data(), 4*N2, cudaMemcpyHostToDevice);
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni);
  one_thread <<<thBlocks, threads>>> (d_A, d_B, d_C);
  cudaMemcpy (C.data(), d_C, 4*N2, cudaMemcpyDeviceToHost);
}

## Slide 61
Any issues?
  We would need to translate from 2D array indices to 1D
  But we have bigger fish to fry…
main() {
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni);
  one_thread <<<thBlocks, threads>>> (d_A, d_B, d_C);
}
__global__ one_thread (float *d_A, float *d_B, float *d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    d_C[r,c] += d_A[r,k]*d_B[k,c];
}

## Slide 62: Moving the data
Good. Now we've moved data between CPU memory and GPU memory.
But how do we get data from GPU memory to the appropriate streaming-multiprocessor shared memory?
  Shared memory is not a cache. A cache is invisible to the programmer, since it's fully managed by the hardware.
  We must manage shared memory ourselves!
  GPUs are fast… but it’s not a free lunch
GPU
GPU memory
CPU
CPU memory

## Slide 63: Shared memory
The whole idea of using a GPU was to store the block triplet for any thread block in the shared memory of the SM that's executing the thread block.
We still have to do that – but how?

## Slide 64
A __shared__ variable has thread-block-wide scope; each thread block effectively has its own SA (unsurprisingly)
Problem: every single thread copies the entire matrices.
__global__ one_thread (float *d_A, float *d_B, float *d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  for r=0..Ni-1
    for c=0..Ni-1
      SA[r, c] = d_A[f(r,c,rb,kb)];
  for ki=0..Ni-1
    r = rb*Ni+ri; c = cb*Ni+ci; k = kb*Ni+ki;
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}
__shared__ tells nvcc to put a variable in shared memory
Bonus: now we can declare 2D arrays
These arrays are the three blocks
copy the arrays ("" for SB)
At some point we'll have to copy back C[]

## Slide 65
Why don't we also check rb and cb?
  Then not all of the SMs would initialize their shared memory
Problems with this?
  It doesn't take advantage of parallelism
  It doesn't actually work. There is a race. What is the race?
__global__ one_thread (float * d_A, float * d_B, float * d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  if ((ri==0) && (ci==0))
    for r=0..Ni-1
      for c=0..Ni-1
        SA[r, c] = d_A[f(r,c,rb,kb)];
        SB[r, c] = d_B[f(r,c,kb,cb)];
  for ki=0..Ni-1
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}
The if statement says that only one thread per block will do the copy

## Slide 66
Different warps in a thread block each advance independently; one warp may start computing before a different warp has loaded the needed data.
__global__ one_thread (float * d_A, float * d_B, float * d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  if ((ri==0) && (ci==0))
    for r=0..Ni-1
      for c=0..Ni-1
        SA[r, c] = d_A[f(r,c,rb,kb)];
        SB[r, c] = d_B[f(r,c,kb,cb)];
  for ki=0..Ni-1
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}

## Slide 67
Now we have nice parallelism for our loads; we still must fix the race.
__global__ one_thread (float * d_A, float * d_B, float * d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  if ((ri==0) && (ci==0))
    for r=0..Ni-1
      for c=0..Ni-1
        SA[ri, ci] = d_A[f(ri,ci,rb,kb)];
        SB[ri, ci] = d_B[f(ri,ci,kb,cb)];
  for ki=0..Ni-1
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}
Each thread in the thread block copies one element

## Slide 68
__syncthreads() is a software barrier.
  Within any thread block: all threads wait at the barrier until every thread in the thread block reaches it.
  Across thread blocks: does nothing.
  The race is fixed
__global__ one_thread (float * d_A, float * d_B, float * d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  SA[ri, ci] = d_A[f(ri,ci,rb,kb)];
  SB[ri, ci] = d_B[f(ri,ci,kb,cb)];
  __syncthreads();
  for ki=0..Ni-1
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}

## Slide 69: One final issue
Yes. Each value of kb is in a different thread block
  Each thread block with different kb but the same rb, cb will try to write the same element in d_C.
__ global__ one_thread (float *d_A, float *d_B, float *d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  SA[ri, ci] = dA[f(ri,ci,rb,kb)];
  SB[ri, ci] = dB[f(ri,ci,kb,cb)];
  __syncthreads();
  for ki=0..Ni-1
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}
main() {
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni)
  one_thread <<<thBlocks, threads>>> (d_A, d_B, d_C)
}
Do we need a critical section here?

## Slide 70: Matrix multiply for a GPU
We had a design issue from the beginning.
There are Nb different block triplets with the same rb and cb but different kb.
  Each of these works together to calculate the same block of C.
They need a critical section. Can we even do that in CUDA?
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r=rb*Ni+ri; c=cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
One thread block per block triplet
Ni2 threads
Each thread does this

## Slide 71: Matrix multiply for a GPU
CUDA does let you do critical sections.
It's usually a bad idea, though; it means that most threads are stalled while one thread works
  It's very inefficient
  Goes against the idea of a warp
Brainstorm: can we change our design to avoid needing it?
for rb=0…Nb-1
  for cb=0..Nb-1
    for kb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for ki=0..Ni-1
            r=rb*Ni+ri; c=cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
Pick the block triplet
One thread block per block triplet
Ni2 threads per thread block
Each thread does this

## Slide 72
Have we fixed our race? Is there any way that two different threads can try to modify the same element in C?
  It is fixed.
  The only possible conflict occurs when different threads have the same rb, cb, ri and ci but different kb or ki.
In this code, each single thread handles:
  one combination of rb, cb, ri and ci
  all values of kb and ki for that combination
for rb=0..Nb-1
  for cb=0..Nb-1
      for kb=0…Nb-1
        for ri=0..Ni-1
          for ci=0..Ni-1
            for ki=0..Ni-1
              r=rb*Ni+ri; c=cb*Ni+ci; k = kb*Ni+ki;
              C[r,c] += A[r,k]*B[k,c];
One thread block per rb, cb
Ni2 threads each block
Each thread does this

## Slide 73
All of our high-level problems are now solved
HW4 is to turn this into code, and run it on a GPU
for rb=0..Nb-1
  for cb=0..Nb-1
      for ri=0..Ni-1
        for ci=0..Ni-1
          for kb=0…Nb-1
            for ki=0..Ni-1
            r=rb*Ni+ri; c=cb*Ni+ci; k = kb*Ni+ki;
            C[r,c] += A[r,k]*B[k,c];
One thread block per rb, cb
Ni2 threads
Each thread does this

## Slide 74: Thread blocks
Each thread block computes one block of C
We’re giving our thread blocks a 2D indices (these correspond to rb, cb).
=
*
C
A
B
0,0 0,1
1,0 1,1

## Slide 75: Threads in a thread block
Each thread computes one element of C
We’re giving our threads 2D indices within a thread block (these correspond to ri, ci).
Note each of the 4 thread blocks has 16 threads, numbered 0,0 to 3,3.
=
*
C
A
B
00
01
10
11
02
03
12
13
20
21
30
31
22
23
32
33

## Slide 76: Which parts of A and B are used
Each output block needs values from whole row of blocks from A and a whole column of blocks from B.
When kb=0, one pair of blocks is in shared memory for this thread block; when kb=1, we must swap the other pair of blocks into shared memory instead.
=
*
C
A
B
00
01
10
11
02
03
12
13
20
21
30
31
22
23
32
33
kb=0 kb=1
kb=0
kb=1

## Slide 77: Which parts of A and B are used
Each thread computes one element of C
It uses an entire row from A and an entire column from B
All 16 threads in a thread block are working (in principle) at the same time.
All 4 thread blocks are working (in principle) at the same time.
=
*
C
A
B
00
01
10
11
02
03
12
13
20
21
30
31
22
23
32
33
kb=0 kb=1
kb=0
kb=1

## Slide 78: In-class example, part 1
__ global__ one_thread (float *d_A, float *d_B, float *d_C) {
  rb=blockIdx.x; cb=blockIdx.y, kb=blockIdx.z;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  SA[ri, ci] = dA[f(ri,ci,rb,kb)];
  SB[ri, ci] = dB[f(ri,ci,kb,cb)];
  __syncthreads();
  for ki=0..Ni-1
    SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
}
main() {
  dim3 thBlocks (Nb,Nb,Nb), threads (Ni,Ni)
  one_thread <<<thBlocks, threads>>> (d_A, d_B, d_C)
}
kb is no longer passed to us (one thread block per rb, cb)
We need a loop for kb
Need to understand this 

## Slide 79: In-class example, part 2
__ global__ one_thread (float *d_A, float *d_B, float *d_C) {
  rb=blockIdx.x; cb=blockIdx.y;
  ri =threadIdx.x; ci=threadIdx.y;
  __shared__ float SA[Ni][Ni], SB[Ni][Ni], SC[Ni][Ni];
  for kb=0..Nb-1 {
    SA[ri, ci] = dA[f(ri,ci,rb,kb)];
    SB[ri, ci] = dB[f(ri,ci,kb,cb)];
    __syncthreads();
    for ki=0..Ni-1
      SC[ri,ci] += SA[ri,ki]*SB[ki,ci];
  }
}
main() {
  dim3 thBlocks (Nb,Nb), threads (Ni,Ni)
  one_thread <<<thBlocks, threads>>> (d_A, d_B, d_C)
}
Make sure that all threads in this block are finished with the old kb before loading the blocks for this kb
Write data back to d_C.
Each thread does all of the work to calculate one element of C. Do we need SC at all, or just one variable “sum” per thread?
What is this function?

## Slide 80: L1 and L2 caches, local mem
Most GPUs actually do have caches (just not very big).
Pascal:
  24KB(?) L1 cache/SM (HSX=256K/core).
  4MB L2 cache/die (HSX=2.5MB/core)
Why bother with an L1?
  Primarily useful for thread-local variables (if you don't have enough registers, and do have temporal locality)
  Big enough to give "reasonable" performance if you don’t take too much time optimizing for shared memory.
  L1 is not coherent!
Why bother with an L2?
  L2 can be useful to even out bursty memory requests
  May even be able to hold some blocks for reuse across SMs.

## Slide 81: Types of functions
Three types of functions:
  __host__ is the default; functions that live on the CPU.
  __device__ is a function that lives on the GPU and can only be called from other GPU functions
  __global__ is a function that lives on the GPU and can be called from the CPU. This is often called a kernel function.

## Slide 82: Types of variables
A function that lives on the GPU (i.e., __device__ and __system__) can qualify its variables in various ways:
  unqualified: a simple variable lives in a register; if it's an array it lives in shared memory.
  __shared__: we've already seen this; the variable lives in shared memory.
  __device__: one copy, lives in GPU memory and is shared by every thread across all blocks. It can still be cached in L2 or L1. Remember, though, that L1 is not coherent!

## Slide 83: Shared-memory banks
What are banks?
  One large memory (like shared memory) gets divided into multiple small pieces.
Why have banks?
  Often, physical reasons (loading, RC)
  But a GPU has more reasons

## Slide 84: CPU requirements
What we really want for a CPU L1 cache
memory
address
data
thread0
Nice model, but we still have to build it.
GPU shared memory: the same problem, bigger scale
  Every thread in a warp will want to access memory all at once
  That’s 32 threads!
address
data
thread1

## Slide 85: GPU requirements
All threads in a warp execute the same instruction
If it’s a load… they all want to access shared mem at once
How do we build a memory that can do this?
address
data
thread0
thread31
memory
…
…
address
data

## Slide 86: Banks are the answer
Banks is to allow simultaneous access to different addresses.
Each bank is a separate little memory
Both threads can access memory at once (as long as they use different banks)
Life is copacetic… but what about a GPU?
address
data
thread0
address
data
thread1
memory
bank0
bank1
bank31
…
WIRES

## Slide 87: Onto a GPU
It works for a GPU, too
Most GPUs have 32 banks in shared memory
address
data
thread0
thread31
memory
bank0
bank1
bank31
…
WIRES,
WIRES,
WIRES
…
…
address
data
THE RULES
All 32 threads in a warp can access at once: if
  each one accesses a different bank, or
  two threads can access the same bank IF they’re both accessing the same memory line (which is 4B wide)
What if you break them?

## Slide 88
Break the rules → accesses are serialized
  Any bank can only access one address at a time. Period
  Break the rules and your code still works – but slowly
  And that’s not why you’re using a GPU, is it?
address
data
thread0
thread31
memory
bank0
bank1
bank31
…
WIRES,
WIRES,
WIRES
…
…
address
data
THE RULES
All 32 threads in a warp can access at once: if
  each one accesses a different bank, or
  two threads can access the same bank IF they’re both accessing the same memory line (which is 4B wide)

## Slide 89
Any hardware designer can make rules. But how can we write software that obeys them?
Why is it so hard?
  CUDA doesn’t let us pick which threads travel together in a warp.
  So we must ensure that all threads in the thread block obey the rules, no matter how they grouped into warps.
How can we ever do this?
  First we have to know which addresses are kept in which banks
  Our old habit, access arrays in row major to get good spatial locality, will not work well
THE RULES
All 32 threads in a warp can access at once: if
  each one accesses a different bank, or
  two threads can access the same bank IF they’re both accessing the same memory line (which is 4B wide)

## Slide 90: Interleaving of addresses in banks
Every successive line goes to the next bank in order
  Line size = 4B
So:
  Addr[3:0] → bank #0
  Addr[7:4] → bank #1
  Addr[127:124] → bank #31
  Addr[131:128] → bank #0

## Slide 91: Does our block algorithm work well?
Assume:
  We’ve drawn one block triplet
  It’s really 32x32
  Each thread works on one output element
If the two colored threads are in the same warp, will they break the rules when they access A?
  Yes, bigtime. They will collide on the A matrix every access
  In fact, every single access to A by two threads in different rows will collide
Can this be fixed?
  Yes, but it’s beyond what we have time for in this course
  You’ll see how much (or little) it matters in your HW
=
*
C
A
B

## Slide 92
Assume:
  We’ve drawn one block triplet
  It’s really 32x32
  Each thread works on one output element
If the two colored threads are in the same warp, will they break the rules when they access B?
  No problem at all!
  Each accesses a different column of B. Each column of B is a separate bank.
  So each thread confines itself to one bank of B
=
*
C
A
B

## Slide 93
The corner case: what about two threads in the same column of C?
If the two colored threads are in the same warp, will they break the rules when they access A?
  Still yes, for the same reasons as before
Will they break the rules when they access B?
  Still no problem!
  They both access the same column of B
  So they both access the same bank of B
  But threads in the same warp are in lockstep, so they always access the same address in the bank.
=
*
C
A
B
THE RULES
All 32 threads in a warp can access at once: if
  each one accesses a different bank, or
  two threads can access the same bank IF they’re both accessing the same memory line (which is 4B wide)

## Slide 94: Conclusion
For a GPU, accessing shared memory in column major works better than row major!
For best speed, we would try to access every array in column major
  We would need another trick to get us there
  Not covered in this course; your HW will tell you if this is a big deal or not

## Slide 95: False sharing
Review from multicore:
  Two (or more) cores
  Each core accesses only one address, so seemingly there is no conflict. However, the different addresses are part of the same cache line, so (as seen by the memory system) all cores are accessing the same line.
  Result: lots of conflicts, inefficient memory access
Interesting observation for GPUs:
  we encourage different threads in a warp to use addresses that result in false sharing!
  How could this be?

## Slide 96: False sharing
In a multicore system, when different cores shared, they have to communicate through the L3.
  This means leaving the core → inefficient.
  CPU keeps the different L1 caches coherent.
Our GPU case is different
  False sharing within a warp is extremely efficient; one cache line gets pulled in, and its pieces get immediately distributed to the different cores of the warp.
What if the false sharing were between threads in the same SM but in different warps?
  You lose the immediate-use advantage. But the threads all use the same L1 and shared memory, so communication is fast.
What if the sharing is between threads in different SMs?
  Now the issue is more like a multicore CPU.
  But GPUs don't bother with coherency, so they don't thrash as much as a CPU.

## Slide 97: Now we know the reason for everything 
HSX: 83 GFLOPS (2/cycle); FLOPS/mem= 3.3
Pascal: 5000 GFLOPS; FLOPS/mem=28
 | Haswell Server | Nvidia Pascal P100
# cores | 18 | 3840
Die area | 660 mm2 (22nm) | 610 mm2 (16nm)
Frequency | 2.3 GHz normal | 1.3 GHz
Max DRAM BW | 100 GB/s | 720 GB/s
LLC size | 2.5 MB/core (L3) | 4 MB L2/chip
LLC-1 size | 256K/core(L2) | 64 KB/SM (64 cores)
Registers/core | 180 per 2 threads | 500
Power | 165 watts | 300 watts
Company market cap | $160B | $90B

## Slide 98
Advanced topics: if/then, shared-memory banks