## Slide 1: EE 193: Parallel Computing
Fall 2017
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lecture 9: Google TPU

## Slide 2: Resources
In-datacenter performance analysis of a tensor-processing unit
  Norm Jouppi et. al, Google, ISCA 2017
https://eecs.berkeley.edu/research/colloquium/170315
  a talk by Dave Patterson
  he mostly just presented the above paper
Efficient Processing of Deep Neural Networks: A Tutorial and Survey
  Vivienne Sze et al., MIT, 2017
  Available at Cornell Libraries
Design and Analysis of a Hardware CNN Accelerator
  Kevin Kiningham et al, 2017 Stanford Tech Report
  Describes a systolic array
  Is it similar to the TPU? Don’t know…

## Slide 3: Summary of this course
Building a one-core computer that’s really fast is impossible
Instead, we build lots of cores, and hope to fill them with lots of threads
  We’ve succeeded
  But we had to do lots of work (especially for a GPU)
Is there a better way?
  Domain-specific architectures
  Build custom hardware to match your problem
  Only cost effective if your problem is really important

## Slide 4: The problem
Three problems that Google faces:
  Speech recognition and translation on phones
  Search ranking
  Google fixes your searches for you
Common solution: deep neural networks

## Slide 5: Neural net
Each node: a weighted sum y=w1in1+w2in2+…
Followed by an excitation function
  e.g., out = (y<0? 0 : 1)
Each vertical slice is a layer
Deep neural net has lots of layers

## Slide 6: Types of neural nets
Multi-layer perceptrons are fully connected (60%)
Convolutional neural net has connections to nearby inputs only (30%)
Recurrent NN has internal state, like an IIR filter (5%)

## Slide 7: What does this remind you of?
Matrix multiplication – yet again!
  y=w1in1+w2in2+… This is a vector dot product
  One layer: output vector = weight matrix * input vector
So, yes, Deep Neural Networks is mostly just lots of matrix multiplies (plus the excitation function)

## Slide 8: How do we make it run fast?
We’ve spent an entire course learning that.
  For Google, it wasn’t good enough
  One network can have 5-100M weights
  Lots and lots of customers
Goal: improve GPU performance by 10x
  Strategy: what parts of a CPU/GPU do we not need?
  Remove them, add more computes

## Slide 9: What did they add?
Matrix-multiply unit
  65K multiply-accumulate units!
  Pascal has 3800 cores.
Lots of on-chip memory to hold the weights, and temporary storage
  3x more on-chip memory than a GPU
  Still can’t hold them all, but a lot
What did they remove to make room for this stuff?

## Slide 10: What did they remove?
No OOO
No speculative execution or branch prediction
  Actually, no branches at all!
Far less registers
  Pascal has 64K registers/SM; TPU has very few
  How can they get away with that?
Like a GPU
Like a GPU
Just the arithmetic

## Slide 11: Very few registers
Outputs of one stage directly feed the next stage
GPU or CPU approach
  stuff outputs into registers
  read them again as next-stage inputs
  costs silicon area, and also power
  just get rid of them, direct feed
  part of what’s called a systolic array
  also remove intermediate registers for the sums

## Slide 12: What did they remove?
Far fewer threads
  Haswell = 2 threads/core
  Pascal  1000 threads/SM
  TPU = ??
No SMT
  But isn’t lots of threads and SMT what makes things go fast?
SMT: when one thread is stalled, swap in another
  Stalls are hard to predict (depend on memory patterns, branch patterns)
  Keep lots of threads waiting
TPU has only one application
TPU has no branches
1 thread!

## Slide 13: Downsides of SMT
Lots of threads required lots of registers
  TPU doesn’t need nearly as many registers
  Moving data back and forth between registers and ALUs costs power
SMT is a way to keep the machine busy during an unpredictable stalls
  It doesn’t change the fact that a thread stalled unpredictably
  It doesn’t make the stalled thread faster
  It improves average latency, not worst-case latency
Google’s requirement:
  Customers want 99% reliability on worst-case time
  They don’t want unpredictable waits more than 1% of the time
  SMT does not fit this customer requirement

## Slide 14: What did they remove?
No OOO
No branches (or branch prediction, speculative execution)
Far less registers
1 thread, no SMT
8-bit integer arithmetic
  training vs inference
  training is in floating point; done infrequently and can be slow
  inference can be done with 8-bit integers
  TPU uses 8-bit MACs. Saves substantial area – but TPU cannot do training

## Slide 15: Results
15-30X faster at inference than GPU or CPU
30X-80X better performance/watt
  “Performance” is 99th percentile

## Slide 16: Block diagram

## Slide 17: Chip floorplan