## Slide 1: EE 194 Advanced VLSI
Spring 2018
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lecture 2: Moore's Law, Scaling and power

## Slide 2: Technology scaling
  Everyone has heard of Moore’s Law. It’s probably been mentioned in most newspapers at some point. But what does it really mean?
  Every generation (1-2 years) all dimensions scale by 0.7
  72=0.5, so devices/unit area doubles
Consequences:
  1000x performance increase from 1990-2010
  Changed our lives
Why is Moore’s Law true?
  It's less of a natural law, and more of a prediction of human progress.
  Actually making this happen has had huge consequences
  The definition of a "generation" is getting longer!
Let's examine the consequences of scaling dimensions

## Slide 3: What do wires look like
Chips have multiple layers of metal
Typically, each successive layer runs perpendicular to the layers above, below
  That was beyond my artistic skills
W
L
H
Carea
Clat

## Slide 4: Wire capacitance
Does anyone remember the formula for capacitance?
  Carea  LW/Hinter-layer
  Ignores fringing cap, etc.
  Cnew= (Lnew)(Wnew)/(Hinter-layer,new)= (.7L)(.7W)/(.7Hinter-layer) = .7C
Intuitive explanation of what capacitance is?
W
L
H
Carea
Clat
a capacitor doesn’t like you to change the voltage across it. A big cap means that it takes a lot of charge flowing in to raise the voltage
Hinterlayer

## Slide 5: What was supposed to happen
The master plan
  Capacitances keep getting smaller.
  A scaled transistor still effectively drove as hard
  So delays keep getting faster.
The plan worked fine from about 1985-2005
  The golden age of computing: everything kept getter better and better all the time 
And then it didn’t
  wire R, physics and money got in the way
  we’ve still not quite figured out what to do about it

## Slide 6: Wire resistance
Does anyone remember the formula for resistance?
  R = L/(WH), where =1.7x10-8 Ωm for copper
  Ignores inductive effects (return resistance, skin effect), …
  Rnew = Lnew/(WnewHnew)= (.7L)/((.7W)(.7H)) = R/.7
  So if a wire just shrinks evenly, its resistance gets higher each generation! Very bad.
W
L
H
Carea
Clat

## Slide 7: Wire resistance
Physical analogy: a pipe of water. It’s hard to get water through a skinny pipe.
  even if it’s short
W
L
H
Carea
Clat

## Slide 8: RC scaling
Wire delay  RC (roughly)
(RC)new=RnewCnew = (?R)(?C)
  So wire RC delay is constant (assuming we’ve shrunk all dimensions equally)
  Rtotal=Rdevice+Rwire
  Wire delay didn’t shrink, and that eventually slowed delay scaling
How does the value of Vdd affect the RC delay?
  RC delay is independent of voltage: raising or lowering supply voltage makes no difference
V
t
=(R/.7)(.7C)=RC

## Slide 9: RC scaling
What about the time to cross a fixed distance (e.g., to cross the die with one long wire)
  R = L/(WH)
  Capacitance  LW/Hinter-layer
  Now L remains constant, rather than shrinking (W, H shrink)
Compute it yourselves:
  Rnew = Lnew/(WnewHnew)= (L)/((.7W)(.7H)) = R/.72
  Cnew= (Lnew)(Wnew)/(Hinter-layer,new)= (L)(.7W)/(.7Hinter-layer) = C
  (RC)new = RnewCnew = (R/.72)(C) = 2RC
The RC delay to cross a fixed distance doubles each generation. Sounds bad?
  In practice, nobody does this (see our HW1).

## Slide 10: Transistor scaling
This is not a course in device physics; we will (must) gloss over almost everything .
Suffice it to say that:
  Scaling transistors is very hard. The physics is becoming black magic (and very expensive). Intel Fab 42 (7nm) = $5B equipment cost.
  1.2nm gate-oxide thickness is only about 5 atoms thick, resulting in gate leakage.
  Device threshold voltages must get smaller to scale speed, but this results in more sub-threshold leakage (kT/q is constant).
Transistors somehow continue to shrink.
Device currents do continue to increase, which (along with less capacitance) keeps delays decreasing… but not much

## Slide 11: Power
Now for the fun part.
What are the units of power and energy (from 1st-semester physics)?
  Energy is an amount of work (Joules)
  Power is energy per unit time (a derivative, J/sec or Watts)
Why we care
  A battery holds a fixed amount of energy. After we expend that much energy, it’s dead.
  If a chip uses 5W of power, then how much heat does it generate?
    5W. A chip does no mechanical work, so all power is converted to heat.
    High power means your chip can double as a toaster .

## Slide 12: A Microprocessor as a HotPlate
= ?

## Slide 13: Circuit-level power, take 1
What is this circuit?
  Simple CMOS inverter
  You all remember this from EE103, right?
  When the input falls, the output ???
VIN
VOUT
C
rises

## Slide 14: Circuit-level power, take 1
When the output rises, energy is expended. Where does it go?
  Energy stored in the electric field of a capacitor = .5CV2
  Energy dissipated as heat via resistance = .5CV2 (extra-credit problem derives this)
If there were no resistance, how much heat would be created?
  None! Ideal capacitors do not generate heat
VIN
VOUT
C

## Slide 15: Dynamic power
A capacitor stores and releases electric charge. This creates an electric field, which stores energy. A capacitor does not create heat.
But the charge on a capacitor gets there through wires and transistors, which have resistance. Any time charge flows through resistance, that process creates heat.
  Intuitively, think of any mechanical object that moves against friction. It gets hot. The more friction and the faster the movement, the hotter it gets.
The power supply charges & discharges capacitance through transistors and wires, which burn power & emit heat.

## Slide 16: Dynamic power
Then energy stored in the capacitor is .5CV2. Miraculously, this is also the heat generated by the resistance.
  The actual resistance of the transistors and wires is irrelevant!
  Not always a general law, but works pretty well for our case.
  See the extra-credit problem for more detail.
If energy to switch one node is .5CV2, then power= =.5CV2f
Which energy are people talking about when they say .5CV2f?
  The energy dissipated as heat through the resistor
  The capacitive energy will get turned into heat when we discharge

## Slide 17: Worst-case power scaling
From about 1980-2005, performance kept increasing
  people kept V fairly high, since higher V → higher freq
  frequency scaled superlinearly
Assumptions for capacitance:
  If die area stayed the same… Ctotal gets linearly bigger each generation (Wtotal, Ltotal remain constant, H shrinks)
  In fact, die area keeps increasing (more xtor → more performance)
Plus, leakage kept getting worse
CV2f
fell slowly
much bigger
not looking good!

## Slide 18: The Power Problem
In about 2005, the industry started getting very serious about power. How did they do it? Necessity was the mother of invention.

## Slide 19: Why power stopped increasing
They avoided having chips double as nuclear reactors by no longer increasing frequency (and other tricks, too)
Because frequency stopped increasing!

## Slide 20: Power scaling since 2005
Frequency has not gotten much higher
  Future topic: DFVS, adapting freq to demand
Voltage scaled down as fast as it could
  But kT/q is a fundamental limit
Die areas have gotten larger over time, .5CV2f hasn’t. Reasons why (architectural or circuits)?
  As noted, f has stayed pretty constant
  Extra die area has been use for low-power caches, with little switching
  Or for integrating system logic, with low f.
  Dark silicon is the logical extension of this
  GPUs are an exception
  Coming soon: clock gating keeps Ceffective << Ctotal

## Slide 21: Cooling an iPod nano ...
iPod relies on passive transfer of heat from case to the air.
Why? Users don’t want
fans in their pocket ...
To stay “cool to the touch”
via passive cooling,
power budget of 5 W.
If iPod nano used 5W all the time, its battery would last 15 minutes

## Slide 22: Battery: Set by size and weight limits ...
Almost full 1 inch depth. Width and height set by available space, weight.
Battery rating: 55 W-hour.
At 2.3 GHz, Intel Core Duo CPU consumes 31 W running a heavy load - under 2 hours battery life! And, just for CPU!
At 1 GHz, CPU consumes
13 Watts. “Energy saver” option uses this mode ...
46x more energy than iPod nano battery. And iPod lets you listen to music for 14 hours!

## Slide 23: Servers: Total Cost of Ownership (TCO)
Machine rooms are expensive. Removing heat dictates how many servers to put in a machine room.
Electric bill adds up! Powering the servers + powering the air conditioners is a big part of TCO.
Reliability: running computers hot makes them fail more often.
Should we care about power for big servers?

## Slide 24: Facebook server farm: Sweden
a

## Slide 25: Advertising campaign for Utah

## Slide 26: Power is a problem
Scaling is making power a bigger and bigger problem
Let’s look at it in more detail – and look at how to minimize it.

## Slide 27: Static Power Dissipation
Short-Circuit Current:
  Direct Current Path between VDD and GND when both NMOS and PMOS transistors are conducting
  caused by finite-slope input signals and by subthreshold leakage
  anyone remember what that means?
Vin
ISC
C

## Slide 28: Static Power Dissipation
Assume Vdd=1V, Vt=.4V
  If .4V<Vin<.6V, then both N and P devices will be on
Lower Vdd to .7V
  What voltage range will incur ISC?
  Subthreshold leakage means that both devices conduct somewhat for (e.g., for the N) Vin<VTn.
  Lowering Vdd definitely reduces ISC.
ISC
C
Vin
Vin >.4 and <.3
So, does not occur. But…

## Slide 29: Effect of slew rate on ISC
Vin can be either the solid black (fast slew rate) or dotted black (slow) line; Vout is blue.
Which Vin will lose more energy from ISC?
  slower slew rate will spend more time in the ISC region
  same currents, but over more time → more energy
V
t
ISC
C
Vin

## Slide 30: Range of reasonable gate sizes
Bigger means faster. But there are diminishing returns. And bigger area means more capacitance and more power
Smaller means less power. But it also means slower. And slower means more ISC through the right-side inverter
Assume that the right-side inv has a fixed size
What are the pros and cons (speed and power) of having the left-side inv be much smaller, about the same, or much larger?

## Slide 31: How far can you lower Vdd?
Lowering Vdd will lower CV2 quadratically, and also lower ISC. How low can you go?
As Vdd approaches VT, gate delay gets much larger (not just linearly)
What if Vdd gets even lower than VT? Can any devices turn on?
  Nominally not, but subthreshold conduction still works
  Inverters can still function
  Very low power, but extremely slow
Can we lower VT?
  Not really; we become susceptible to exterior fixed-magnitude noise
  kT/q is constant, and we get hit by random thermal noise

## Slide 32: Static Power Dissipation
Gate leakage is a quantum tunneling phenomenon
  The gate oxide is an insulator; classical physics says no current can flow through it
  When gate-oxide thickness is small enough, quantum tunneling can occur
  electron’s momentum & position cannot both be known precisely; if you know it is not moving fast enough to surmount the energy barrier, then you don’t know which side of the oxide it’s on
C
Gate leakage
Vin

## Slide 33: In-class group exercise
Why would each of these tricks reduce static power?
Use fewer & smaller-width transistors
  Less transistors leaking; and I=V/R, so more R means less Isc each
Lower supply voltage
  reduces subthreshold leakage and thus ISC
Keep signal slew rates fast
  Less time when both transistors are on, so reduces Isc duration
Increase VT
  reduces subthreshold leakage (but hurts speed)
  Why might physical designers use high-VT devices, but then change to low-VT on critical paths?
  To expend leakage power only where it will do the most good
Switch to high-k dielectric
  reduces gate leakage (but increases gate capacitance)

## Slide 34: Reducing dynamic power
Next up: how can we reduce dynamic power?

## Slide 35: Activity factor
We said that:
  energy to switch one node is .5CV2
  power= =.5CV2f
In more detail:
  power= = (.5CV2)∙AF∙f
AF is the activity factor
  potentially different for every node
  says (on average) how many switches to expect per cycle
Ceff  AF ∙ C
  combines AF and C into one number: so power= .5CeffV2f
this assumed that switches/sec=f; i.e., every node switches once every cycle

## Slide 36: Activity-factor examples
Consider a counter that increments every cycle
What is the activity factor for…
  Its low-order bit (bit #0)?
  Bit #1?
  The clock?
  Vdd?
If bits #0 and #1 have C=20ff, Cclock=500ff and Vdd has C=10000ff, which has the most dynamic power?
1
.5
2
0
The clock overwhelms any other single node (and is often comparable to all other nodes combined)

## Slide 37: Lowering Dynamic Power
Reducing Vdd has a quadratic effect
  Also increases gate delay ~linearly (until Vdd→VT)
  If we lower voltage and freq, power reduces cubically.
Keep It Simple, Stupid
  architectural complexity → size → long wires, big capacitances → power.
Reduce switching activity
  Clock Gating idle units or stalled pipe stages
  Reduces AF and thus Ceffective.

## Slide 38: Clock gating
Perhaps the most common technique for reducing power.
It is powerful.
  Consider the cone of logic driving a node (i.e., the transitive fanin all the way back to registers).
  If all of the registers are clocked by the same clock, and it’s gated, then the entire cone is quiescent.
Turn off as many clocks as you can!
  Leave on the ones that are doing real work 
Examples to draw:
  E-stage adder and multiplier: clock them together?
  Two bits of the same datapath: clock them together?

## Slide 39: Limits to clock gating
Flops that are changing must clock 
Physical-design limits on granularity
  It’s physically painful to make many low-fanout clocks.
  So we usually have a reasonably small number of fairly high-fanout clocks
  We can only gate off the clock when everything it drives is guaranteed to be inactive.
Turning off an entire pipe stage, or an entire unit, is a Really Good Thing

## Slide 40: Di/dt noise
Circuits 101: V = L di/dt
  L = inductance (dominated by how big your package is)
  di/dt = how fast total supply current changes
  When current changes rapidly, you get voltage spikes
Any physical intuition for why that is?
  An inductor will not let the current through it change instantly.
  When you try to do so, it induces a voltage to create a counteracting current.
time
current
voltage

## Slide 41: Di/dt noise
Circuits 101: V = L di/dt
So if
  we are doing lots of computation, and
  we suddenly run out of data and stop, then…
  … our voltage rises (and, e.g., perhaps puncture gate oxide)
And if
  we are waiting for data and so not doing much, and
  the data arrives and we quickly do computation, then…
  … our voltage drops (and, e.g., latches lose state).
But didn’t we just say to turn off clocks aggressively?
  Yes, but not too aggressively 
  And don’t turn them all on at once!
  Big servers often have micro-architectural hooks to control this
Consequences:
  Limits how aggressively we can turn off circuits to conserve power
  It’s one limit on how low we can make Vdd (i.e., we have to be sure the supply voltage stays a lot bigger than the di/dt noise!).

## Slide 42: Summary of reducing power
We went over many ways to reduce power:
  Keep supply voltage as low as feasible (within performance limits)
  Keep Vt high (except for critical paths)
  Keep frequency as low as possible
  Keep gate delays “reasonable”
  Sleep units whenever possible
  Turn off clocks to reduce dynamic power (but watch out for di/dt)
  Remember: architectural complexity → size → long wires, big capacitances → power (Keep It Simple, Stupid)

## Slide 43: The future
Everyone has predicted the end of Moore’s Law for 15 years already.
  It hasn’t stopped yet, but it definitely has slowed down.
  Manufacturing costs have risen.
  Any “Law” predicting exponential growth clearly cannot keep going forever!
  And Moore’s Law violates Murphy’s Law .
Living with the end of Moore’s Law (power) will be a recurring theme for the rest of the course

## Slide 44: Coming up later…
EE194/Advanced Architecture focuses on architectural power savings.
Our next topic will be static-timing analysis and speed binning
  lots of connections with minimizing power and setting Vdd
Then comes clocking
  we’ll cover conditional clocks in a lot of detail
Another unit on DFVS
  all about saving power by lowering V and F
We may also discuss dark silicon
We may discuss timed digital logic
  Perhaps the most power-efficient form of digital logic

## Slide 45: In-class exercises
If we double the thickness of the oxide between metal layers, how does that affect R and C of wires? Can you think of any disadvantage to doing this?
A particular circuit has a total of 10 pF of capacitance, and runs at 2 GHz at .9V with an activity factor of .2. Compute Pdyn. If the static power is 1mW, compute the total power. If the computation requires 2000 cycles, how much heat will be generated?