## Slide 1: EE 194: Advanced VLSI
Spring 2018
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Static-timing analysis and speed binning

## Slide 2: Intro
What is static-timing analysis?
  A way to predict how fast our chip will run before we build it.
  Not bad, huh?
Why do we care?
  Well, we want our chips to run fast, don’t we?
How well does it work?
  Pretty well, most of the time
  So so, some of the time
  Spectacularly bad, every now and then

## Slide 3: Can’t we just run SPICE?
Yes, we could – if we didn’t mind waiting a few million years .
Why so long?
  The SPICE model is very accurate – and so it’s slow.
  But there are reasonably-fast, reasonably-accurate versions of SPICE; that’s not really the problem
SPICE (or any other simulation) only tests the things that we give it patterns for.

## Slide 4: Can’t we just run SPICE?
Three inputs. Each can rise, fall, stay zero or stay one.
How many input patterns for this little network?
  43 = 64
  It gets real big, real fast, for networks with lots of inputs 
A
B
AA
BB
C
D
Q
7
3
2
5
1
1
0

## Slide 5: Can’t we just run SPICE?
It gets worse…
Can’t we just run SPICE on the “important” patterns?
  Who decides what is important?
  Are you good at thinking, in advance, of every possible issue in a complex design?
We want a tool that tests even the critical paths we haven't thought of!

## Slide 6: Static vs. dynamic
Static usually means “pattern-independent,” vs. dynamic meaning “only for certain input patterns.”
  SPICE is a dynamic simulator; it only simulates the patterns that you give it.
  Note: it’s perfectly fine for modeling our library cells; they just have a few inputs.
Can you think of another dynamic simulator commonly used?
  Most Verilog, VHDL simulators
In principle, STA literally checks every path
  (We'll see later that this is only “almost” true )
  No issues of writing a pattern for a particular path.
  Sounds great – but just how can you check every path?

## Slide 7: Paths in a toy circuit
What are the paths (from an input to the output)?
What are the delays of the 3 paths?
  red=14, blue=10, green=5.
Note the concept: we only trace paths; the logic is irrelevant
But will a “real” circuit have too many paths?
A
B
AA
BB
C
D
Q
7
3
2
5

## Slide 8: Reconvergence
2 paths from A→B
How many total paths from A to D?
8 paths total, and it's exponential in the depth of the logic.
  A→B→C→D, A→AA→B→C→D, …
So how can STA check an exponential number of paths?
1
1
2
1
4
1
A
B
C
D
AA
BB
CC
, 2 from B→C
, 2 from C→D

## Slide 9: PERT charts
Developed by the US Navy in 1950s to manage the Polaris missile project
  Concerned about the Soviet nuclear arsenal
  Developed a ballistic missile launched from a submarine
  Wanted to catch up quickly, hired 3000 contractors, but the resulting schedule mess was too complex
  They needed an automated method to compute the critical path to developing Polaris.

## Slide 10: PERT chart for getting to school
What time do you get to school?
What is the critical path?
walk to school
(5)
lock house
(2)
breakfast
(7)
dress
(3)
wake up
at t=0
7
3
9
14

## Slide 11: Pert chart for getting to school
What works for school, also works for gates.
What is the timing & critical path?
We have completely ignored the logic function (AND vs. OR, etc) of the network!
  So the tools to automate a submarine schedule may work for us
  And in fact STA does work most of the time 
walk to school
(5)
lock house
(2)
breakfast
(7)
dress
(3)
7
3
9
14
7
wake up
at t=0
3
2
5
B
C
A
0
0
0
Notes: The items in our PERT chart don’t have a logic function; the algorithms for PERT cannot handle one

## Slide 12: Pert chart for getting to school
Key observations:
  Again: we have completely ignored the logic function (AND vs. OR, etc) of the network!
  No need to trace paths from subcritical inputs (this is how we can quickly trace an exponential number of paths)
7
3
9
14
7
3
2
5
B
C
A
0
0
0

## Slide 13: Reconvergence
Figure out the most critical path from A to B.
  Then totally ignore the A→B path!
Figure out the most critical way to extend it from B→C
  Then totally ignore any other way to get from B→C
Ditto from C→D
No longer tracing an exponential number of paths
  Assumes the subcritical paths cannot become important
  If logic mattered, our assumption would be untrue
1
1
2
1
4
1
A
B
C
D
AA
BB
CC

## Slide 14: Sequentials
Two main types of sequential elements: edge-triggered (usually called flops) and level-sensitive (usually called latches).
My drawing convention:
D Q
CLK
CLK
flop has a little triangular notch
latch has a square notch
D Q

## Slide 15: Flops
Q can only change on the rising edge of CLK.
The time from when CLK rises to when Q changes is called tclk→Q.
D is not allowed to change in the red window of tsetup before the rising edge of CLK. Anyone remember why?
  There’s usually an internal state node that could be metastable otherwise
CLK
D
Q
D Q
tclk→Q
CLK
tsetup

## Slide 16: Flops and timing
Flops are marvelous. No matter what time D changes, it doesn’t affect the timing of Q.
  Q always changes tclk→Q after the rising edge of CLK.
Let's define t=0 as the rising edge of CLK. Then what is the latest arrival time for Q?
If we assign the constant value tclk→Q to all flop outputs, then they essentially turn into primary inputs!
  Thus, STA with loops of flops is very simple.
CLK
D
Q
tclk→Q
tclk→Q

## Slide 17: Flop example (group exercise)
What is the latest arrival time on the node OUT? (Assume CLK rises at t=0, and tclk→Q=1).
How about all of the other nodes?
What is the fastest cycle time that the circuit can operate at? (Assume tsetup=2).
AA
BB
C
E
7
3
2
5
D Q
CLK
OUT
1
4
8
10
15
17

## Slide 18: What if the clock is nontrivial?
A clock will usually drive long distances and many loads, and will need buffering.
Assume CLK rises at t=0, and all gate delays are 1. If tclk→Q=1, then what is the arrival time at Q1?
So we don’t always know our flop-output arrival time up front. How can we deal this this?
  Just do all of the clocks first.
D Q
CLK
0
1
2
Q1
A
B
C
3

## Slide 19: In-class exercise
What is the arrival time on all nodes?
What is the minimum clock cycle time where the circuit functions correctly?
Draw the timing diagram on the board, showing both clock R.E.
D Q
CLK
0
1
Q0
A
B
3
D Q
1
C2
Q1
C3
2
3
4
4
3 (not 5!)
Assume tclk→Q=tsetup=1
1
1
1

## Slide 20: Latches
Q can change any time that CLK is high.
The time from when D rises to when Q changes is called tD→Q, and from CLK rising to Q changing is tclk→Q.
D is not allowed to change in the red window of tsetup before the falling edge of CLK.
CLK
D
Q
tD→Q
CLK
tclk→Q
D Q

## Slide 21: Loops of latches
All of a sudden, there are two loops. What are they?
How can STA figure out the arrival times?
  It’s like a dog chasing its tail…
  First look at the loops.
  The looping part of any path must be ≤ one full cycle.
D Q
D Q
CLK
C2
C3

## Slide 22: Latches: the summary
Latches make STA algorithms more difficult
  Loop detection and checking is needed
  Paths flow through latches, and the flow-through path may be critical
  Algorithms are more complex, but still work fine
So why do people use latches?
  They are more resistant to clock skew
  But their disadvantages usually outweigh this
  The homework will explore the issue further.

## Slide 23: Now the fun begins...
So far, as long as we use flops and not latches, static-timing analysis seems easy 
  We’ve pulled off the amazing trick of analyzing every path, in just a small amount of time
  Because of that, we can even check paths we never thought of.
Now it’s time to take this easy problem and make it hard .
  OK, really it was hard all along
Gate delay, and false paths, and common clocks, oh my
  Pretty soon you’re going to understand why commercial STA tools don’t always work perfectly!

## Slide 24: What does delay mean?
We’ve talked a lot about “delay,” but we’ve not actually defined it.
Red=inverter input voltage
Blue = inverter output voltage
Length of black arrow = gate delay
Interesting question:
I drew the black arrow at the point where each waveform crossed Vdd/2. Any thoughts on if this is a good or bad choice?
  It’s probably not the best of choices; it can lead to negative delay!
  Make sure we know about Vsw
How would you define the inverter’s delay?
time
V
Vdd/2

## Slide 25: What things affect delay?
Now we know what delay is... what affects it?
Simplest model: the inverter is a resistor, its load (e.g., wiring + downstream gates) is a capacitor.
  Delay = R*C.
OUT
load
C
Vdd
IN
inv
What things affect the values for R and C?
  Bigger driver devices→smaller R; bigger load devices or more wire →bigger C.
  And much more...
Increase R or C, and the output slope gets slower, and the ∆t increases.
R

## Slide 26: Input slope
In reality, the gate delay depends heavily on the slope of the input voltage. Why?
  Slower input slope means that the output transistors spend less time being fully turned on.
  We drew our resistor as a fixed resistor depending only on the device size; in reality the resistor size also depends on the input slope.
Red=input voltage
Blue = output voltage
Length of black arrow = gate delay
time
V

## Slide 27: Other things that affect resistance
Multiple inputs switching at once
  When more than one input switches at roughly the same time, it usually affects the gate delay
  Draw this on the board for a NAND3.
What makes it hard to analyze
  It’s often logically impossible for multiple inputs to switch at exactly the same time (but we’re not looking at logic)
  The delay effect is heavily dependent on the exact amount of overlap, so a little bit of analysis error at the inputs means more error at the outputs
Notes: And let *them* draw the NAND3!

## Slide 28: Capacitive coupling
We talked about what affects the R. Now let’s talk about the C.
V
A
inv1
invA
C1
C2
We talked about modeling inv2 and wiring cap as a grounded capacitor (C1).
Bigger C1 → slower slew rate on node V, slower delay for inv1, as mentioned.
A floating capacitor (C2) is harder. The aggressor (A) can inject charge into the victim (V); the resulting effect on delay varies with the slew rates of V and A, as well as the timing of when they both switch.
inv2
Key idea: model this complex circuit as just an R & C again, so we can easily analyze it.

## Slide 29: Capacitive coupling: case #1
The first case is when the aggressor A is quiet.
V
inv1
A
invA
C1
C2
If A does not switch, then A is essentially a ground.
The same situation occurs if A does switch, but not at the same time as when V is switching.

## Slide 30: Capacitive coupling: case #2
A switches in the same direction as V.
V
inv1
A
invA
C1
C2
If aggressor A switches at the same time and at the same direction as V, then A and V are always at the same voltage. Then there is no voltage across C2, and no dV/dt, and no charge transfer. It becomes effectively zero.

## Slide 31: Capacitive coupling: case #3
A switches in the opposite direction as V.
V
inv1
inv2
A
inv3
C1
C2
If aggressor A switches at the same time and in the opposite direction as V, then the aggressor tries to prevent V from switching. C2 effectively becomes larger (1.5x to 4x, depending on the situation)!
kC2

## Slide 32: The problem with coupling
Coupling capacitors arise anytime two wires are near each other.
  Adjacent metal layers run at 90° to each other, so a long wire has many wires crossing it above and below.
  There may be thousands of small floating caps attached to a long wire.
If we only knew
  which direction all of those aggressor nodes were switching, and
  when in the cycle they switched
then we could convert them into grounded fixed capacitors and compute the delay for each node, so we could then run timing analysis. But…

## Slide 33: The problem with coupling
If we only knew
  which direction all of those aggressor nodes were switching, and
  when in the cycle they switched
But that’s what STA is supposed to tell us, and we can’t run STA because we don’t know gate delays yet!
But there are probably many architectural reasons that not all of them can switch the same direction in the same time. Ummm… remember we agreed not to let logic functionality enter into STA!

## Slide 34: Coupling cap, in practice
What do people do in practice?
  Some caps should be counted at 0x, some at 1x, some at ≈2x.
  Compromise: count them all at 1.5x.
  Or whatever other magic number you chose. And change it if your project is behind schedule .
Draw a long-wire example on the board
  Do full shielding and offset inverters

## Slide 35: Summary so far
How well does STA work?
  Reasonably well, most of the time
  So so, some of the time
  Spectacularly bad, every now and then
The problems:
  Capacitive loading greatly affects delay
  The correct capacitance is essentially impossible to model
  Multiple-inputs-switching delay variation is also difficult to model correctly
False paths, coming up!

## Slide 36: What about voltage?
How does voltage affect delay?
  Increase Vdd → reduce delay
Why? In our model, does it affect R, C or both?
  Mini-homework: think about it, discuss it with your friends, & we’ll discuss it next time

## Slide 37: False paths
False paths are the bane of STA.
We’ve made wonderful simplifying assumptions:
  the problem of timing is completely independent from the logic functionality.
  Subcritical inputs cannot be part of long paths
These are correct 99% of the time – but 99% is not nearly good enough!
False paths break them . Let’s see why.

## Slide 38: False path with two muxes
The path from B to I is only valid if S=1
The path from I to Q is only valid if S=0
Therefore the path B→I→Q is a false path.
Why would anyone design such a silly circuit?
0
1
0
1
A
B
C
S
Q
I
Perhaps it make sense in a larger context. E.g.,
  the first mux is in another faraway block
  We already use I somewhere in this block.
  We want Q=mux(S?C:A); we do Q=mux(S?C:I) instead, so as to save a wire.
  Similar cases occur in a carry-skip adder (see the HW)

## Slide 39: Another mini-homework
Can you think of other false-path examples?
  They’re sprinkled throughout computer architecture
  The BGFs that we’ll discuss in the clocking section have them
  You can look ahead at the HW for the adder example
Notes: Any time there are multiple sources driving a bus (with some slower than others), and multiple destinations receiving the bus (again, with some slower than others), and the combination of slow driver -> slow receiver tells the architecture to stall for a cycle. Or, lots of critical paths occur during reset – at which time you can usually guarantee that nobody cares.

## Slide 40: False path with two muxes
Consider the input arrival times shown above. How should we propagate them? (Assume both muxes have a delay of 1).
The green path is false
We could ignore the fact that B→I→Q is false, and claim that the arrival time on Q is 7. However, it really isn’t, and this may cause us to mistakenly think the chip doesn’t work at speed.
0
1
0
1
A
B
C
S
Q
I
1
3
5
2
6
3 or 7?
The critical path through this logic is A→I→Q
Ugly – we’ve now intermixed logic & timing. Yes, it’s ugly, but there’s no choice .
Input A is subcritical to the mux – but it’s the one that matters 
5

## Slide 41: How do we know a path is false?
Lots of papers in the mid '90s trying to determine this automatically. None was really practical.
Where we are today
  a path is false if somebody says it is.
Result: STA is an iterative process
  Run the STA tool
  It shows you lots of really long paths that are actually false
  Tell the tool they are false
  Go to #1
Question: how much do you trust your architects?

## Slide 42: Common clocks
If the clock period is 1000 ps, and the flops have tclk→Q=tsetup=0, then how much delay can the logic have?
But now let’s look at how the clock is actually created.
CLK
D Q
D Q
logic
PLL
Also 1000ps

## Slide 43: Real-life problems
The PLL has jitter.
The inverters have unpredictable delay. Why?
  Delay depends on process, voltage, temperature, coupling capacitors, …
How long do you think the inverter chain might be for a CPU?
  Several cycles long!
CLK
D Q
D Q
logic
PLL

## Slide 44: Real-life problems
Why would we care? No matter how unpredictable or changeable the delay from CLKPLL to CLK, the same CLK feeds both flops. Why would any skew or jitter matter?
  Clock skew (which is the same every cycle) will not matter here. Clock jitter (which can change every cycle) does. Why?
  Because the 2nd flop receives a signal a full cycle after the 1st flop sends it – i.e., the path starts and ends on different clock edges.
CLK
D Q
D Q
logic
PLL
CLKPLL

## Slide 45: The problem with jitter
Timing constraint: Δt1+tlogic≤tclk_per+Δt2
  or tlogic≤tclk_per+(Δt2-Δt1)
  And so if Δt2<Δt1, we cannot have as much logic.
Why would we have Δt2<Δt1?
  Again, changes in voltage, coupling caps.
CLK
CLKPLL
Flop #1 output
Flop #2 input
Δt1
Δt2
tclk_per
tlogic

## Slide 46: It can get much worse
Now the “common clock” is just the first 5 inverters.
The final inverter is different for the two flops. How does this make life worse?
  Unpredictable device size & clock skew can also break our path just like jitter did before
Look at the common-clock app (on the class website)
CLK
D Q
D Q
logic
PLL

## Slide 47: Another in-class exercise
What is the minimum clock cycle time where the circuit functions correctly?
Hint: putting latest arrival times on every gate may not be useful. You may have to look at min/max times on some gates, and may even have to analyze each path separately.
D Q
CLK
Q0
A
B
D Q
1
C2
Q1
C3
Assume tclk→Q=tsetup=1
Assume the clock buffers each have
  nominal delay of 1ns
  ±.1ns jitter, ±.2ns skew.
1
C4A
C4B

## Slide 48: Another in-class exercise
Consider the path in blue. Draw the timing diagram.
The common clock point is C4A. Do we care about skew? Jitter?
Draw the appropriate min/max delay numbers.
What is the minimum cycle time?
D Q
CLK
Q0
A
B
D Q
1
C2
Q1
C3
Assume tclk→Q=tsetup=1
Assume the clock buffers each have
  nominal delay of 1ns
  ±.1ns jitter, ±.2ns skew.
1
C4A
C4B
.9-1.1
1.8-2.2
2.7-3.3
5.3
Jitter but not skew
4.3
5.3+tsetup≤tc+2.7, or tc≥3.6

## Slide 49: Another in-class exercise
Consider the path in green. Draw the timing diagram.
The common clock point is C3. Do we care about skew? Jitter?
Draw the appropriate min/max delay numbers.
What is the minimum cycle time?
D Q
CLK
Q0
A
B
D Q
1
C2
Q1
C3
Assume tclk→Q=tsetup=1
Assume the clock buffers each have
  nominal delay of 1ns
  ±.1ns jitter, ±.2ns skew.
1
C4A
C4B
.9-1.1
1.8-2.2
3.5
5.5
Jitter but not skew through C3, and both for C4A,C4B
4.5
5.5 + tsetup≤tc+2.5, or tc≥4.0
2.5

## Slide 50: Another in-class exercise
What would happen if we had 100 clock buffers instead of just four?
  The delta between min vs. max would get much bigger, and the minimum clock period would get bigger.
D Q
CLK
Q0
A
B
D Q
1
C2
Q1
C3
1
C4A
C4B
Lesson to be learned?
Keep jitter low, by
keeping di/dt low
keeping clock delays fast
shielding your clocks

## Slide 51: Binning
We’ve pretended that each gate has a single delay that is just a simple number
  except for coupling on delay
Another big issue: manufacturing variation
Every chip is a little bit different. Why?
  Manufacturing process is very delicate & hard to control precisely.
  Chemical deposition, polishing, ion implantation, …
Final chips will actually have a bell-shaped curve of frequency
1GHz 1.5GHz 2GHz
fraction of chips at this freq

## Slide 52: Binning
Bell curve again. Each point is one process corner; show the 3 corners for each of N, P
The nine classic corners:
  P devices can be Slow, Typical or Fast
  N devices can be Slow, Typical or Fast
  Typically, “slow” and “fast” are 3-sigma values
  Result: 9 process corners
  “FT” means “fast N devices, typical P devices.”
How would the delay for a TT inverter compare to an FF inverter?
  it would be slower

## Slide 53: Binning
The are 9 common corners. How many different numbers could we pick for gate delays?
  Perhaps 9. But really, the N and P devices can come from any points on the curve.
  So how do we get the numbers for gate delay? What SPICE model should we use?
Option #1: pick the SS corner
  All of the gate delays become quite slow
  If STA works with these numbers, then every chip you manufacture should work. (Is this true?)
  Not quite; SS is just 3σ
  And the worst case for clocks is often the fast delay!

## Slide 54: Binning
Next idea:
  Run STA at TT
  Some chips will run as predicted; some faster, some slower
Try to sell all of the chips
  Charge more for the fast ones? Any other strategies that might make more money? What might customers value more than speed?
  The fastest may also be the most power hungry. Charge more for the best speed per watt.
  Exact details depend on what your customers value.

## Slide 55: Problems with binning
Binning is expensive in a manufacturing line
  Need to mechanically separate chips into different bins using fancy robots
  Need to keep inventory of many different types
  Any examples of consumer chips that are not binned?
  Sure – most everything except for CPUs
What if you’re designing an unbinned chip?
  you have a tradeoff.
  Run STA at TT?
  Run STA at SS?
  No real way to fix this for now (advanced binning algorithms will help)
half your chips will fail.
you overdesign and lose power

## Slide 56: The economics of servers
Most CPUs: you can just design at TT and let the chips fall into whatever speed bin they will.
Servers are different:
  A big server has lots of memory, disks, cooling
  Cost of the CPU is “relatively” small
  People will pay $$ for the fastest CPU; nobody wants a slow one.
Now we’re back to square 1
  binning doesn’t help much when your customer only wants one bin!

## Slide 57: Binning
Which bin will we put the 1.3 GHz chip in?
Will the 1.8GHz chip go into the 1.6GHz bin or 2GHz?
  1.6. Because we want it to actually work, after all!
  Any benefit to the customer of getting a chip that can run faster than specced?
  Maybe they can over-clock it (but most customers don’t care)
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Assume that our product speed bins are 1.3GHz, 1.6GHz and 2 GHz.
1.3 GHz 

## Slide 58: Binning
Observation: this curve was made at one specific Vdd (say 1V)
  If we lower Vdd, the chips will all run slower
  What if we take our 1.8GHz@1V part, and lower Vdd just enough to make it run at 1.6 GHz max?
  Any benefits?
  Lower power! Any reason a customer will care?
  Do you care if your cell phone lasts longer before recharging . We might advertise 6 hour battery life, but in practice most phones will do better than that.
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Assume that our product speed bins are 1.3GHz, 1.6GHz and 2 GHz.
1.6GHz

## Slide 59: Binning
Observation: we can play that game in both directions.
  Any benefits to raising Vdd?
  Make our “1.8GHz” chip run at 2GHz; or even make our 1.3GHz chip run at 2GHz.
But wait: can we just raise Vdd on every chip high enough to put it into the fastest bin, and sell it for the most money?
  Sometimes, yes. But there are limits.
  Raise Vdd too high and the gate oxide will puncture, or the chip will melt.
  But in fact, we’ve oversimplified what the bins really are
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Assume that our product speed bins are 1.3GHz, 1.6GHz and 2 GHz.
2GHz

## Slide 60: Binning
In today’s world, each bin has a spec for both minimum freq and also max power.
  Because most customers care about both!
  We’ll have various bins, each with a freq & power number. And of course, faster and cooler each sell for more money.
  Bin points are picked to make the most money and not throw away too many chips
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Assume that our product speed bins are 1.3GHz, 1.6GHz and 2 GHz.
Freq | Power | Price
1.3GHz | 4W | $200
1.3GHz | 2W | $300
1.6GHz | 4W | $250
1.6GHz | 2W | $350
2GHz | 5W | $300
2GHz | 2W | $500

## Slide 61
So any ideas how to put each chip into the most profitable bin?
Specifically: for a given chip, you do “Set voltage to V; run tests and see if they pass; measure power.”
  But do this operation as few times as possible; test time is expensive
  Assume you can set V to a granularity of .01 volts.
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Freq | Power | Price
1.3GHz | 4W | $200
1.3GHz | 2W | $300
1.6GHz | 4W | $250
1.6GHz | 2W | $350
2GHz | 5W | $300
2GHz | 2W | $500
for each freq in {1.3GHz, 1.6GHz 2GHz}
  for every Vdd from, say, .1V to 2V
    run test and see if it passes and what the power is;
    if it passes and the freq,power are OK for some bin
      note that fact;
of all the bins we’ve marked, pick the one that gives the most money;

## Slide 62
Ideas how to run fewer tests?
  Test for the most profitable bin first, and quit once you have any pass
  Use a binary search instead of trying every V
  Remember all of the failing V/F points and never re-test if you know it will fail
  Remember passing V/F points and curve-fit to predict passing Vdd at other freq (only useful if a test passes, but the chip exceeds the power limit for that bin)
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Freq | Power | Price
1.3GHz | 4W | $200
1.3GHz | 2W | $300
1.6GHz | 4W | $250
1.6GHz | 2W | $350
2GHz | 5W | $300
2GHz | 2W | $500
for each freq in {1.3GHz, 1.6GHz 2GHz}
  for every Vdd from, say, .1V to 2V
    run test and see if it passes and what the power is;
    if it passes and the freq,power are OK for some bin
      note that fact;
of all the bins we’ve marked, pick the one that gives the most money;

## Slide 63
So any ideas how to put each chip into the most profitable bin?
Specifically: for a given chip, you do “Set voltage to V; run tests and see if they pass; measure power.”
  But do this operation as few times as possible; test time is expensive
  Assume you can set V to a granularity of .01 volts.
  Can you use every bit of new knowledge to inform future actions?
Take some time and brainstorm. Ideas?
  Test for the most profitable bin first, and quit once you have any pass
  Remember all of the failing V/F points and never re-test if you know it will fail
  Remember passing V/F points and curve-fit to predict passing Vdd at other freq (only useful if a test passes, but the chip exceeds the power limit for that bin)
1GHz 1.5GHz 2GHz
1.8GHz
1.3GHz
Freq | Power | Price
1.3GHz | 4W | $200
1.3GHz | 2W | $300
1.6GHz | 4W | $250
1.6GHz | 2W | $350
2GHz | 5W | $300
2GHz | 2W | $500

## Slide 64: Hierarchical STA
STA tools run relatively fast. But…
  chips are big! Full-chip flat STA is not very practical
Solution: hierarchical STA.
  Pretty much standard in most designs today
  All major tools support it

## Slide 65
Problems:
  while each of the blocks may be reasonably small, there may be lots of them, and the full chip is big
  block 1 may be finished a month earlier than the rest; it should get feedback before the full chip is built
Solution to both problems: hierarchical STA
Block 1
Block 3
Block 2
Block 4

## Slide 66
Problem: if we only have block 1, how can you check either of these paths?
  Start with timing estimates at all interface pins
  The estimates serve as a specification for the not-yet-designed logic
  Driving logic must meet those numbers; receiving team uses them
Where might the numbers come from?
  Best estimates from the design team
  Give and take as each team wants their life to be easy
Block 1
D Q
D Q
Q D
Q D
Block 2
t=5.2
t=4.7
Notes: The driving box will push for late numbers; receiving will want early numbers

## Slide 67: Limits of top-down STA
Any reason this isn’t a perfect solution? I.e., any need for anything more than 4 single-block STA runs?
  Maintaining the database of interface timings is no fun
  Cross-block paths are hard to model fully (we’ll see that shortly)
Block 1
Block 3
Block 2
Block 4

## Slide 68: Bottom-up STA
That was top-down
Little by little, all of the blocks get finished
Next comes bottom-up STA

## Slide 69: Bottom-up STA
Assume all four blocks are done
Each block may have lots of gates
What is bottom-up STA?
  Replace the block by a (simple) model
  Do one top-level STA run that doesn’t look at all of the gates, but just uses models of each block
  Runs fast
Sounds great – but what is the “model?”
Block 1
Block 3
Block 2
Block 4

## Slide 70: Black-box model
Output nodes: replace each pin by its arrival time
  Assume tc=10 and tck→Q= tsetup=tinv=1
Input nodes: replace each pin by its required time
Internal logic vanishes
Block 1
D Q
D Q
Q D
Q D
Block 2
tarr=2
D Q
Q D
tarr=2
treq=8
treq=8

## Slide 71: Problems with black-box model
Any objections? Anything it cannot handle?
  It’s not obvious what this buys us above running each block separately
  Consider the following circuit…
Block 1
Block 2
tarr=2
tarr=2
treq=8
treq=8

## Slide 72
What made this circuit hard to analyze?
  The two flops have parts of the clock tree in common, parts separate
  Assume PLL output is at t=0, 1 delay per inv, tc=10
Any problems so far?
  All of our common-clock information has been lost 
  We cannot compute timing of the flop-to-flop path!
CLK
D Q
D Q
logic
PLL
Block 1
Block 2
tarr=6
tarr=6

## Slide 73: Grey-box model
STA tools typically build a grey-box model
  Black-box model shows no internal detail (inaccurate)
  White-box model shows all internal detail (i.e., flat and slow)
  Grey-box model shows “just enough” internal detail
With all of this, hierarchical STA is still painful

## Slide 74: False paths, revisited
Remember this? B →I →Q is a false path
What if the separation into blocks splits it?
  The correct timing for interface node I is 6
  At the top level, nodes B and Q do not even exist, so STA cannot enforce a false path
0
1
0
1
A
B
C
S
Q
I
1
3
5
2
6
5
Block 1
Block 2

## Slide 75: Backup

## Slide 76: Valentine’s Day joke
What did the level-sensitive latch say when its clock input was "1"?
  You turn me on