## Slide 1: EE 194: Advanced VLSI
Spring 2018
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Clocking

## Slide 2: Clocking
What we’ll learn:
  Conditional clocking: implementation and timing
  Clock-distribution networks: how to send one signal to a million destinations
  Clock-domain crossing: how different clocks talk to each other

## Slide 3: Conditional clocking
What is a conditional clock?
  A clock that doesn’t always fire.
Why do we care?
  Most obvious and common reason: power
  But it can also be important for functionality
CClk
Clk

## Slide 4: Conditional clocking and power
We’ve drawn a 64-bit datapath. Assume that:
  Both pipe stages have unconditionally-clocked “valid bits” saying if they hold valid data
  Pipe stage #1 (i.e., D1[63:0]) does not have valid data this cycle
  Neither does pipe stage #0.
Is there any reason for CLK1 to fire?
Does it do any harm if CLK1 fires?
In what ways would it save power if we don’t fire CLK1?
  Saves clock power.
  Ensures that the datapath bits don’t randomly toggle also.
D Q
D Q
D0[63:0]
.
.
.
D1[63:0]
LOGIC
D Q
D Q
.
.
.
CLK0
CLK1
No
No (presumably valid1 will remain 0)

## Slide 5: Cond. clocking and functionality
Consider the same pipe, and assume:
  D1 holds valid data
  D1 is stalled (e.g., because of a cache miss), and so the instruction in D1 must stay there for another cycle
Should we fire CLK1?
  No. If we do then we will lose this instruction.
  This is not optional. Yes, it does happen to save power; but the main reason is functionality.
D Q
D Q
D0[63:0]
.
.
.
D1[63:0]
LOGIC
D Q
D Q
.
.
.
CLK0
CLK1

## Slide 6: High-level timing of cond clocks
Assume that each rising clock edge clocks in a new machine state. Which clock edge should machine state in State 2 affect?
  The current state cannot affect the clocks that generated it – those already happened. It actually affects next state.
Clk
State 1 | State 2 | State 3 | State 4

## Slide 7: Building a conditional clock
Assume EN is based on the current state (and should affect the next state)
Does this circuit work?
D Q
EN
CLK
CCLK
When EN is always high, CCLK always fires. Good?
CLK
EN
CCLK
Sure

## Slide 8: Building a conditional clock
What if EN rises or falls? Do you like this timing?
  EN in any state is affecting the clock before the next state happens
  We get runt clock pulses when EN changes, which breaks timing
D Q
EN
CCLK
CLK
EN
CCLK
CLK

## Slide 9
Better?
  Yes. Now EN correctly affects the next cycle’s clock, and there are no more runt clocks. This is how it’s usually done.
Next up: timing constraints to generate the cond. clock
D Q
EN
CCLK
CLK
EN
CCLK
D Q
CLK
EN_D
EN_D

## Slide 10
What are the constraints?
  Blue arrows are normal delay; red ones are constraints
  Note the setup time on the flow-through latch is to the closing edge
  It’s harder than it looks! (the logic, flow-through, and early target)
EN1
CLK
EN1
CCLK
EN_D
EN2
EN2
D Q
CCLK
D Q
CLK
EN_D
logic

## Slide 11: Geographical problems
So, conditional clocks are hard because:
  difficult critical path to an early clock
  sometimes, architectural/geographical issues
Assume there is an issue, and pipe stage D2 stalls. Time for traffic to back up…
  D1 cannot move forwards, because there’s no place for the data to go. So it stalls.
  Then the same thing happens to D0. And so on…
Pipe stalls can back up over many stages.
  A stall condition in D2 must control CLK0
  But the pipe stages may be very far away 
D Q
D Q
D0[63:0]
.
.
.
LOGIC
D Q
D Q
.
.
.
CLK0
CLK1
D Q
D Q
.
.
.
CLK2
LOGIC
D2[63:0]
D1[63:0]

## Slide 12: In-class exercise
Draw a three-stage pipeline.
Each stage has:
  valid bit, straight from a flop
  stall bit, flop plus some logic
  unconditionally-clocked ctl
Draw the gates/equations for:
  valid bit (in terms of current valids, stalls)
  datapath clock enables
Do you see any bad critical paths (especially if our pipe were 10 stages long)?
  What might we do about this?

## Slide 13: Avoiding downstream stalls
Where do stalls come from?
  The usual data hazards, control hazards, cache misses…
Which of these could be a late-stage stall?
  Hazards are known at issue time
  Cache misses are only known by the cache tags, which are located in the caches, which can be far away
How do we avoid stall signals traveling long distances for cache-miss stalls?
  Use a micro-architecture where cache misses are not blocking
  Tomosulo does not force stalls behind a cache miss (except for true data dependencies)

## Slide 14: More geographical problems
What if…
  an instruction is launched speculatively
  it starts to execute and gets about halfway done
  we find out there was a mispredict, and can squash it
  but it’s already quite far away from the branch resolution logic
How can we turn off its clocks so far away?
  It’s OK to wait a cycle, if needed, to squash the clocks
  The squash signal can usually catch up to the instruction in a cycle or two
  Worst case, we just avoid the instruction retiring (i.e., use the ROB)
D Q
D Q
D0[63:0]
.
.
.
LOGIC
D Q
D Q
.
.
.
CLK0
CLK1
D Q
D Q
.
.
.
CLK2
LOGIC
D2[63:0]
D1[63:0]

## Slide 15: Alternative to conditional clocks
Another option: recirculating mux
  If EN=1, then (instead of CLK0 not firing) D0[] recirculates
  Functionally equivalent to cond clock, and the critical path is usually easier
  Now CLK0 doesn’t have the condition in it.
  Burns more clock power, but easier critical path
  Sorry, no free lunches
D Q
D Q
D0[63:0]
.
.
.
LOGIC
D Q
D Q
.
.
.
CLK0
CLK1
D Q
D Q
.
.
.
CLK2
LOGIC
D2[63:0]
D1[63:0]
EN
0
1
0
1

## Slide 16: Di/dt noise
Circuits 101: V = L di/dt
  L = inductance (dominated by how big your package is)
  di/dt = how fast total supply current changes
  When current changes rapidly, you get voltage spikes
Physical intuition:
  An inductor will not let the current through it change instantly.
  When you try to do so, it induces a voltage to create a counteracting current.
time
current
voltage
Remember this issue from our process/scaling lectures?

## Slide 17: Di/dt noise
Ringing frequency is usually determined by the package LC, which is often much slower than the clock frequency
  Often about 100 MHz
  I’ve drawn 1GHz clock and 100 MHz resonance
  There are the usual forced and natural responses
time
Vdd
CLK
CCLK

## Slide 18: Marching on a bridge
Worst case is if the clock conditioning aligns with package resonance
  Architects may want to try and avoid this case!
time
Vdd
CLK
CCLK

## Slide 19: Clock distribution: the problem
What is the problem we face?
  We have to deliver a clock to 10M flops.
  We have to do it with minimal skew & jitter. And minimal power. We’ll soon see why this is hard.
  We must be able to gate local clocks.

## Slide 20: Minimizing clock skew
Let’s look at skew (forget jitter for a moment)
Try to size drivers to minimize skew
Use the calculator at https://www.ece.tufts.edu/ee/194VLS/html/sizing_calc.html
L=4000DU, W=4DU
L=3500DU, W=4DU
20,2,10,2
20,2,10,2
Size Inv #1 to minimize delay to CLK1
Size Inv #2 to equalize the delay on CLK2
INV1
INV2
CLK1
CLK2
WN1=21 → delay=337.2
WN2=5 → delay=337.6

## Slide 21
Now let’s change some parameters and see what happens
L=4000DU, W=4DU
L=3500DU, W=4DU
20,2,10,2
20,2,10,2
42,2,21,2
10,2,5,2
CLK1
337.2
CLK2
337.6
Change device R from 50KΩ/□ to 52. Results?
Return device R to 50K, and change wire R from .030 KΩ/□ to .031.
What happened? Why did skew increase?
  Our two clocks had the same total delay, but different fractions in wires & devices. So changing wire or device parameters affected each clock differently.
Is this (i.e., manufacturing variation causing unequal clock delays) a problem with skew, jitter, or both?
  Skew, because it doesn’t change over time.
346.9, 344
339, 343.5

## Slide 22: Minimizing clock skew
What if our clocks had been perfectly symmetrical?
L=4000DU, W=4DU
L=4000DU, W=4DU
20,2,10,2
20,2,10,2
42,2,21,2
42,2,21,2
CLK1
337.2
CLK2
337.2
What if our clocks had been perfectly symmetrical? Would changing manufacturing process corner have resulted in clock skew?
  No, both clocks would have been affected equally
What about OCV?
  This would still create skew

## Slide 23: Skew summary
We can design for zero skew at nominal process values, but any manufacturing variation can bring back skew
Making our clock wiring and loads completely symmetrical will help, but is not always easy
Skew is a percentage of delay, so reducing delay will reduce skew (but often costs power)

## Slide 24: Minimizing jitter
Now that skew is “somewhat under control,” on to jitter.
Do you remember what causes jitter?
  changes in V and C. What causes these?
  10% change in Vdd or in Cload will cause about 10% change in gate delay.
  Conclusion: Δdelay  delay.
So max jitter is a fixed % of total clock delay. What can we do about this?
  Decrease the total delay of the clock buffers (again, this costs power)
  Shielding clock lines can help a lot to reduce C variability (expensive in area)
  You can try to reduce di/dt. That’s easier said than done
There is no magic bullet
di/dt → ΔV
coupling on delay → ΔC

## Slide 25: Clock power
Why do we care about minimizing clock power? It’s only the clock, right?
How much power do you think a clock might burn?
  From the paper “An x86-64 Core Implemented in 32nm SOI CMOS,” ISSCC 2010 (AMD)
  Chip power is 8% from the clock grid, 4% from clock gaters & 17% from flops. So the clocks burn almost ⅓ of total power!
Is that surprising?
  Perhaps not. We burn active power on transitions, and clocks transition a lot.

## Slide 26: Summary of clock skew/jitter
There are no silver bullets – just careful engineering. Let’s look at some engineering solutions.
  H trees
  Binary trees
  Busbars

## Slide 27: H trees, motivation
Draw one PLL & two flops on the board, with the PLL right between the two. It’s easy to drive the two flops with wires and/or buffers so there’s no skew between them.
Now try again, but with PLL not in the middle.
  Trading device delay vs. wire delay didn’t work well.
  Try to have the same wire lengths to each load, to minimize skew
Now try again, but with 3 flops.
Can we generalize this idea?
  Deliver the clock to many places with the same wire lengths?

## Slide 28: H tree
Each green dot is a clock driver.
The final clocks are available at the corners of the final H’s (or reasonably nearby the corners).
With enough levels, we can get clocks nearly everywhere.
What are advantages of an H tree vs. our simple scheme?
  Now the metal delays to all loads are equal.
Does it solve all problems?
  No. We still may have unequal gate loading.
  Typically there’s enough metal cap in the H tree to make that less relevant. That’s a lot of metal!
  Deliver to all corners ≠ deliver everywhere

## Slide 29: Same idea, less metal
Start with a 1D equivalent of an H tree (often called a binary tree)
Add extra routes to the actual loads
Pro: much less wire than an H tree
Con:
  Extra routes are not balanced, resulting in more skew
  There might be a lot of extra routes

## Slide 30: Busbars
Add occasional busbars in various locations
  many places you can put them.
What good are they?
  They help to even out clock-edge arrival times.
  If, e.g., the top wire rises earlier than the bottom one, the busbar becomes a “low-R” short from power to ground
  Forces edges to occur at roughly the same time.
What is the cost of a busbar?
  More loading
  Short circuits → power!
  Nonetheless, they are effective and widely used.

## Slide 31: Active deskew
We would like nearby locations to have low skew.
H trees are not perfect. The red-arrow skew may be high. Why?
  On-die variation, and the common clock point is far back.
  Busbars help, but cost power and aren’t perfect
Active deskew: monitor the two clocks at the red arrow, compare them and adjust red buffer delays until they match.

## Slide 32: What to do?
At the end of the day, none of these solutions are good enough to drive one clock over an entire chip.
  We can reduce skew, but only at the cost of power and jitter.
  We can reduce jitter, but only at the cost of power.
  At some point, even busbars have R too high to work.
We need a good trick. Here it is:
  power mostly gets burned by clock transitions.
Why is that?
  Charging or discharging a node turns power →heat.
  Leaving a node at 0 or 1 burns only leakage power.

## Slide 33: Slow clocks are nice
What if our clock were 100 MHz rather than 2 GHz? What would be the pros/cons?
  Less power, for sure. But also a slower chip!
A phase-locked loop is a nearly-magic bullet for clock generation.
It takes an input clock, and generates an output clock
  The output clock can be N times faster than the input
  The output clock is locally generated (inside the PLL) – it rejects jitter on the input clock.

## Slide 34: PLL internals
What does this circuit do?
  It’s a ring oscillator
  Clock period  3 * inverter delay
Delay depends on Vdd
  Change Vdd → increase frequency
  We’ve thus built a Voltage-Controlled Oscillator (VCO)
  Make sure we can control the ring-oscillator Vdd separately from everything else 

## Slide 35: PLL internals
Phase comparator makes the VCO run a bit faster or slower until it lines up with the input clock.
We have thus built a fancy clock buffer
  “Fancy” because it rejects input jitter. How?
  And fancy because…
VCO
Clkin
Clkout
Phase comparator

## Slide 36: PLL internals
Add a “divide by N” into the feedback loop
What does this do?
  Now Clkout/N will match Clkin
  I.e., Clkout matches Clkin*N.
We’ve built a jitter-rejecting frequency multiplier
VCO
Clkin
Clkout
/ N
Phase comparator

## Slide 37: Multi-domain distribution
Divide the chip into geometric regions
Mother PLL has balanced 100MHz routes to each daughter
Each daughter PLL multiplies 100MHz→2GHz and then distributes within that region.
The four daughter distributions run at full speed
dist #1
dist #2
dist #3
dist #4
mother PLL
daughter PLL
daughter PLL
daughter PLL
daughter PLL

## Slide 38: Multi-domain distribution
Power to distribute the 100 MHz clock?
  Nice and small
Skew and jitter of the region clocks?
  Again, they are smaller grids, with less delay. And the daughter PLLs reject most of the mother distribution’s jitter!
Power to distribute the region clocks?
  Don’t need to fight skew/jitter with power as much
dist #1
dist #2
dist #3
dist #4
mother PLL
daughter PLL
daughter PLL
daughter PLL
daughter PLL

## Slide 39: Multi-domain distribution
Summary: now each region can have a “small” high-quality distribution network.
Any issues?
  No man is an island; how do different domains talk to each other?
  Maybe it’s not so bad – “most” communication is local.
dist #1
dist #2
dist #3
dist #4
mother PLL
daughter PLL
daughter PLL
daughter PLL
daughter PLL

## Slide 40: Crossing clock domains
There are lots of techniques to cross clock domains. We’ll talk about a few.
To understand them, first we have to talk about hold times.
  We did setup times.
  Now for the other half of the picture.

## Slide 41: Hold time
The time from when CLK rises to when Q changes is called tclk→Q.
D is not allowed to change in the red window of tsetup before the rising edge of CLK.
D also cannot change in the orange window of thold after CLK rises.
CLK
D
Q
D Q
CLK
tclk→Q
The same issue with a metastable internal state node.
Anyone remember why?
Anyone know why?

## Slide 42: Direct flop-to-flop transfer
dlogic,max+tsetup≤ tc+Δc
dlogic,min ≥ thold+ Δc
D Q
D Q
dlogic
ClkD
ClkR
CLKR
CLKD
dlogic,min
dlogic, max
tsetup
thold
tcycle
Δc
tcycle
Does a late receiver clock make setup time easier or harder?
Hold time?
Easier
Harder

## Slide 43: Direct flop-to-flop transfer
dlogic,max+tsetup≤ tc+Δcmin
dlogic,min ≥ thold+Δcmax
PLLm
PLL1
PLL2
D Q
D Q
D Q
D Q
dlogic
ClkD
ClkR
Define Δc as how much later ClkR is than ClkD (considering skew & jitter)… and it’s negative if ClkD is later than ClkR.
thold + Δcmax≤ dlogic≤ tc+Δcmin-tsetup
Do you think Δcmin can be negative?
Almost certainly

## Slide 44: Direct flop-to-flop transfer
Violate the setup time:
  fix it by slowing tc.
What if you violate the hold time?
  you must throw away the chip. Lowering frequency won’t help.
  Too much skew and you throw away the chip.
  Throwing away a chip is money down the drain .
PLLm
PLL1
PLL2
D Q
D Q
D Q
D Q
dlogic
ClkD
ClkR
thold + Δcmax≤ dlogic≤ tc+Δcmin- tsetup

## Slide 45: In-class problem
Assume that:
  skew = ±100ps, jitter=±50ps
  tsetup=thold=20ps
Pick the value for dlogic that satisfies all timing constraints and allows the minimal tc. What is that tc?
PLLm
PLL1
PLL2
D Q
D Q
dlogic
ClkD
ClkR
thold+Δcmax≤ dlogic≤ tc+Δcmin-tsetup
20ps+150ps≤ dlogic≤ tc+(-150ps) – 20ps
170ps≤ dlogic≤ tc-170ps
Pick dlogic=170ps, and then tc≥340ps

## Slide 46: Extreme skew
What if the skew is bigger than your desired cycle time? Our constraints become
  dlogic≥ thold+Δcmax
  dlogic≤ tc+Δcmin-tsetup
Clearly we will not succeed at either one. So what can we do?
  Increase the cycle time a lot…
  But that kills performance, “just” to make clock crossings work
PLLm
PLL1
PLL2
D Q
D Q
dlogic
ClkD
ClkR
thold+Δcmax≤ dlogic≤ tc+Δcmin-tsetup
tcycle
0

## Slide 47: Multiple frequencies
PLL0
PLL1 (x10)
PLL2 (x10)
D Q
D Q
D Q
D Q
dlogic
ClkD
ClkR
100 MHz
1 GHz
1 GHz
Use the slow clock to transfer data between domains. Now our tcycle is only 100 MHz, and tcycle>>tskew.
Problem solved?
  Sure, but two more problems were created
  We’ve just moved the problem, not eliminated the skew

## Slide 48: Heartbeat clocks
The PLL1 and PLL2 clocks have high skew relative to each other
HB1 is just a PLL1 conditional clock
HB2 is just a PLL2 conditional clock
Very low skew between PLL1↔HB1, PLL2↔HB2 or AHB2
High cycle time between HB1/AHB2
PLL0
PLL1
HB1
PLL2
HB2
AHB2

## Slide 49
PLL0
PLL1 (x10)
PLL2 (x10)
D Q
D Q
D Q
D Q
dlogic
ClkD HB1
AHB2 ClkR
100 MHz
Does this work?
  Works fine. No issues with skew or jitter
  Quite simple; just a conditional clock
Any issues?
  Our transfer clocks are only running at 100 MHz.
  It would be nice to have more bandwidth
PLL0
PLL1
HB1
PLL2
HB2
AHB2

## Slide 50: Higher throughput
The idea:
Write new data into a different flop every cycle
Sort of like a pipeline but each flop clocks only once
Read it into the output flop some time later
D
Q
CLK_D0
D
Q
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
CLK_D4
Like a pipeline, we can achieve high throughput (even if latency is also high)

## Slide 51: Don’t throw away chips
t=0: fire CLK_D0.
t=10: fire CLK_D1
t=20: fire CLK_D2
D
Q
CLK_D0
D
Q
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
CLK_D4
data 0
data 1
data 2
data 3
data 4
t=30: fire CLK_D3, mux reads data0 & fires CLK_R
t=40: fire CLK_D4 , mux reads data1 & fires CLK_R
data 0
data 1

## Slide 52: Don’t throw away chips
t=0: fire CLK_D0.
t=10: fire CLK_D1
t=20: fire CLK_D2
D
Q
CLK_D0
D
Q
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
CLK_D4
data 0
data 1
data 2
data 3
data 4
t=30: fire CLK_D3, mux reads data0 & fires CLK_R
t=40: fire CLK_D4 , mux reads data1 & fires CLK_R
What is the throughput?
New data every cycle

## Slide 53: Don’t throw away chips
t=0: fire CLK_D0.
t=10: fire CLK_D1
t=20: fire CLK_D2
D
Q
CLK_D0
D
Q
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
CLK_D4
data 0
data 1
data 2
data 3
data 4
t=30: fire CLK_D3, mux reads data0 & fires CLK_R
t=40: fire CLK_D4 , mux reads data1 & fires CLK_R
What is the latency?
Data0 is written at t=0 and read at t=30

## Slide 54: Don’t throw away chips
t=0: fire CLK_D0.
t=10: fire CLK_D1
t=20: fire CLK_D2
D
Q
CLK_D0
D
Q
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
CLK_D4
data 0
data 1
data 2
data 3
data 4
t=30: fire CLK_D3, mux reads data0 & fires CLK_R
t=40: fire CLK_D4 , mux reads data1 & fires CLK_R
What is the timing constraint from the data0 flop to the output?
dmux,max+Δcmax +tsetup≤ 3*tc

## Slide 55: What have we built?
A sort of a pipeline
  After the initial setup, we write & read new data every cycle
  Because the latency is big, the timing constraints are easy
  If the skew gets worse, we can just bump up the latency
The problem, of course…
  We cannot really build a chip with an infinite number of flops .
  Any ideas?

## Slide 56: Avoiding infinite flops
After we read out data0, that flop never gets used again.
  That’s why we need an infinite number of flops.
Is there a way to reuse the flops?
  What if we only use 4 flops, but recycle them?
D
Q
CLK_D0
D
Q
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
CLK_D4
data 0
data 1
data 2
data 3
data 4

## Slide 57: Avoiding infinite flops
t=0: fire CLK_D0.
t=10: fire CLK_D1
t=20: fire CLK_D2
t=30: fire CLK_D3, mux reads data0 & fires CLK_R
D
Q
CLK_D0
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
data 0
data 1
data 2
data 3
data 0
Now the top-left flop no longer holds useful data, so we can reuse it

## Slide 58: Avoiding infinite flops
t=0: fire CLK_D0.
t=10: fire CLK_D1
t=20: fire CLK_D2
t=30: fire CLK_D3, mux reads data0 & fires CLK_R
D
Q
CLK_D0
D
Q
D
Q
D
Q
mux
D
Q
CLK_R
CLK_D1
CLK_D2
CLK_D3
data 0
data 1
data 2
data 3
t=40: fire CLK_D0 , mux reads data1 & fires CLK_R
t=50: fire CLK_D1 , mux reads data2 & fires CLK_R
t=60: fire CLK_D2, mux reads data3 and fires CLK_R
data 0
data 1
data 4
data 2
data 5
data 6
data 3

## Slide 59: How good is this?
Have we solved the world’s problems with 4 flops?
Why did we need 4 and not 3? What good would it be to have 5 and not 4?
  More flops allows us to suck up more skew & jitter (at the expense of more latency).
Can we make this programmable post-silicon?
  Sure. Just have a register somewhere (programmable via fuses or via software) that tells you to (e.g.,) ignore the 4th flop.

## Slide 60: Does this structure look familiar?
Have we built something that you’ve seen before?
  Yes, it’s called a FIFO! You put stuff in every cycle and it comes out a few cycles later.
  The mux and conditional clocks would be controlled by cyclic counters (a write pointer and a read pointer) that are offset from each other.
FIFOs like this are perhaps the most common means of moving data across clock domains.
  But only if the driver & receiver clock domains are at the same frequency.

## Slide 61: Multiple frequencies
More and more clocks have different domains at different frequencies. Examples for a CPU:
  Some cores run faster than others (lets you throw power at whichever core has the most critical load)
  The uncore typically runs slower than the cores
  External memory runs still slower, and the on-die memory controller runs at the memory speed
  Ditto for various peripherals
Can we fit this into our clock generation and distribution?

## Slide 62: How to do multiple frequencies
Remember that a PLL can multiply its input clock by any integer.
The trick: let different daughter PLLs multiply by different numbers.

## Slide 63: Multiple frequencies
PLL0
PLL1 (x10)
PLL2 (x15)
D Q
D Q
D Q
D Q
dlogic
Clkt
Clkr
100 MHz
1 GHz
1.5 GHz
It’s easy to have different clock domains at different frequencies
But what does it mean to transfer data between them?

## Slide 64: The problem with multiple freq.
If you keep putting 3 pieces of data in and only taking 2 out (to either a simple flop or a FIFO), you immediately run out of space 
Is there any problem in the reverse direction?
  Sure, you’re pulling out data that doesn’t exist.
Is there anything we can do about that?
CLK_1.5G
CLK_1G
2 cycles
3 cycles
2 cycles
3 cycles

## Slide 65: Condition the fast clock
Skip an occasional fast-clock cycle so that now they both fire 10 times every .01μs.
The fast clock is still a 1.5GHz clock, but does not fire every cycle. Does this buy us anything?
It does!
CLK_1.5G
CLK_1G
2 cycles
3 cycles
2 cycles
3 cycles

## Slide 66: Life as seen by the crossing
We can look at these waveforms as two clocks with the same frequency, but with horrendous skew.
Hey – we already know how to deal with this problem! How?
  Use a big FIFO.
CLK_1.5G
CLK_1G
nicely aligned
lots of skew
nicely aligned
lots of skew

## Slide 67: Life as seen by the fast domain
Whatever flop receives data from the CLK_1.5G flop must know that it can receive valid data in some cycles and not others.
  Most pipelines work that way, anyway
But as far as timing goes, there’s no problem at all. Why?
  It’s just one clock talking to another, both at the same frequency in the same domain
CLK_1.5G
CLK_1.5G_next

## Slide 68: Bubble-generator FIFO
We have invented (well, re-invented ) the bubble-generator FIFO (BGF)
It’s a FIFO where enough clock pulses in the fast-clock domain get turned off so that the FIFO works.
As always, the FIFO depth depends on the clock skew + jitter. Now, it also depends on the frequency ratios. Why?
  Because they effectively create more skew

## Slide 69: In-class problem: how much skew did we make?
Assume that:
  Mother clock is 100MHz (i.e., 10ns)
  Daughter clocks are 1GHz (1000ps) and 1.5GHz (666ps)
  We skip the 3rd clock as drawn above
Just how much is the worst-case skew?
What if we had skipped the 2nd clock pulse instead?
CLK_1.5G (receiver)
CLK_1G (driver)
2 cycles
3 cycles
2 cycles
3 cycles
666ps
000ps
1333ps
1000ps
1000ps
000ps
000ps
000ps
666-1000=-333ps
1333-1000= 333ps

## Slide 70: A few more PLL topics
We want our clocks to be as clean and jitter free as possible. So we play a few more tricks

## Slide 71: Add a filter PLL
What good can this do?
  Filter PLL rejects any offchip-generated noise and jitter
  We get an extra stage of jitter rejection
dist #1
dist #2
dist #3
dist #4
mother PLL
daughter PLL
daughter PLL
daughter PLL
daughter PLL
filter PLL

## Slide 72: Duty-cycle correction
Add a divide by 2
  Ensures that duty cycle is 50%
  May be necessary to if Clkout frequency is too slow for the VCO
VCO
Clkin
Clkout
/ N
Phase comparator
/ 2
VCOout
Clkout

## Slide 73: Separate analog supplies
The normal Vdd that is used for digital logic gets noisy
  Gate switching creates di/dt
  Decoupling cap can only do so much
We often use a separate Vdd,analog that drives only analog logic
  Not polluted by the digital-logic noise
  Analog logic doesn’t create as many spikes
  Analog logic benefits from a cleaner power supply
VCO
Clkin
Clkout
/ N
Phase comparator
/ 2

## Slide 74: More topics
Salmon ladders
  How do you send a signal from the early domain to the late domain(s)?
Back pressure
  What if the receiving end of a BGF can stall?

## Slide 75: How can we minimize variation?
Let’s make a model of manufacturing variation
  Device L and W, and wire L & W & H, vary by fixed delta amounts. Let’s make up some numbers.
  Device L can change ± .1DU.
  Wire W can change ±.5 DU, wire R by ±.001 KOhms/square.
Can we design a strategy to minimize delay variation?
  Use big W, L for MOS and for wires. So a fixed Δ becomes a smaller %.
  This will cause power and area problems!
  At least now we have a solution, even if it’s not a good one 

## Slide 76: Minimizing clock skew
This time, we used device L=5DU, wire W=15DU.
The delay numbers increased slightly
Let’s try the same perturbations
L=4000DU, W=15DU
L=3500DU, W=15DU
20,2,10,2
20,2,10,2
174,5,87,5
67.4,5,33.7,5
CLK1
368.5
CLK2
368.7
370.5,
372.5(2X better)
Change device L from 5DU to 5.1. Results?
Return L to 2DU, and change wire R from .030KOhms/sq to .031.
377.7,
374.6 (about the same). Why?

## Slide 77: Skew summary
We can design for zero skew at nominal process values, but any manufacturing variation can bring back skew
Using wide wires and long-channel devices can help, but only up to a point
  And they cause extra capacitance, which wastes power
  More on this shortly

## Slide 78: How can we decrease clock delay?
All of the sizing techniques we’ve talked about.
If we use faster (but lower gain) inverters, what happens to our power?
Our sizing knowledge helps us to make a faster clock-distribution network
  We’re driving some very big output load. Why?
  10 million flops.
gets higher, since self-loading increases as gate delay decreases

## Slide 79: How does decreasing skew affect jitter & power?
We talked about increasing wire W & device W & L to minimize skew.
How does increasing wire W affect clock delay?
  Doubling wire width halves wire R (but not total R) and increases wire C (but doesn’t double it). It sometimes reduces delay, but always increases loading.
How about increasing both device W & L?
  Increasing device W & L increases cap, hurts delay
  What happens if you just increase device W & not L?
    You decrease delay… up to a point.
Bottom line: making things bigger increases capacitance and hence power.
  Power = CV2f.
  It often makes things slower, increasing jitter

## Slide 80: Summary of skew and jitter
We can reduce skew by increasing W & L for wires and devices
  But that increases delay (which increases jitter) and also increases power
We can reduce jitter by
  shielding clock wires (expensive in area)
  decreasing delay (costs power and area, and can only be done within limits)
  trying to improve di/dt (very hard)
There is no magic bullet

## Slide 81: Clock gating
We can (and must) gate the clocks so as to reduce both clocking & downstream power.
So that means AND gates.
How do clock delay and clock power change if we replace an INV with a NAND2?
  Both get worse .
  Remember that a NAND2 has less gain than an INV?
Clk
En