## Slide 1: EE 194 Advanced VLSI
Spring 2018
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lecture 7: Dark silicon

## Slide 2: Resources
The future of microprocessors, Shekhar Borkar 2011
  “The past 20 years were the ‘great old days’; the next 20 years will hopefully be the ‘pretty good new days’ ”
  Good overall description of dark silicon, multiple heterogeneous cores, accelerators, futures
Computational sprinting, HPCA 2012
  Read this for Wednesday

## Slide 3: Power problems, yet again
The same old problem:
  # of devices is rising at a slower and slower rate
  But still faster than power/device is falling
  Arguably the central problem of VLSI nowadays.
Time to look at the problem one more time, and see how much we like our solutions so far

## Slide 4: Mini-quiz (review)
Why is Moore’s Law slowing down?
  It’s getting hard to scale Vt, since it’s approaching kT/q
  Dimensions are nearing quantum sizes
  So: manufacturing is getting harder.
Why is Moore’s Law not stopping?
  We’ve mostly stopped scaling down V
  We’re not at the quantum scale yet!
Dennard scaling (i.e., constant fields and shrinking V) has close to stopped. Why?
  Again, it’s getting hard to scale Vt
  The end of scaling down Vdd means that power is rising 

## Slide 5: What have we done about it?
What are the things we’ve talked about to get around this big problem
  conditional clocking
  DVFS
  Multiple cores
Let’s go over them one by one

## Slide 6: Conditional clocking
What was good about it?
  Turn off the clocks that aren’t doing anything
  Also stops downstream data nodes from wiggling
  Makes our computation more efficient.
What limits its application?
  Eventually you need clocks running if you’re going to do computation 
  Every generation, power gets exponentially worse; so if our solution is cond. clocking, then we have to turn off more and more clocks each generation!
Conclusion: we need cond. clocking, but it’s not enough.

## Slide 7: DVFS
What was the central idea?
  Lower V,F and save power and energy (but run slower)
What was good about it?
  lowering V/F is cubically good!
What limits its application?
  it can be hard to know the correct V/F to run at
Big-picture problem:
  if we really care so much about power, we really should be running at the lowest V possible – and almost never raising V
  But when that doesn’t give us enough computes/cycle, there’s not real good answer other than raising V/F (which is inefficient).

## Slide 8: Multiple cores
Why do we do multiple cores?
  Every generation we have more transistors to use
  We added lots of fancy architectural features: OOO, speculative, big caches
  But we got to where those techniques were adding more transistors, but the IPC wasn’t getting much better and the energy/instruction was often getting worse!
  Now we usually do many smaller cores
What was good about it?
  Small cores are more power-efficient than large ones
What limits its application?
  Not every application can use lots of threads

## Slide 9: Heterogeneous cores
How many cores should we put on a chip?
  8 tiny cores? 4 small cores? 2 medium ones? One big one?
  The best answer depends on the application
Assume: the problem we care about can be broken into 4 threads
  Ask the same question again: how many cores to build?
  Probably 4 small.
Assume: now we care most about an app with 2 threads. Now?
  Then build 2 medium cores.
What if we care about both apps?
  Build 4 small cores and two medium!
  Example: Apple A11 Bionic (the CPU that powers IPhone X).
  It has two fast cores and 4 slow ones.

## Slide 10: Heterogeneous
4 small cores and two big ones!?! And usually only use one set or the other!?!
Why not 4 small cores, and crank up Vdd when we only have 2 threads?
  usually doesn’t work as well as two larger cores. High V/F is cubically inefficient.
Why not 2 big cores, and drop the voltage when we can?
  more parallelism = more efficient
  Hopefully we were already running at a low voltage
Isn’t that wasteful of area?
  Yes, but our premise is that we have more transistors than we know what to do with
Isn’t that wasteful of clock power?
  No, since we turn off the clocks in any unused core
  This is how we turn on fewer clocks every generation 
Don’t the unused cores still have static power?
  Lower Vdd enough to reduce that
  Don’t need to do it fast; this is DVFS-level granularity or even slower

## Slide 11: Video decoding
Observations:
  we often watch videos on our phones!
  Video decompression is compute intensive
Does conditional clocking help on video?
  Sure, but the parts of the die that are computing still have to clock 
  And there’s lots of computing
Does multicore help on video?
  Maybe, if we can split decompression over multiple small cores
Does DVFS help on video?
  We can adjust voltage to frame rate
All of these are good – but we can do better!

## Slide 12: Accelerators
Where does a general-purpose CPU spend its power?
  Doing real work, and…
  Circuits for speculative, OOO execution
  Moving data between memory/cache/regfiles and execution units
Much of these are not really doing any computation!
Ideas:
  Build a special-purpose machine
  Build just as many registers as we need for, e.g., MP4
  Put the registers near the execution units
  Throw away speculative/OOO
Result: a very power-efficient machine that does only one thing and is useless otherwise

## Slide 13: Group exercise
Assume:
  we have lots of registers
  8 variables are already in registers: A0, B0, A1, B1, A2, B2, A3, B3
  We want to compute A0*B0 + A1*B1 + A2*B2 + A3*B3
General-purpose way:
  Write assembly code (e.g., for MIPS) to do the computation
Design your own accelerator for it:
  Use as many multipliers and adders as you want
  The final result must go back into the register file
  Try to avoid putting intermediate results into the register file
Which way will be more power efficient? Faster?

## Slide 14: More accelerators
Accelerators have been around forever
Any idea why nobody cared until recently?
  When CPUs got 2x faster every year, accelerators were not worth the trouble
  No reason to care about their power advantage in the past
Example
  IPhone has a neural engine.
  Not sure if they have an MP4 decoder anywhere… they’re not telling (may be part of their GPU or video encoder)

## Slide 15: Dark silicon
What is dark silicon?
  Lots of transistors available
  Cannot use them all at once (too much power)
Solution: build more things than you will use at once
  Build multiple heterogeneous cores
  Build multiple accelerators
  At any give time, use the most efficient tool for your problem
  Leave the others idle, with stopped clocks and low Vdd
  Idle units are “dark silicon”

## Slide 16: Computational sprinting
Chief ideas:
  Observation: we often only need intense computing for a short time
  We might not care as much about instantaneous power as about chip temperature
  Chip + package + heat sink combination has substantial thermal mass; its temperature may take a while to rise substantially
  You can run at a long-term-unsustainable power level – as long as you don’t do it too long

## Slide 17: Discussion questions
What are the main assumptions that the paper makes about how the proposed chip would be used? Do you think they are valid?
They only talk about using multiple small cores. Why not use heterogeneous cores?
What type of thermal time constants do you think they are talking about?
The more thermal mass you have, the longer you can sprint for. Are there any downsides of having more thermal mass?
What are phase-change materials, and why do the authors like them?
What do they do if the chip reaches maximum temperature and the user is still demanding lots of computes?
What about di/dt issues?
What are your overall thoughts on the paper?